## Slide 1: BLM6112 Advanced Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
http://www3.yildiz.edu.tr/~naydin

## Slide 2
Information Systems:
Fundamentals

## Slide 3: Informatics
The term informatics broadly describes the study and practice of
  creating,
  storing,
  finding,
  manipulating
  sharing
information.

## Slide 4: Informatics - Etymology
In 1956 the German computer scientist Karl Steinbuch coined the word Informatik
    [Informatik: Automatische Informationsverarbeitung ("Informatics: Automatic Information Processing")]
The French term informatique was coined in 1962 by Philippe Dreyfus
    [Dreyfus, Phillipe. L’informatique. Gestion, Paris, June 1962, pp. 240–41]
The term was coined as a combination of information and automatic to describe the science of automating information interactions

## Slide 5: Informatics - Etymology
The morphology—informat-ion + -ics—uses
the accepted form for names of sciences,
  as conics, linguistics, optics,
or matters of practice,
  as economics, politics, tactics
linguistically, the meaning extends easily
  to encompass both
    the science of information
    the practice of information processing.

## Slide 6: Data - Information - Knowledge
Data
  unprocessed facts and figures without any added interpretation or analysis.
    {The price of crude oil is $80 per barrel.}
Information
  data that has been interpreted so that it has meaning for the user.
    {The price of crude oil has risen from $70 to $80 per barrel}
      [gives meaning to the data and so is said to be information to someone who tracks oil prices.]

## Slide 7: Data - Information - Knowledge
Knowledge
  a combination of information, experience and insight that may benefit the individual or the organisation.
    {When crude oil prices go up by $10 per barrel, it's likely that petrol prices will rise by 2p per litre.}
      [This is knowledge]
      [insight: the capacity to gain an accurate and deep understanding of someone or something; an accurate and deep understanding]

## Slide 8: Converting data into information
Data becomes information when it is applied to some purpose and adds value for the recipient.
  For example a set of raw sales figures is data.
    For the Sales Manager tasked with solving a problem of poor sales in one region, or deciding the future focus of a sales drive, the raw data needs to be processed into a sales report.
  It is the sales report that provides information.

## Slide 9: Converting data into information
Collecting data is expensive
  you need to be very clear about why you need it and how you plan to use it.
  One of the main reasons that organisations collect data is to monitor and improve performance.
    if you are to have the information you need for control and performance improvement, you need to:
      collect data on the indicators that really do affect performance
      collect data reliably and regularly
      be able to convert data into the information you need.

## Slide 10: Converting data into information
To be useful, data must satisfy a number of conditions. It must be:
  relevant to the specific purpose
  complete
  accurate
  timely
    data that arrives after you have made your decision is of no value

## Slide 11: Converting data into information
  in the right format
    information can only be analysed using a spreadsheet if all the data can be entered into the computer system
  available at a suitable price
    the benefits of the data must merit the cost of collecting or buying it.
The same criteria apply to information.
  It is important
    to get the right information
    to get the information right

## Slide 12: Converting information to knowledge
Ultimately the tremendous amount of information that is generated is only useful if it can be applied to create knowledge within the organisation.
There is considerable blurring and confusion between the terms information and knowledge.

## Slide 13: Converting information to knowledge
think of knowledge as being of two types:
  Formal, explicit or generally available knowledge.
    This is knowledge that has been captured and used to develop policies and operating procedures for example.
  Instinctive, subconscious, tacit or hidden knowledge.
    Within the organisation there are certain people who hold specific knowledge or have the 'know how'
      {"I did something very similar to that last year and this happened….."}

## Slide 14: Converting information to knowledge
Clearly, both types of knowledge are essential for the organisation.
Information on its own will not create a knowledge-based organisation
  but it is a key building block.
The right information fuels the development of intellectual capital
  which in turns drives innovation and performance improvement.

## Slide 15: Definition(s) of system
A system can be broadly defined as an integrated set of elements that accomplish a defined objective.
People from different engineering disciplines have different perspectives of what a "system" is.
For example,
  software engineers often refer to an integrated set of computer programs as a "system"
  electrical engineers might refer to complex integrated circuits or an integrated set of electrical units as a "system"
As can be seen, "system" depends on one’s perspective, and the “integrated set of elements that accomplish a defined objective” is an appropriate definition.

## Slide 16: Definition(s) of system
A system is an assembly of parts where:
  The parts or components are connected together in an organized way.
  The parts or components are affected by being in the system (and are changed by leaving it).
  The assembly does something.
  The assembly has been identified by a person as being of special interest.
Any arrangement which involves the handling, processing or manipulation of resources of whatever type can be represented as a system.
Some definitions on online dictionaries
  http://en.wikipedia.org/wiki/System
  http://dictionary.reference.com/browse/systems
  http://www.businessdictionary.com/definition/system.html

## Slide 17: Definition(s) of system
A system is defined as multiple parts working together for a common purpose or goal.
Systems can be large and complex
  such as the air traffic control system or our global telecommunication network.
Small devices can also be considered as systems
  such as a pocket calculator, alarm clock, or 10-speed bicycle.

## Slide 18: Definition(s) of system
Systems have inputs, processes, and outputs.
When feedback (direct or indirect) is involved, that component is also important to the operation of the system.
To explain all this, systems are usually explained using a model.
A model helps to illustrate the major elements and their relationship, as illustrated in the next slide

## Slide 19: A systems model

## Slide 20: Information Systems
The ways that organizations
  Store
  Move
  Organize
  Process
their information

## Slide 21: Information Technology
Components that implement information systems,
  Hardware
    physical tools: computer and network hardware, but also low-tech things like pens and paper
  Software
    (changeable) instructions for the hardware
  People
  Procedures
    instructions for the people
  Data/databases

## Slide 22: Digital System
Takes a set of discrete information (inputs) and discrete internal information (system state) and generates a set of discrete information (outputs).
System State
Discrete
Information
Processing
System
Discrete
Inputs
Discrete
Outputs

## Slide 23: A Digital Computer Example
Synchronous or Asynchronous?
Inputs: Keyboard, mouse, modem, microphone
Outputs: CRT, LCD, modem, speakers
Notes: Answer: Part of specification for a PC is in MHz. What does that imply? A clock which defines the discrete times for update of state for a synchronous system. Not all of the computer may be synchronous, however.

## Slide 24: Signal
An information variable represented by physical quantity.
For digital systems, the variable takes on discrete values.
Two level, or binary values are the most prevalent values in digital systems.
Binary values are represented abstractly by:
  digits 0 and 1
  words (symbols) False (F) and True (T)
  words (symbols) Low (L) and High (H)
  and words On and Off.
Binary values are represented by values or ranges of values of physical quantities

## Slide 25: A typical measurement system

## Slide 26: Transducers
A “transducer” is a device that converts energy from one form to another.
In signal processing applications, the purpose of energy conversion is to transfer information, not to transform energy.
In physiological measurement systems, transducers may be
  input transducers (or sensors)
    they convert a non-electrical energy into an electrical signal.
    for example, a microphone.
  output transducers (or actuators)
    they convert an electrical signal into a non-electrical energy.
    For example, a speaker.

## Slide 27: Analogue signal
The analogue signal
  a continuous variable defined with infinite precision
is converted to a discrete sequence of measured values which are represented digitally
Information is lost in converting from analogue to digital, due to:
  inaccuracies in the measurement
  uncertainty in timing
  limits on the duration of the measurement
These effects are called quantisation errors

## Slide 28: Digital signal
The continuous analogue signal has to be held before it can be sampled
Otherwise, the signal would be changing during the measurement
Only after it has been held can the signal be measured, and the measurement converted to a digital value

## Slide 29: Signal Encoding: Analog-to Digital Conversion
Continuous (analog) signal ↔ Discrete signal x(t) = f(t) ↔ Analog to digital conversion ↔ x[n] = x [1], x [2], x [3], ... x[n]

## Slide 30: Analog-to Digital Conversion
ADC consists of four steps to digitize an analog signal:
  Filtering
  Sampling
  Quantization
  Binary encoding
Before we sample, we have to filter the signal to limit the maximum frequency of the signal as it affects the sampling rate.
Filtering should ensure that we do not distort the signal, ie remove high frequency components that affect the signal shape.

## Slide 32: Sampling
The sampling results in a discrete set of digital numbers that represent measurements of the signal
  usually taken at equal intervals of time
Sampling takes place after the hold
  The hold circuit must be fast enough that the signal is not changing during the time the circuit is acquiring the signal value
We don't know what we don't measure
In the process of measuring the signal, some information is lost

## Slide 33: Sampling
Analog signal is sampled every TS secs.
Ts is referred to as the sampling interval.
fs = 1/Ts is called the sampling rate or sampling frequency.
There are 3 sampling methods:
  Ideal - an impulse at each sampling instant
  Natural - a pulse of short width with varying amplitude
  Flattop - sample and hold, like natural but with single amplitude value
The process is referred to as pulse amplitude modulation PAM and the outcome is a signal with analog (non integer) values

## Slide 35
Recovery of a sampled sine wave for different sampling rates

## Slide 40
According to the Nyquist theorem, the sampling rate must be
at least 2 times the highest frequency contained in the signal.
Sampling Theorem
Fs  2fm

## Slide 41: Quantization
Sampling results in a series of pulses of varying amplitude values ranging between two limits: a min and a max.
The amplitude values are infinite between the two limits.
We need to map the infinite amplitude values onto a finite set of known values.
This is achieved by dividing the distance between min and max into L zones, each of height 
 = (max - min)/L

## Slide 42: Quantization Levels
The midpoint of each zone is assigned a value from 0 to L-1 (resulting in L values)
Each sample falling in a zone is then approximated to the value of the midpoint.

## Slide 43: Quantization Zones
Assume we have a voltage signal with amplitutes Vmin=-20V and Vmax=+20V.
We want to use L=8 quantization levels.
Zone width = (20 - -20)/8 = 5
The 8 zones are: -20 to -15, -15 to -10, -10 to -5, -5 to 0, 0 to +5, +5 to +10, +10 to +15, +15 to +20
The midpoints are: -17.5, -12.5, -7.5, -2.5, 2.5, 7.5, 12.5, 17.5

## Slide 44: Assigning Codes to Zones
Each zone is then assigned a binary code.
The number of bits required to encode the zones, or the number of bits per sample as it is commonly referred to, is obtained as follows:
nb = log2 L
Given our example, nb = 3
The 8 zone (or level) codes are therefore: 000, 001, 010, 011, 100, 101, 110, and 111
Assigning codes to zones:
  000 will refer to zone -20 to -15
  001 to zone -15 to -10, etc.

## Slide 45
Quantization and encoding of a sampled signal

## Slide 46: Quantization Error
When a signal is quantized, we introduce an error
  the coded signal is an approximation of the actual amplitude value.
The difference between actual and coded value (midpoint) is referred to as the quantization error.
The more zones, the smaller 
  which results in smaller errors.
BUT, the more zones the more bits required to encode the samples
  higher bit rate

## Slide 47: Analog-to-digital Conversion
Example An 12-bit analog-to-digital converter (ADC) advertises an accuracy of ± the least significant bit (LSB). If the input range of the ADC is 0 to 10 volts, what is the accuracy of the ADC in analog volts?
Solution:
If the input range is 10 volts then the analog voltage represented by the LSB would be:
Hence the accuracy would be ± 0.0024 volts.

## Slide 48: Sampling related concepts
Over/exact/under sampling
Regular/irregular sampling
Linear/Logarithmic sampling
Aliasing
Anti-aliasing filter
Image
Anti-image filter

## Slide 49: Steps for digitization/reconstruction of a signal
Band limiting (LPF)
Sampling / Holding
Quantization
Coding
These are basic steps for A/D conversion
D/A converter
Sampling / Holding
Image rejection
These are basic steps for reconstructing a sampled digital signal

## Slide 50: Digital data: end product of A/D conversion and related concepts
Bit: least digital information, binary 1 or 0
Nibble: 4 bits
Byte: 8 bits, 2 nibbles
Word: 16 bits, 2 bytes, 4 nibbles
Some jargon:
  integer, signed integer, long integer, 2s complement, hexadecimal, octal, floating point, etc.

## Slide 52: Data types
Our first requirement is to find a way to represent information (data) in a form that is mutually comprehensible by human and machine.
  Ultimately, we need to develop schemes for representing all conceivable types of information - language, images, actions, etc.
  Specifically, the devices that make up a computer are switches that can be on or off, i.e. at high or low voltage.
  Thus they naturally provide us with two symbols to work with:
    we can call them on and off, or 0 and 1.

## Slide 53: What kinds of data do we need to represent?
Numbers
signed, unsigned, integers, floating point, complex, rational, irrational, …
Text
characters, strings, …
Images
pixels, colors, shapes, …
Sound
Logical
true, false
Instructions
…
Data type:
  representation and operations within the computer

## Slide 54: Number Systems – Representation
Positive radix, positional number systems
A number with radix r is represented by a string of digits: An - 1An - 2 … A1A0 . A- 1 A- 2 … A- m + 1 A- m in which 0 £ Ai < r and . is the radix point.
The string of digits represents the power series:
(
)
(
)
(Number)r
=
å
å
+
j = - m
j
j
i
i = 0
i
r
A
r
A
(Integer Portion)
+
(Fraction Portion)
i = n - 1
j = - 1

## Slide 55: Decimal Numbers
“decimal” means that we have ten digits to use in our representation
  the symbols 0 through 9
What is 3546?
  it is three thousands plus five hundreds plus four tens plus six ones.
  i.e. 3546 = 3×103 + 5×102 + 4×101 + 6×100
How about negative numbers?
  we use two more symbols to distinguish positive and negative:
  + and -

## Slide 56: Decimal Numbers
“decimal” means that we have ten digits to use in our representation (the symbols 0 through 9)
What is 3546?
  it is three thousands plus five hundreds plus four tens plus six ones.
  i.e. 3546 = 3.103 + 5.102 + 4.101 + 6.100
How about negative numbers?
  we use two more symbols to distinguish positive and negative:
  + and -

## Slide 57: Unsigned Binary Integers
 | 3-bits | 5-bits | 8-bits
0 | 000 | 00000 | 00000000
1 | 001 | 00001 | 00000001
2 | 010 | 00010 | 00000010
3 | 011 | 00011 | 00000011
4 | 100 | 00100 | 00000100
Y = “abc” = a.22 + b.21 + c.20
N = number of bits
Range is:
0  i < 2N - 1
(where the digits a, b, c can each take on the values of 0 or 1 only)
Problem:
How do we represent negative numbers?

## Slide 58: Signed Binary Integers -2s Complement representation-
Transformation
  To transform a into -a, invert all bits in a and add 1 to the result
-16 | 10000
… | …
-3 | 11101
-2 | 11110
-1 | 11111
0 | 00000
+1 | 00001
+2 | 00010
+3 | 00011
… | …
+15 | 01111
Range is:
-2N-1 < i < 2N-1 - 1
Advantages:
Operations need not check the sign
Only one representation for zero
Efficient use of all the bits

## Slide 59: Limitations of integer representations
Most numbers are not integer!
  Even with integers, there are two other considerations:
Range:
  The magnitude of the numbers we can represent is determined by how many bits we use:
    e.g. with 32 bits the largest number we can represent is about +/- 2 billion, far too small for many purposes.
Precision:
  The exactness with which we can specify a number:
    e.g. a 32 bit number gives us 31 bits of precision, or roughly 9 figure precision in decimal repesentation.
We need another data type!

## Slide 60: Real numbers
Our decimal system handles non-integer real numbers by adding yet another symbol - the decimal point (.) to make a fixed point notation:
  e.g. 3456.78 = 3.103 + 4.102 + 5.101 + 6.100 + 7.10-1 + 8.10-2
The floating point, or scientific, notation allows us to represent very large and very small numbers (integer or real), with as much or as little precision as needed:
  Unit of electric charge e = 1.602 176 462 x 10-19 Coulomb
  Volume of universe = 1 x 1085 cm3
    the two components of these numbers are called the mantissa and the exponent

## Slide 61: Real numbers in binary
We mimic the decimal floating point notation to create a “hybrid” binary floating point number:
  We first use a “binary point” to separate whole numbers from fractional numbers to make a fixed point notation:
    e.g. 00011001.110 = 1.24 + 1.103 + 1.101 + 1.2-1 + 1.2-2 => 25.75
      (2-1 = 0.5 and 2-2 = 0.25, etc.)
  We then “float” the binary point:
    00011001.110 => 1.1001110 x 24
      mantissa = 1.1001110, exponent = 4
  Now we have to express this without the extra symbols ( x, 2, . )
    by convention, we divide the available bits into three fields:
    sign, mantissa, exponent

## Slide 62: IEEE-754 fp numbers - 1
s
biased exp.
fraction
1
8 bits
23 bits
N = (-1)s x 1.fraction x 2(biased exp. – 127)
32 bits:
Sign: 1 bit
Mantissa: 23 bits
  We “normalize” the mantissa by dropping the leading 1 and recording only its fractional part (why?)
Exponent: 8 bits
  In order to handle both +ve and -ve exponents, we add 127 to the actual exponent to create a “biased exponent”:
    2-127 => biased exponent = 0000 0000 (= 0)
    20 => biased exponent = 0111 1111 (= 127)
    2+127 => biased exponent = 1111 1110 (= 254)

## Slide 63: IEEE-754 fp numbers - 2
Example: Find the corresponding fp representation of 25.75
    25.75 => 00011001.110 => 1.1001110 x 24
    sign bit = 0 (+ve)
    normalized mantissa (fraction) = 100 1110 0000 0000 0000 0000
    biased exponent = 4 + 127 = 131 => 1000 0011
    so 25.75 => 0 1000 0011 100 1110 0000 0000 0000 0000 => x41CE0000
Values represented by convention:
  Infinity (+ and -): exponent = 255 (1111 1111) and fraction = 0
  NaN (not a number): exponent = 255 and fraction  0
  Zero (0): exponent = 0 and fraction = 0
    note: exponent = 0 => fraction is de-normalized, i.e no hidden 1

## Slide 64: IEEE-754 fp numbers - 3
Double precision (64 bit) floating point
1
11 bits
52 bits
N = (-1)s x 1.fraction x 2(biased exp. – 1023)
64 bits:
Range & Precision:
  32 bit:
    mantissa of 23 bits + 1 => approx. 7 digits decimal
    2+/-127 => approx. 10+/-38
  64 bit:
    mantissa of 52 bits + 1 => approx. 15 digits decimal
    2+/-1023 => approx. 10+/-306
s
biased exp.
fraction

## Slide 65: Binary Numbers and Binary Coding
Flexibility of representation
  Within constraints below, can assign any binary combination (called a code word) to any data as long as data is uniquely encoded.
Information Types
  Numeric
    Must represent range of data needed
    Very desirable to represent data such that simple, straightforward computation for common arithmetic operations permitted
    Tight relation to binary numbers
  Non-numeric
    Greater flexibility since arithmetic operations not applied.
    Not tied to binary numbers

## Slide 66: Non-numeric Binary Codes
Given n binary digits (called bits), a binary code is a mapping from a set of represented elements to a subset of the 2n binary numbers.
Example: A binary code for the seven colors of the rainbow
Code 100 is not used
Binary Number
000
001
010
011
101
110
111
Color
Red
Orange
Yellow
Green
Blue
Indigo
Violet

## Slide 67: Number of Bits Required
Given M elements to be represented by a binary code, the minimum number of bits, n, needed, satisfies the following relationships:
    2n > M > 2(n – 1)
    n =log2 M where x , called the ceiling function, is the integer greater than or equal to x.
Example: How many bits are required to represent decimal digits with a binary code?
  4 bits are required (n =log2 9 = 4)
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 68: Number of Elements Represented
Given n digits in radix r, there are rn distinct elements that can be represented.
But, you can represent m elements, m < rn
Examples:
  You can represent 4 elements in radix r = 2 with n = 2 digits: (00, 01, 10, 11).
  You can represent 4 elements in radix r = 2 with n = 4 digits: (0001, 0010, 0100, 1000).

## Slide 69: Binary Coded Decimal (BCD)
In the 8421 Binary Coded Decimal (BCD) representation each decimal digit is converted to its 4-bit pure binary equivalent
This code is the simplest, most intuitive binary code for decimal digits and uses the same powers of 2 as a binary number,
  but only encodes the first ten values from 0 to 9.
    For example: (57)dec  (?) bcd
    ( 5 7 ) dec
    = (0101 0111)bcd
Notes: Answer 1: 6
Answer 2: 1010, 1011, 1100, 1101, 1110, 1111

## Slide 70: Error-Detection Codes
Redundancy (e.g. extra information), in the form of extra bits, can be incorporated into binary code words to detect and correct errors.
A simple form of redundancy is parity, an extra bit appended onto the code word to make the number of 1’s odd or even.
  Parity can detect all single-bit errors and some multiple-bit errors.
A code word has even parity if the number of 1’s in the code word is even.
A code word has odd parity if the number of 1’s in the code word is odd.

## Slide 71: 4-Bit Parity Code Example
Fill in the even and odd parity bits:
The codeword "1111" has even parity and the codeword "1110" has odd parity. Both can be used to represent 3-bit data.
Even Parity
Odd Parity
Message
-
Parity
Message
-
Parity
000
-
000
-
001
-
001
-
010
-
010
-
011
-
011
-
100
-
100
-
101
-
101
-
110
-
110
-
111
-
111
-
Notes: Even Parity Bits: 0, 1, 1, 0, 1, 0, 0, 1
Odd Parity Bits: 1, 0, 0, 1, 0, 1, 1, 0

## Slide 72: ASCII Character Codes
American Standard Code for Information Interchange
This code is a popular code used to represent information sent as character-based data.
It uses 7- bits to represent
  94 Graphic printing characters
  34 Non-printing characters
Some non-printing characters are used for text format
  e.g. BS = Backspace, CR = carriage return
Other non-printing characters are used for record marking and flow control
  e.g. STX = start text areas, ETX = end text areas.

## Slide 73: ASCII Properties
ASCII has some interesting properties:
Digits 0 to 9 span Hexadecimal values 3016 to 3916
Upper case A-Z span 4116 to 5A16
Lower case a-z span 6116 to 7A16
  Lower to upper case translation (and vice versa) occurs by flipping bit 6
Delete (DEL) is all bits set,
  a carryover from when punched paper tape was used to store messages

## Slide 74: UNICODE
UNICODE extends ASCII to 65,536 universal characters codes
  For encoding characters in world languages
  Available in many modern applications
  2 byte (16-bit) code words

## Slide 75: Warning: Conversion or Coding?
Do NOT mix up "conversion of a decimal number to a binary number" with "coding a decimal number with a binary code".
1310 = 11012
  This is conversion
13  0001 0011BCD
  This is coding

## Slide 76: Another use for bits: Logic
Beyond numbers
  logical variables can be true or false, on or off, etc., and so are readily represented by the binary system.
  A logical variable A can take the values false = 0 or true = 1 only.
  The manipulation of logical variables is known as Boolean Algebra, and has its own set of operations
    which are not to be confused with the arithmetical operations.
  Some basic operations: NOT, AND, OR, XOR

## Slide 77: Binary Logic and Gates
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.
We study Boolean algebra as foundation for designing and analyzing digital systems!

## Slide 78: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values.
Variable identifier examples:
  A, B, y, z, or X1 for now
  RESET, START_IT, or ADD1 later

## Slide 79: Logical Operations
The three basic logical operations are:
  AND
  OR
  NOT
AND is denoted by a dot (·)
OR is denoted by a plus (+)
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable

## Slide 80: Notation Examples
Examples:
  Y=A.B is read “Y is equal to A AND B.”
  z=x+y is read “z is equal to x OR y.”
  X=Ā is read “X is equal to NOT A.”
Note: The statement:
  1 + 1 = 2 (read “one plus one equals two”)
is not the same as
  1 + 1 = 1 (read “1 or 1 equals 1”).

## Slide 81: Operator Definitions
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0
=
0
1
=

## Slide 82: Truth Tables
0
1
1
0
X
NOT
X
Z
=
Truth table - a tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 83: Transistor: Building Block of Computers
Microprocessors contain millions of transistors
  Intel Pentium 4 (2000): 48 million
  IBM PowerPC 750FX (2002): 38 million
  IBM/Apple PowerPC G5 (2003): 58 million
Logically, each transistor acts as a switch
Combined to implement logic functions
  AND, OR, NOT
Combined to build higher-level structures
  Adder, multiplexer, decoder, register, …
Combined to build processor
Notes: Intel and Pentium are trademarks of Intel Corporation. IBM and PowerPC are trademarks of International Business Machines Corporation. Apple is a trademark of Apple Computer, Inc.

## Slide 84: Building Functions from Logic Gates
Combinational Logic Circuit
  output depends only on the current inputs
  stateless
Sequential Logic Circuit
  output depends on the sequence of inputs (past and present)
  stores information (state) from past inputs

## Slide 85: Basic Logic Gates

## Slide 86: Waveform behavior in time
Timing diagram
X
0
0
1
1
Y
0
1
0
1
X
·
Y
(AND)
0
0
0
1
X
+
Y
(OR)
0
1
1
1
(NOT)
X
1
1
0
0
OR gate
X
Y
Z
=
X
+
Y
X
Y
Z
=
X
·
Y
AND gate
X
Z
=
X
NOT gate or
inverter

## Slide 87: Logic Diagrams and Expressions
Boolean equations, truth tables and logic diagrams describe the same function!
Truth tables are unique; expressions and logic diagrams are not. This gives flexibility in implementing functions.
X
Y
F
Z
Logic Diagram
Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F
×
+
=

## Slide 88: Boolean Algebra
Involution
Idempotence
Existence of complement
Existence of 0 and1
Commutative
Associative
Distributive
DeMorgan’s
2.
X
. 1
X
=
4.
X
. 0
0
=
6.
X . X
X
=
8.
0
=
X . X
An algebraic structure defined on a set of at least two elements, B, together with three binary operators (denoted +, · and ) that satisfies the following basic identities:
10.
X + Y
Y + X
=
12.
(X + Y)
Z
+
X + (Y
Z)
+
=
14.
X(Y +
Z)
XY
XZ
+
=
16.
X + Y
X . Y
=
11.
XY
YX
=
13.
(XY)
Z
X(Y
Z)
=
15.
X
+ YZ
(X + Y)
(X + Z)
=
17.
X . Y
X + Y
=
1.
X
+ 0
X
=
3.
+
X
1
1
=
5.
X + X
X
=
7.
1
=
X + X
9.
X = X

## Slide 89: Boolean Operator Precedence
The order of evaluation in a Boolean expression is:
1.
Parentheses
2.
NOT
3.
AND
4.
OR
Consequence: Parentheses appear around OR expressions
Example: F = A(B + C)(C + D)

## Slide 90: Example 1: Boolean Algebraic Proof
A + A·B = A (Absorption Theorem)
Proof Steps Justification (identity or theorem)
A + A·B
= A · 1 + A · B X = X · 1
= A · ( 1 + B) X · Y + X · Z = X ·(Y + Z)(Distributive Law)
= A · 1 1 + X = 1
= A X · 1 = X
Our primary reason for doing proofs is to learn:
  Careful and efficient use of the identities and theorems of Boolean algebra, and
  How to choose the appropriate identity or theorem to apply to make forward progress, irrespective of the application.

## Slide 91: Example 2: Boolean Algebraic Proofs
AB + AC + BC = AB + AC (Consensus Theorem)
Proof Steps: Justification (identity or theorem)
AB + AC + BC
= AB + AC + 1 · BC
= AB + AC + (A + A) · BC
= AB + AC + ABC + ABC
= AB (1+C) + AC (1+B)
= AB · 1 + AC · 1
= AB + AC
Notes: Justification 1: 1 . X = X
Justification 2: X + X’ = 1
= AB + A’C + ABC + A’BC X(Y + Z) = XY + XZ (Distributive Law)
= AB + ABC + A’C + A’BC X + Y = Y + X (Commutative Law)
= AB . 1 + ABC + A’C . 1 + A’C . B X . 1 = X, X . Y = Y . X (Commutative Law)
= AB (1 + C) + A’C (1 + B) X(Y + Z) = XY +XZ (Distributive Law)
= AB . 1 + A’C . 1 = AB + A’C X . 1 = X

## Slide 92: Example 3: Boolean Algebraic Proofs
Proof Steps Justification (identity or theorem)
=
Y
X
Z
)
Y
X
(
+
+
)
Z
X
(
X
Z
)
Y
X
(
+
=
+
+
Y
Y
Notes: = X’ Y’ Z + X Y’ (A + B)’ = A’ . B’ (DeMorgan’s Law)
= Y’ X’ Z + Y’ X A . B = B . A (Commutative Law)
= Y’ (X’ Z + X) A(B + C) = AB + AC (Distributive Law)
= Y’ (X’ + X)(Z + X) A + BC = (A + B)(A + C) (Distributive Law)
= Y’ . 1 . (Z + X) A + A’ = 1
= Y’ (X + Z) 1 . A = A, A + B = B + A (Commutative Law)

## Slide 93: Useful Theorems
x
y
×
y
Laws
s
DeMorgan'
x
x
×
=
+
y
x
=
+
y
(
)
(
)
n
inimizatio
M
y
y
y
x
y
y
y
x
=
+
+
=
×
×
+
x
x
z
y
x
z
y
z
y
x
+
×
+
=
+
×
+
×
+
x
x
(
)
(
)
(
)
(
)
(
)
+
=
+
+
Consensus
z
y
x
z
y
z
y
x
×
×
×
×
×
x
x
(
)
tion
Simplifica
y
x
y
x
y
x
y
x
×
=
+
×
+
=
×
+
x
x

## Slide 94: Proof of Simplification
y
y
y
x
=
×
×
x
+
(
)
(
)
y
y
y
x
=
+
+
x
Notes: x . y + x’ . y
= (x + x’) . y X(Y + Z) = XY + XZ (Distributive Law)
= 1 . y X + X’ = 1
= y X . 1 = X

## Slide 95: Proof of DeMorgan’s Laws
+
y
x
x
=
y
×
y
x
×
y
x
+
=
Notes: It is important that we do not USE DeMorgan’s Laws in doing this proof. This requires a different proof method. We will show that, x’ . y’, satisfies the definition of the complement of (x + y), defined as (x + y)’ by DeMorgan’s Law.
To show this we need to show that A + A’ = 1 and A.A’ = 0 with A = x + y and A’ = x’. y’. This proves that x’. y’ = (x + y)’.
Part 1: Show x + y + x’. y’ = 1.
x + y + x’. y’
= (x + y + x’) (x + y + y’) X + YZ = (X + Y)(X + Z) (Distributive Law)
= (x + x’ + y) (x + y + y’) X + Y = Y + X (Commutative Law)
= (1 + y)(x + 1) X + X’ = 1
= 1 . 1 1 + X = 1
= 1 1 . X = 1
Part 2: Show (x + y) . x’. y’ = 0.
(x + y) . x’. y’
= (x . x’. y’ + y . x’. y’) X (Y + Z) = XY + XZ (Distributive Law)
= (x . x’. y’ + y . y’ . x’) XY = YX (Commutative Law)
= (0 . y’ + 0 . x’) X . X’ = 0
= (0 + 0) 0 . X = 0
= 0 X + 0 = X (With X = 0)
Based on the above two parts, x’y’ = (x + y)’
The second DeMorgans’ law is proved by duality. Note that DeMorgan’s Law, given as an identity is not an axiom in the sense that it can be proved using the other identities.

## Slide 96: Boolean Function Evaluation
z
x
y
x
F4
+
=
xy
F1
=
z
x
F2
=
y
z
+
x
z
y
x
z
y
x
F3
+
=
y
+
1
0
0
1
1
1
0
0
0
1
0
1
1
1
0
0
Notes: F3 is 1 for x’y’z’, x’yz, xy’z’ and xy’z => F3 = 1,0,0,1,1,1,0,0
F4 is 1 for xy’z’, xy’z, x’y’z and x’y z => F4 = 0,1,0,1,1,1,0,0

## Slide 97: More than 2 Inputs?
AND/OR can take any number of inputs.
  AND = 1 if all inputs are 1.
  OR = 0 if any input is 0.
  Similar for NAND/NOR.
Can implement with multiple two-input gates, or with single CMOS circuit.
Notes: NAND and NOR are not associative.
Jim Conrad’s example:
NAND(NAND(0,0), 1) = NAND(1, 1) = 0
NAND(0, NAND(0,1)) = NAND(0, 0) = 1

## Slide 98: Functions and Functional Blocks
The functions considered are those found to be very useful in design
Corresponding to each of the functions is a combinational circuit implementation called a functional block.
In the past, many functional blocks were implemented as SSI, MSI, and LSI circuits.
Today, they are often simply parts within a VLSI circuit.

## Slide 99: Rudimentary Logic Functions
Functions of a single variable X
Can be used on the inputs to functional blocks to implement other than the block’s intended function
Functions of
One
V
a
ria
b
le
X
F
= 0
F
= X
F
=
F = 1
0
1
0
0
0
1
1
0
1
1
X
0
1
F
0
F
1
(a)
F
0
F
1
V
CC
or V
DD
(b)
X
F
X
(c)
X
F
X
(d)

## Slide 100: Multiple-bit Rudimentary Functions
Multi-bit Examples:
A wide line is used to represent a bus which is a vector signal
In (b) of the example, F = (F3, F2, F1, F0) is a bus.
The bus can be split into individual bits as shown in (b)
Sets of bits can be split from the bus as shown in (c) for bits 2 and 1 of F.
The sets of bits need not be continuous as shown in (d) for bits 3, 1, and 0 of F.
4
2:1
F(2:1)
2
F
(c)
F
(d)
4
3,1:0
F(3), F(1:0)
3
0
F
3
1
F
2
F
1
A
F
0
(a)
A
0
1
A
1
2
3
4
F
0
(b)
A

## Slide 101: Enabling Function
Enabling permits an input signal to pass through to an output
Disabling blocks an input signal from passing through to an output, replacing it with a fixed value
The value on the output when it is disable can be Hi-Z (as for three-state buffers and transmission gates), 0 , or 1
When disabled, 0 output
When disabled, 1 output
Enabling applications?
X
F
EN
(a)
EN
X
F
(b)

## Slide 102: Decoding
Decoding - the conversion of an n-bit input code to an m-bit output code with n £ m £ 2n such that each valid code word produces a unique output code
Circuits that perform decoding are called decoders
Here, functional blocks for decoding are
  called n-to-m line decoders, where m £ 2n, and
  generate 2n (or fewer) minterms for the n input variables

## Slide 103: Decoder Examples
1-to-2-Line Decoder
2-to-4-Line Decoder
Note that the 2-4-line made up of 2 1-to-2- line decoders and 4 AND gates.
A
D
0
D
1
0
1
0
1
0
1
(a)
(b)
D
1
=
A
A
D
0
=
A
A
1
0
0
1
1
A
0
0
1
0
1
D
0
1
0
0
0
D
1
0
1
0
0
D
2
0
0
1
0
D
3
0
0
0
1
(a)
D
0
=
A
1
A
0
D
1
=
A
1
A
0
D
2
=
A
1
A
0
D
3
=
A
1
A
0
(b)
A
1
A
0

## Slide 104: Decoder Expansion - Example
Result

## Slide 105: Decoder with Enable
In general, attach m-enabling circuits to the outputs
Truth table for the function
  Note use of X’s to denote both 0 and 1
  Combination containing two X’s represent four binary combinations
Alternatively, can be viewed as distributing value of signal EN to 1 of 4 outputs
In this case, called a demultiplexer
EN
A
1
A
0
D
0
D
1
D
2
D
3
(b)
EN
A
1
A
0
D
0
D
1
D
2
D
3
0
1
1
1
1
X
0
0
1
1
X
0
1
0
1
0
1
0
0
0
0
0
1
0
0
0
0
0
1
0
0
0
0
0
1
(a)

## Slide 106: Encoding
Encoding - the opposite of decoding - the conversion of an m-bit input code to a n-bit output code with n £ m £ 2n such that each valid code word produces a unique output code
Circuits that perform encoding are called encoders
An encoder has 2n (or fewer) input lines and n output lines which generate the binary code corresponding to the input values
Typically, an encoder converts a code containing exactly one bit that is 1 to a binary code corresponding to the position in which the 1 appears.

## Slide 107: Selecting
Selecting of data or information is a critical function in digital systems and computers
Circuits that perform selecting have:
  A set of information inputs from which the selection is made
  A single output
  A set of control lines for making the selection
Logic circuits that perform selecting are called multiplexers
Selecting can also be done by three-state logic or transmission gates

## Slide 108: Multiplexers
A multiplexer selects information from an input line and directs the information to an output line
A typical multiplexer has n control inputs (Sn - 1, … S0) called selection inputs, 2n information inputs (I2n - 1, … I0), and one output Y
A multiplexer can be designed to have m information inputs with m < 2n as well as n selection inputs

## Slide 109: 2-to-1-Line Multiplexer
Since 2 = 21, n = 1
The single selection variable S has two values:
  S = 0 selects input I0
  S = 1 selects input I1
The equation:
Y = I0 + SI1
The circuit:
S

## Slide 110: Example: 4-to-1-line Multiplexer
2-to-22-line decoder
22 ´ 2 AND-OR
S
1
Decoder
S
0
Y
S
1
Decoder
S
0
Y
S
1
Decoder
4
x
2 AND-OR
S
0
Y
I
2
I
3
I
1
I
0

## Slide 111: Multiplexer Width Expansion
Select “vectors of bits” instead of “bits”
Use multiple copies of 2n ´ 2 AND-OR in parallel
Example: 4-to-1-line quad multi- plexer

## Slide 112: Functional Blocks: Addition
Binary addition used frequently
Addition Development:
  Half-Adder (HA), a 2-input bit-wise addition functional block,
  Full-Adder (FA), a 3-input bit-wise addition functional block,
  Ripple Carry Adder, an iterative array to perform binary addition, and
  Carry-Look-Ahead Adder (CLA), a hierarchical structure to improve performance.

## Slide 113: Functional Block: Half-Adder
A 2-input, 1-bit width binary adder that performs the following computations:
A half adder adds two bits to produce a two-bit sum
The sum is expressed as a sum bit , S and a carry bit, C
The half adder can be specified as a truth table for S and C 
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 0
0 1
0 1
1 0
X
Y
C
S
0
0
0
0
0
1
0
1
1
0
0
1
1
1
1
0

## Slide 114: Implementations: Half-Adder
The most common half adder implementation is (e)
A NAND only implementation is:
Y
X
C
Y
X
S
×
=
Å
=
)
(
C
)
Y
X
(
×
=
X
Y
C
S
X
Y
C
S
C
)
Y
X
(
S
×
+
=

## Slide 115: Functional Block: Full-Adder
A full adder is similar to a half adder, but includes a carry-in bit from lower stages. Like the half-adder, it computes a sum bit, S and a carry bit, C.
  For a carry-in (Z) of 0, it is the same as the half-adder:
  For a carry- in (Z) of 1:
Z
0
0
0
0
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0
0
0 1
0 1
1 0
Z
1
1
1
1
X
0
0
1
1
+ Y
+ 0
+ 1
+ 0
+ 1
C S
0 1
1 0
1 0
1
1

## Slide 116: Logic Optimization: Full-Adder
Full-Adder Truth Table:
Full-Adder K-Map:
X
Y
Z
C
S
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Z
0
1
3
2
4
5
7
6
1
1
1
1
S
X
Y
Z
0
1
3
2
4
5
7
6
1
1
1
1
C

## Slide 117: Equations: Full-Adder
From the K-Map, we get:
The S function is the three-bit XOR function (Odd Function):
The Carry bit C is 1 if both X and Y are 1 (the sum is 2), or if the sum is 1 and a carry-in (Z) occurs. Thus C can be re-written as:
The term X·Y is carry generate.
The term XY is carry propagate.
Z
Y
Z
X
Y
X
C
Z
Y
X
Z
Y
X
Z
Y
X
Z
Y
X
S
+
+
=
+
+
+
=
Z
Y
X
S
Å
Å
=
Z
)
Y
X
(
Y
X
C
Å
+
=

## Slide 118: Implementation: Full Adder
Full Adder Schematic
Here X, Y, and Z, and C (from the previous pages) are A, B, Ci and Co, respectively. Also, G = generate and P = propagate.
Note: This is really a combination of a 3-bit odd function (for S)) and Carry logic (for Co): (G = Generate) OR (P =Propagate AND Ci = Carry In)
Co = G + P · Ci
Ai
Bi
Ci
Ci+1
Gi
Pi
Si

## Slide 119: 4-bit Ripple-Carry Binary Adder
A four-bit Ripple Carry Adder made from four 1-bit Full Adders:

## Slide 120: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit (1's Complement.)
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 121: Combinational vs. Sequential
Combinational Circuit
  always gives the same output for a given set of inputs
    ex: adder always generates sum and carry, regardless of previous inputs
Sequential Circuit
  stores information
  output depends on stored information (state) plus input
    so a given input might produce different outputs, depending on the stored information

## Slide 122: Introduction to Sequential Circuits
Combinatorial Logic
  Next state function Next State = f(Inputs, State)
  Output function (Mealy) Outputs = g(Inputs, State)
  Output function (Moore) Outputs = h(State)
Output function type depends on specification and affects the design significantly
Combina-tional
Logic
Storage Elements
Inputs
Outputs
State
Next
State

## Slide 123: R-S Latch: Simple Storage Element
R is used to “reset” or “clear” the element – set it to zero.
S is used to “set” the element – set it to one.
If both R and S are one, out could be either zero or one.
  “quiescent” state -- holds its previous value
  note: if a is 1, b is 0, and vice versa
1
0
1
1
1
1
0
0
1
1
0
0
1
1

## Slide 124: R-S Latch Summary
R = S = 1
  hold current value in latch
R=1, S = 0
  set value to 1
R = 0, S = 1
  set value to 0
R = S = 0
  both outputs equal one
  final state determined by electrical properties of gates
  Don’t do it!

## Slide 125: D Latch
Adding an inverter to the S-R Latch, gives the D Latch:
Note that there are no “indeterminate” states!
Q
D
Q(t+1)
Comment
0
0
0
No change
0
1
1
Set Q
1
0
0
Clear Q
1
1
1
No Change
C
D
Q
Q
D
Q
C
Q

## Slide 126: Register
A register stores a multi-bit value.
  We use a collection of D-latches, all controlled by a common WE.
  When WE=1, n-bit value D is written to register.

## Slide 127: Representing Multi-bit Values
Number bits from right (0) to left (n-1)
  just a convention -- could be left to right, but must be consistent
Use brackets to denote range: D[l:r] denotes bit l to bit r, from left to right
May also see A<14:9>, especially in hardware block diagrams.
A = 0101001101010101
A[2:0] = 101
A[14:9] = 101001
0
15

## Slide 128: Memory
Now that we know how to store bits, we can build a memory – a logical k × m array of stored bits.
•
•
•
k = 2n
locations
m bits
Address Space:
number of locations (usually a power of 2)
Addressability:
number of bits per location (e.g., byte-addressable)

## Slide 129: 22 x 3 Memory
address
decoder
word select
word WE
address
write
enable
input bits
output bits
Notes: Decoder asserts one of the word select lines, based on address.
Word select activates one of the output AND gates, which drives the selected data to the output OR gate. (For a read, this is basically a MUX -- decoder ANDed with signals, results ORed together.)
When writing, the only WE bits for the proper word are asserted (based on decoder again).

## Slide 130: More Memory Details
This is a not the way actual memory is implemented.
  fewer transistors, much more dense, relies on electrical properties
But the logical structure is very similar.
  address decoder
  word select line
  word write enable
Two basic kinds of RAM (Random Access Memory)
Static RAM (SRAM)
  fast, maintains data as long as power applied
Dynamic RAM (DRAM)
  slower but denser, bit storage decays – must be periodically refreshed
Also, non-volatile memories: ROM, PROM, flash, …

## Slide 131: State Machine
Another type of sequential circuit
  Combines combinational logic with storage
  “Remembers” state, and changes output (and state) based on inputs and current state
State Machine
Combinational
Logic Circuit
Storage
Elements
Inputs
Outputs

## Slide 132: Combinational vs. Sequential
Two types of “combination” locks
4
1
8
4
30
15
5
10
20
25
Combinational
Success depends only on the values, not the order in which they are set.
Sequential
Success depends on the sequence of values
(e.g, R-13, L-22, R-3).

## Slide 133: The Clock
Frequently, a clock circuit triggers transition from one state to the next.
At the beginning of each clock cycle, state machine makes a transition, based on the current state and the external inputs.
“1”
“0”
time
One
Cycle

## Slide 134: Implementing a Finite State Machine
Combinational logic
  Determine outputs and next state.
Storage elements
  Maintain state representation.
State Machine
Combinational
Logic Circuit
Storage
Elements
Inputs
Outputs
Clock

## Slide 135: Storage: Master-Slave Flipflop
A pair of gated D-latches, to isolate next state from current state.
During 1st phase (clock=1), previously-computed state becomes current state and is sent to the logic circuit.
During 2nd phase (clock=0), next state, computed by logic circuit, is stored in Latch A.

## Slide 136: Storage
Each master-slave flipflop stores one state bit.
The number of storage elements (flipflops) needed is determined by the number of states (and the representation of each state).
Examples:
  Sequential lock
    Four states – two bits

## Slide 137: Finite State Machine
A description of a system with the following components:
A finite number of states
A finite number of external inputs
A finite number of external outputs
An explicit specification of all state transitions
An explicit specification of what determines each external output value
Often described by a state diagram.
  Inputs trigger state transitions.
  Outputs are associated with each state (or with each transition).

## Slide 138: State of Sequential Lock
Our lock example has four different states, labelled A-D:
A: The lock is not open, and no relevant operations have been performed.
B: The lock is not open, and the user has completed the R-13 operation.
C: The lock is not open, and the user has completed R-13, followed by L-22.
D: The lock is open.

## Slide 139: State Diagram
Shows states and actions that cause a transition between states.

## Slide 140: Sequential Circuit Design Procedure
Specification
Formulation
  Obtain a state diagram or state table
State Assignment
  Assign binary codes to the states
Flip-Flop Input Equation Determination
  Select flip-flop types and derive flip-flop equations from next state entries in the table
Output Equation Determination
  Derive output equations from output entries in the table
Optimization
  Optimize the equations
Technology Mapping
  Find circuit from equations and map to flip-flops and gate technology
Verification
  Verify correctness of final design

## Slide 141: Example: Sequence Recognizer Procedure
To develop a sequence recognizer state diagram:
  Begin in an initial state in which NONE of the initial portion of the sequence has occurred (typically “reset” state).
  Add a state that recognizes that the first symbol has occurred.
  Add states that recognize each successive symbol occurring.
  The final state represents the input sequence (possibly less the final input value) occurence.
  Add state transition arcs which specify what happens when a symbol not in the proper sequence has occurred.
  Add other arcs on non-sequence inputs which transition to states that represent the input subsequence that has occurred.
The last step is required because the circuit must recognize the input sequence regardless of where it occurs within the overall sequence applied since “reset.”.

## Slide 142: State Assignment
Each of the m states must be assigned a unique code
Minimum number of bits required is n such that n ≥ log2 m where x is the smallest integer ≥ x
There are useful state assignments that use more than the minimum number of bits
There are 2n - m unused states

## Slide 143: Sequence Recognizer Example
Example: Recognize the sequence 1101
  Note that the sequence 1111101 contains 1101 and "11" is a proper sub-sequence of the sequence.
Thus, the sequential machine must remember that the first two one's have occurred as it receives another symbol.
Also, the sequence 1101101 contains 1101 as both an initial subsequence and a final subsequence with some overlap, i. e., 1101101 or 1101101.
And, the 1 in the middle, 1101101, is in both subsequences.
The sequence 1101 must be recognized each time it occurs in the input sequence.

## Slide 144: Example: Recognize 1101
Define states for the sequence to be recognized:
  assuming it starts with first symbol,
  continues through each symbol in the sequence to be recognized, and
  uses output 1 to mean the full sequence has occurred,
  with output 0 otherwise.
Starting in the initial state (Arbitrarily named "A"):
  Add a state that recognizes the first "1."
  State "A" is the initial state, and state "B" is the state which represents the fact that the "first" one in the input subsequence has occurred.
  The output symbol "0" means that the full recognized sequence has not yet occurred.
A
B
1/0

## Slide 145: Example: Recognize 1101 ...
After one more 1, we have:
  C is the state obtained when the input sequence has two "1"s.
Finally, after 110 and a 1, we have:
  Transition arcs are used to denote the output function (Mealy Model)
  Output 1 on the arc from D means the sequence has been recognized
  To what state should the arc from state D go? Remember: 1101101 ?
  Note that D is the last state but the output 1 occurs for the input applied in D. This is the case when a Mealy model is assumed.
A
B
1/0
C
1/0
A
B
1/0
C
1/0
0/0
D
1/1

## Slide 146: Example: Recognize 1101 ...
Clearly the final 1 in the recognized sequence 1101 is a sub-sequence of 1101. It follows a 0 which is not a sub-sequence of 1101. Thus it should represent the same state reached from the initial state after a first 1 is observed. We obtain:
1/1
D
A
B
1/0
C
1/0
0/0
A
B
1/0
C
1/0
0/0
D
1/1
23Ekim2k8

## Slide 147: Example: Recognize 1101 ...
The state have the following abstract meanings:
  A: No proper sub-sequence of the sequence has occurred.
  B: The sub-sequence 1 has occurred.
  C: The sub-sequence 11 has occurred.
  D: The sub-sequence 110 has occurred.
  The 1/1 on the arc from D to B means that the last 1 has occurred and thus, the sequence is recognized.
1/1
A
B
1/0
C
1/0
D
0/0

## Slide 148: Example: Recognize 1101 ...
The other arcs are added to each state for inputs not yet listed. Which arcs are missing?
  "0" arc from A
  "0" arc from B
  "1" arc from C
  "0" arc from D.
1/1
A
B
1/0
C
1/0
D
0/0

## Slide 149: Example: Recognize 1101 ...
State transition arcs must represent the fact that an input subsequence has occurred. Thus we get:
Note that the 1 arc from state C to state C implies that State C means two or more 1's have occurred.
C
1/1
A
B
1/0
1/0
D
0/0
0/0
0/0
1/0
0/0

## Slide 150: Formulation: Find State Table
From the State Diagram, we can fill in the State Table.
There are 4 states, one input, and one output. We will choose the form with four rows, one for each current state.
From State A, the 0 and 1 input transitions have been filled in along with the outputs.
1/0
0/0
0/0
1/1
A
B
1/0
C
1/0
D
0/0
0/0
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
B
C
D
1/0
B
0
0/0
A
0

## Slide 151: Formulation: Find State Table
From the state diagram,
we complete the state table.
What would the state diagram and state table look like for the Moore model?
1/0
0/0
0/0
0/0
1/1
A
B
1/0
C
1/0
D
0/0
State
Present
Next State
x=0 x=1
Output
x=0 x=1
A
A B
0 0
B
A C
0 0
C
D C
0 0
D
A B
0 1

## Slide 152: Example: Moore Model for Sequence 1101
For the Moore Model, outputs are associated with states.
We need to add a state "E" with output value 1 for the final 1 in the recognized input sequence.
  This new state E, though similar to B, would generate an output of 1 and thus be different from B.
The Moore model for a sequence recognizer usually has more states than the Mealy model.

## Slide 153: Example: Moore Model ...
We mark outputs on states for Moore model
Arcs now show only state transitions
Add a new state E to produce the output 1
Note that the new state, E produces the same behavior in the future as state B. But it gives a different output at the present time. Thus these states do represent a different abstraction of the input history.
A/0
B/0
C/0
D/0
0
E/1
0
0
0
1
1
1
1
1
0

## Slide 154: Example: Moore Model ...
The state table is shown below
A/0
B/0
C/0
D/0
0
E/1
0
0
0
1
1
1
1
1
0
Present
State
Next State
x=0 x=1
Output
y
A
A
B
0
B
A
C
0
C
D
C
0
D
A
E
0
E
A
C
1

## Slide 155: State Assignment – Example 1
How may assignments of codes with a minimum number of bits?
  Two
    A = 0, B = 1 or A = 1, B = 0
Does it make a difference?
  Only in variable inversion, so small, if any.
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
A
B
0
0
B
A
B
0
1

## Slide 156: State Assignment – Example 2
How may assignments of codes with a minimum number of bits?
  4  3  2  1 = 24
Does code assignment make a difference in cost?
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
A B
0 0
B
A C
0 0
C
D C
0 0
D
A B
0 1

## Slide 157: State Assignment – Example 2 ...
Assignment 1: A = 0 0, B = 0 1, C = 1 0, D = 1 1
The resulting coded state table:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 1 1 | 1 0 | 0 | 0
1 1 | 0 0 | 0 1 | 0 | 1

## Slide 158: State Assignment – Example 2 ...
Assignment 2: A = 0 0, B = 0 1, C = 1 1, D = 1 0
The resulting coded state table:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 1 | 0 | 0
1 1 | 1 0 | 1 1 | 0 | 0
1 0 | 0 0 | 0 1 | 0 | 1

## Slide 159: Find Flip-Flop Input and Output Equations: Example 2 - Assignment 1
Y2
Y1
X
1
0
0
0
0
0
0
0
Y2
Y1
X
0
0
1
0
1
0
0
1
Y2
Y1
X
1
0
0
0
0
0
1
1
D1
D2
Z
Assume D flip-flops
Interchange the bottom two rows of the state table, to obtain K-maps for D1, D2, and Z:

## Slide 160: Optimization: Example 2: Assignment 1
Performing two-level optimization:
D1 = Y1Y2 + XY1Y2 D2 = XY1Y2 + XY1Y2 + XY1Y2 Z = XY1Y2 Gate Input Cost = 22
Y2
Y1
X
1
0
0
0
0
0
0
0
Y2
Y1
X
0
0
1
0
1
0
0
1
Y2
Y1
X
1
0
0
0
0
0
1
1
D1
D2
Z

## Slide 161: Find Flip-Flop Input and Output Equations: Example 2 - Assignment 2
Y2
Y1
X
1
0
0
0
0
0
0
0
Y2
Y1
X
1
0
1
0
1
0
1
0
Y2
Y1
X
0
0
0
0
1
1
1
0
Assume D flip-flops
Obtain K-maps for D1, D2, and Z:
D1
D2
Z

## Slide 162: Optimization: Example 2: Assignment 2
Performing two-level optimization:
D1 = Y1Y2 + XY2 Gate Input Cost = 9 D2 = X Select this state assignment for Z = XY1Y2 completion of the design
Y2
Y1
X
1
0
0
0
0
0
0
0
Y2
Y1
X
1
0
1
0
1
0
1
0
Y2
Y1
X
0
0
0
0
1
1
1
0
D1
D2
Z

## Slide 163: Map Technology
Library:
  D Flip-flops with Reset (not inverted)
  NAND gates with up to 4 inputs and inverters
Initial Circuit:
Clock
D
D
C
R
Y2
Z
C
R
Y1
X
Reset

## Slide 164: Mapped Circuit - Final Result
Clock
D
D
C
R
Y2
Z
C
R
Y1
X
Reset

## Slide 165
SCHEMATICS &
SIMULATION
LAYOUT
MIXED SIGNAL
INTEGRATION
FINAL
SYNTHESIS & SIMULATION
STATIC TIMING ANALYSIS
LAYOUT,
PLACE & ROUTE
FINAL
MIXED SIGNAL
INTEGRATION
VHDL
Cadence
Leapfrog
Synopsys
Design Analyzer
VERILOG
Virtuoso
VirtuosoMixed Signal
Synopsys
DC shell
PEARL
Silicon
Ensemble
GDSII
for
foundry
GDSII
Cadence
Spectre
ANALOGUE
DIGITAL
Typical mixed signal design flow

## Slide 166: The chip manufacturing process
Notes: After being sliced from the silicon ingot, blank wafers are put through 20 to 40 steps to create patterned wafers (see Figure 1.13). These patterned wafers are then tested with a wafer tester, and a map of the good parts is made. Then, the wafers are diced into dies (see Figure 1.9). In this figure, one wafer produced 20 dies, of which 17 passed testing. (X means the die is bad.) The yield of good dies in this case was 17/20, or 85%. These good dies are then bonded into packages and tested one more time before shipping the packaged parts to customers. One bad packaged part was found in this final test.

## Slide 167: A 12-inch (300 mm) wafer of Intel Core i7 (Courtesy Intel)
Notes: A 12-inch (300 mm) wafer of Intel Core i7 (Courtesy Intel). The number of dies on this 300 mm (12 inch) wafer at 100% yield is 280, each 20.7 by 10.5 mm. The several dozen partially rounded chips at the boundaries of the wafer are useless; they are included because it’s easier to create the masks used to pattern the silicon. This die uses a 32-nanometer technology, which means that the smallest features are approximately 32 nm in size, although they are typically somewhat smaller than the actual feature size, which refers to the size of the transistors as “drawn” versus the final manufactured size.

## Slide 168
SRAM
Analogue signal conditioning modules
uProcessor
ADC
Serial-parallel interface
Oscillator+DAC
DS-SS Encoder
Hall-effect sensor
RF
Clock divider
Typical post synthesis layout

## Slide 169
Picture of the fabricated chip

## Slide 171: Testing board for the chip
Top side Bottom side
Notes: In this slide top and bottom sides of the testing board are shown. This board was designed by Alex and produced in-house (Electronics lab in Edinburgh).