## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
http://www.yildiz.edu.tr/~naydin

## Slide 2: The Von Neumann Model/Architecture
Also called stored program computer (instructions in memory).
Two key properties:
  Stored program
    Instructions stored in a linear memory array
    Memory is unified between instructions and data
      The interpretation of a stored value depends on the control signals
        When is a value interpreted as an instruction?
  Sequential instruction processing
    One instruction processed (fetched, executed, and completed) at a time

## Slide 3: A computing System (Reminder)
What is a computer?
  in terms of what?
    Functional
    Structural
Functional definition
  Data processing
  Data storage
  Data movement
  Control
Structural definition
  Central processing unit
  Main memory
  Input/Output
  System interconnection

## Slide 4: Structure - Top Level
Computer
Computer
Peripherals
Communication
lines
Main
Memory
Input
Output
Systems
Interconnection
Central
Processing
Unit

## Slide 5: Structure - The CPU
CPU
Computer
CPU
I/O
Memory
System
Bus
Arithmetic
and
Logic Unit
Control
Unit
Internal CPU
Interconnection
Registers

## Slide 6: Structure - The Control Unit
Control Unit
Control
Memory
Control Unit
Registers and
Decoders
Sequencing
Logic
CPU
Control
Unit
ALU
Registers
Internal
Bus

## Slide 7: The Stored Program Computer
1943: ENIAC
  Presper Eckert and John Mauchly -- first general electronic computer. (or was it John V. Atanasoff in 1939?)
  Hard-wired program -- settings of dials and switches.
1944: Beginnings of EDVAC
  among other improvements, includes program stored in memory
1945: John von Neumann
  wrote a report on the stored program concept, known as the First Draft of a Report on EDVAC
The basic structure proposed in the draft became known as the “von Neumann machine” (or model).
  a memory, containing instructions and data
  a processing unit, for performing arithmetic and logical operations
  a control unit, for interpreting instructions

## Slide 8: Von Neumann Model

## Slide 9: ENIAC - details
Decimal (not binary)
20 accumulators of 10 digits
Programmed manually by switches
18,000 vacuum tubes
30 tons
15,000 square feet
140 kW power consumption
5,000 additions per second
http://www.seas.upenn.edu/~museum/

## Slide 10: Interface to Memory
How does processing unit get data to/from memory?
MAR: Memory Address Register
MBR (MDR): Memory Buffer (Data) Register
To LOAD a memory location (A):
  Write the address (A) into the MAR.
  Send a “read” signal to the memory.
  Read the data from MBR.
To STORE a value (X) to a location (A):
  Write the data (X) to the MBR.
  Write the address (A) into the MAR.
  Send a “write” signal to the memory.

## Slide 11: Processing Unit
Functional Units (Execution unit)
  ALU = Arithmetic and Logic Unit
  could have many functional units. some of them special-purpose (multiply, square root, …)
Registers
  Small, temporary storage
  Operands and results of functional units
Word Size
  number of bits normally processed by ALU in one instruction
  also width of registers

## Slide 12: Input and Output
Devices for getting data into and out of computer memory
Each device has its own interface, usually a set of registers (I/OAR and I/OBR)
Some devices provide both input and output
  disk, network
Program that controls access to a device is usually called a driver.

## Slide 13: Control Unit
Orchestrates execution of the program
Instruction Register (IR) contains the current instruction.
Program Counter (PC) contains the address of the next instruction to be executed.
Control unit:
  reads an instruction from memory
    the instruction’s address is in the PC
  interprets the instruction, generating signals that tell the other components what to do
    an instruction may take many machine cycles to complete

## Slide 14: Program Concept
Hardwired systems are inflexible
General purpose hardware can do different tasks, given correct control signals
Instead of re-wiring, supply a new set of control signals

## Slide 15: What is a program?
A sequence of steps
For each step, an arithmetic or logical operation is done
For each operation, a different set of control signals is needed

## Slide 16: Instruction Processing
Decode instruction
Evaluate Address
fetch OPerands from memory
EXecute operation
Store result
Fetch instruction from memory

## Slide 17: Instruction
The instruction is the fundamental unit of work.
Specifies two things:
  opcode: operation to be performed
  operands: data/locations to be used for operation
An instruction is encoded as a sequence of bits. (Just like data!)
  Often, but not always, instructions have a fixed length, such as 16 or 32 bits.
  Control unit interprets instruction: generates sequence of control signals to carry out operation.
  Operation is either executed completely, or not at all.
A computer’s instructions and their formats is known as its Instruction Set Architecture (ISA).

## Slide 18: Instruction Processing: FETCH
Load next instruction (at address stored in PC) from memory into Instruction Register (IR).
  Copy contents of PC into MAR.
  Send “read” signal to memory.
  Copy contents of MBR into IR.
Then increment PC, so that it points to the next instruction in sequence.
  PC becomes PC+1.
EA
OP
EX
S
F
D

## Slide 19: Instruction Processing: DECODE
First identify the opcode.
  A n-to-2n decoder asserts a control line corresponding to the desired opcode.
Depending on opcode, identify other operands from the remaining bits.
EA
OP
EX
S
F
D

## Slide 20: Instruction Processing: EVALUATE ADDRESS
For instructions that require memory access, compute address used for access.
Examples:
  add offset to base register
  add offset to PC
  add offset to zero
EA
OP
EX
S
F
D

## Slide 21: Instruction Processing: FETCH OPERANDS
Obtain source operands needed to perform operation.
Examples:
  load data from memory (LDA)
  read data from register file (ADD)
EA
OP
EX
S
F
D

## Slide 22: Instruction Processing: EXECUTE
Perform the operation, using the source operands.
Examples:
  send operands to ALU and assert ADD signal
  do nothing (e.g., for loads and stores)
EA
OP
EX
S
F
D

## Slide 23: Instruction Processing: STORE RESULT
Write results to destination. (register or memory)
Examples:
  result of ADD is placed in destination register
  result of memory load is placed in destination register
  for store instruction, data is stored to memory
    write address to MAR, data to MBR
    assert WRITE signal to memory
EA
OP
EX
S
F
D

## Slide 24: Changing the Sequence of Instructions
In the FETCH phase, we increment the Program Counter by 1.
What if we don’t want to always execute the instruction that follows this one?
  examples: loop, if-then, function call
Need special instructions that change the contents of the PC.
These are called control instructions.
  jumps are unconditional -- they always change the PC
  branches are conditional -- they change the PC only if some condition is true (e.g., the result of an ADD is zero)

## Slide 25: Instruction Processing Summary
Instructions look just like data -- it’s all interpretation.
Four basic kinds of instructions:
  Data processing instructions
    Arithmetic and logic instructions (ADD, AND, …)
  Data storage instructions
    Memory instructions (LDA, STA)
  Data movement instructions
    I/O instructions (IN, OUT, …)
  Program flow control instructions
    Test and branch instructions (JMP, BRP, …)
Six basic phases of instruction processing:
F  D  EA  OP  EX  S
  not all phases are needed by every instruction
  phases may take variable number of machine cycles

## Slide 26: Control Unit State Diagram
The control unit is a state machine.
Here is part of a simplified state diagram:

## Slide 27: Stopping the Clock
Control unit will repeat instruction processing sequence as long as clock is running.
  If not processing instructions from your application, then it is processing instructions from the Operating System (OS).
  The OS is a special program that manages processor and other resources.
To stop the computer:
  AND the clock generator signal with ZERO
  When control unit stops seeing the CLOCK signal, it stops processing.

## Slide 28: Dataflow Model of a Computer
Von Neumann model
An instruction is fetched and executed in control flow order
  As specified by the instruction pointer
  Sequential unless explicit control flow instructio
Dataflow model
An instruction is fetched and executed in data flow order
  i.e., when its operands are ready
  i.e., there is no instruction pointer
  Instruction ordering specified by data flow dependence
    Each instruction specifies “who” should receive the result
    An instruction can “fire” whenever all operands are received
  Potentially many instructions can execute at the same time
  Inherently more parallel

## Slide 29: von Neumann vs Dataflow
Consider a von Neumann program (sequential) vs dataflow execution
Which model is more natural to you as a programmer?
All major instruction set architectures today use von Neumann
  x86, ARM, MIPS, SPARC, Alpha, POWER PC

## Slide 30
Fundamental Computer Elements

## Slide 31: Fundamental computer elements
Data processing
  Provided by gates
Data storage
  Provided by memory cells
Data movement
  The paths between components are used to move data from/to memory
Control
  The paths between components can carry control signals

## Slide 32: Levels of Representation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
ALUOP[0:3] <= InstReg[9:11] & MASK
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Specification
Compiler
Assembler
Machine Interpretation
°
°

## Slide 33: Computer Components-CPU

## Slide 34: CPU Structure
CPU must:
  Fetch instructions
  Interpret instructions
  Fetch data
  Process data
  Write data
Notes: 22

## Slide 35: Registers
CPU must have some working space (temporary storage)
  Called registers
Number and function vary between processor designs
One of the major design decisions
Top level of memory hierarchy
Notes: 23

## Slide 36: Registers in the P perform two roles:
User-visible registers
  Enable the machine- or assembly language programmer to minimize main memory references by optimizing use of registers
Control and status registers
  Used by the control unit to control the operation of the processor and by priviliged, operating system programs to control the execution of programs

## Slide 37: User Visible Registers
General Purpose registers
Data registers
Address registers
Condition Codes (flags)
Notes: 24

## Slide 38: Condition Code Registers
Sets of individual bits
  e.g. result of last operation was zero
Can be read (implicitly) by programs
  e.g. Jump if zero
Can not (usually) be set by programs
Notes: 29

## Slide 39: Control & Status Registers
Program Counter (PC)
  Contains the address of an instruction to be fetched
Instruction Decoding Register (IR)
  Contains the instruction most recently fetched
Memory Address Register (MAR)
  Contains the addres of location in memory
Memory Buffer Register (MBR)
  Contains a word or data to be written to memory or the word most recently read
Notes: 30

## Slide 40: Program Status Word
A set of bits containing status information
Includes Condition Codes (flags)
  Sign
    sign of last result
  Zero
    set when the result is 0
  Carry
    set if an operation resulted in a carry (addition) into or borrow (subtraction) out of a high order bit
  Equal
    set if a logical compare result is equality
  Overflow
    used to indicate arithmetic overflow
  Interrupt enable/disable
    used to enable or disable interrupts
Notes: 31

## Slide 41: Example Register Organizations

## Slide 42: Computer Components-Memory

## Slide 43: Operation of Memory
Each memory location has a unique address
Address from an instruction is copied to the MAR which finds the location in memory
CPU determines if it is a store or retrieval
Transfer takes place between the MBR and memory
  MBR is a two way register

## Slide 44: Relationship between MAR, MBR and Memory
Address
Data

## Slide 45: MAR-MBR Example

## Slide 46: Visual Analogy of Memory

## Slide 47: Individual Memory Cell

## Slide 48: Memory Capacity
Determined by two factors
  Number of bits in the MAR
    2K where K = width of the register in bits
  Size of the address portion of the instruction
    4 bits allows 16 locations
    8 bits allows 256 locations
    32 bits allows 4,294,967,296 or 4 GB
Important for performance
  Insufficient memory can cause a processor to work at 50% below performance

## Slide 49: Memory Hierarchy
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store

## Slide 50: Memory Hierarchy
This storage organization can be thought of as a pyramid:

## Slide 51: Cache
Small amount of fast memory
Sits between normal main memory and CPU
May be located on CPU chip or module

## Slide 52: Virtual Memory
Cache memory enhances performance by providing faster memory access speed.
Virtual memory enhances performance by providing greater memory capacity, without the expense of adding main memory.
Instead, a portion of a disk drive serves as an extension of main memory.
If a system uses paging, virtual memory partitions main memory into individually managed page frames, that are written (or paged) to disk when they are not immediately needed.

## Slide 53: RAM: Random Access Memory
DRAM (Dynamic RAM)
  Most common, cheap
  Volatile: must be refreshed (recharged with power) 1000’s of times each second
SRAM (static RAM)
  Faster than DRAM and more expensive than DRAM
  Volatile
  Frequently small amount used in cache memory for high-speed access used

## Slide 54: Dynamic RAM Structure

## Slide 55: Stating RAM Structure

## Slide 56: Read Only Memory (ROM)
Permanent storage
  Nonvolatile
Used in...
  Microprogramming
  Library subroutines
  Systems programs (BIOS)
  Function tables

## Slide 57: Types of ROM
Written during manufacture
  Very expensive for small runs
Programmable (once)
  PROM
  Needs special equipment to program
Read “mostly”
  Erasable Programmable (EPROM)
    Erased by UV
  Electrically Erasable (EEPROM)
    Takes much longer to write than read
  Flash memory
    Erase whole memory electrically

## Slide 58: Types of External Memory
SSD
  Fast
  Expensive (relatively)
Magnetic Disk
  RAID
  Removable
Optical
  CD-ROM
  CD-Recordable (CD-R)
  CD-R/W
  DVD
Magnetic Tape

## Slide 59: Computer Components-I/O

## Slide 60: Input/Output Problems
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU and RAM
Need I/O modules

## Slide 61: Input/Output Module
Interface to CPU and Memory
Interface to one or more peripherals
I/O Module Function:
  Control & Timing
  CPU Communication
  Device Communication
  Data Buffering
  Error Detection
I/O Module Block Diagram

## Slide 62: External Devices
External Devices:
  Human readable
    Screen, printer, keyboard
  Machine readable
    Monitoring and control
  Communication
    Modem
    Network Interface Card (NIC)
External Device Block Diagram

## Slide 63: I/O Steps
CPU checks I/O module device status
I/O module returns status
If ready, CPU requests data transfer
I/O module gets data from device
I/O module transfers data to CPU
Variations for output, DMA, etc.

## Slide 64: I/O Architectures
I/O can be controlled in four general ways:
  Programmed I/O
    Reserves a register for each I/O device.
    Each register is continually polled to detect data arrival.
  Interrupt-Driven I/O
    Allows the CPU to do other things until I/O is requested.
  Direct Memory Access (DMA)
    Offloads I/O processing to a special-purpose chip that takes care of the details.
  Channel I/O
    Uses dedicated I/O processors.

## Slide 65: Computer Components- Bus

## Slide 66: Bus
The physical connection that makes it possible to transfer data from one location in the computer system to another
Group of electrical conductors for carrying signals from one location to another
4 kinds of signals
  Data
    Alphanumeric
    Numerical
    instructions
  Addresses
  Control signals
  Power (sometimes)

## Slide 67: Bus
Connects CPU and Memory
I/O peripherals: on the same bus as CPU/memory or separate bus
Physical packaging commonly called backplane
  Also called system bus or external bus
  Example of broadcast bus (address bus)
  Part of printed circuit board called motherboard that holds CPU and related components

## Slide 68: Bus Characteristics
Protocol
  Documented agreement for communication
  Specification that spells out the meaning of each line and each signal on each line
Throughput, i.e., data transfer rate in bits per second
Data width in bits carried simultaneously

## Slide 69: Bus types
Data Bus
  Carries data
  Width is a key determinant of performance
    8, 16, 32, 64 bit
  Address bus
  Identify the source or destination of data
  Bus width determines maximum memory capacity of system
    e.g. 8080 has 16 bit address bus giving 64k address space
  Control Bus
  Control and timing information
    Memory read/write; I/O read/write; Transfer acknowledge; Bus request; Bus grant; Interrupt request; Interrupt acknowledge; Clock; Reset

## Slide 70: What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires
Physical Realization of Bus Architecture

## Slide 71: Motherboard
Printed circuit board that holds CPU and related components including backplane

## Slide 73: Typical PC Interconnections
Bus interface bridges connect different bus types

## Slide 74: Instructions
Instruction:
  Direction given to a computer
  Causes electrical signals to be sent through specific circuits for processing
The operation of the processor is determined by the instructions it executes,
  which is referrred as machine instructions or computer instructions
The collection of different instructions that the processor execute is referred as the processor’s instruction set.

## Slide 75: What is an Instruction Set?
The complete collection of instructions that are understood by a CPU
  Machine Code
  Binary
Usually represented by assembly codes
Differentiates computer architecture by the
  Number of instructions
  Complexity of operations performed by individual instructions
  Data types supported
  Format (layout, fixed vs. variable length)
  Use of registers
  Addressing (size, modes)
Notes: 2

## Slide 76: Instruction Elements
Operation code (OPCODE): task
  Do this
Source OPERAND reference(s)
  To this
Result OPERAND reference
  Put the answer here
Next Instruction Reference
  When you have done that, do this...
OPCODE
Source
OPERAND
Result
OPERAND
Addresses

## Slide 77: Instruction Elements
Source and Result Operands can be in one of the following areas:
  Main memory
  Virtual memory
  Cache
  CPU register
  I/O device
Notes: 4

## Slide 78: Instruction Format
Machine-specific template that specifies
  Length of the op code
  Number of operands
  Length of operands
Simple 32-bit Instruction Format

## Slide 79: Instruction Types
Data Transfer (load, store)
  Most common, greatest flexibility
  Involve memory and registers
  What’s a word ? 16? 32? 64 bits?
Arithmetic
  Operators + - / * ^
  Integers and floating point
Logical or Boolean
  Relational operators: > < =
  Boolean operators AND, OR, XOR, NOR, and NOT
Single operand manipulation instructions
  Negating, decrementing, incrementing

## Slide 80: More Instruction Types
Bit manipulation instructions
  Flags to test for conditions
Shift and rotate
Program control
Stack instructions
Multiple data instructions
I/O and machine control

## Slide 81: Register Shifts and Rotates

## Slide 82: Program Control Instructions
Program control
  Jump and branch
  Subroutine call and return

## Slide 83: Instruction Cycle
Two steps:
  Fetch
  Execute

## Slide 84: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and performs required actions

## Slide 85: Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 86: A simple example – A hypotetical machine

## Slide 87: A simple example –
Next figure illustrates a partial program execution.
It adds the contents of the memory word at address 940 to the contents of the memory word at address 941 and stores the result in the address 941.
Here 3 instructions (3 fetch and 3 execute cycles) are required

## Slide 88: Example of Program Execution

## Slide 89
A virtual processor for understanding instruction cycle
The Visible Virtual Machine (VVM)

## Slide 90: The von Neumann Model
This is a general depiction of a von Neumann system:
These computers employ a fetch-decode-execute cycle to run programs as follows . . .

## Slide 91
The control unit fetches the next instruction from memory using the program counter to determine where the instruction is located.

## Slide 92
The instruction is decoded into a language that the ALU can understand.

## Slide 93
Any data operands required to execute the instruction are fetched from memory and placed into registers within the CPU.

## Slide 94
The ALU executes the instruction and places results in registers or memory.

## Slide 95: A virtual processor for understanding instruction cycle

## Slide 96: The VVM Machine
The Visible Virtual Machine (VVM) is based on a model of a simple computer device called the Little Man Computer which was originally developed by Stuart Madnick in 1965, and revised in 1979.
The VVM is a virtual machine because it only appears to be a functioning hardware device.
In reality, the VVM "hardware" is created through a software simulation. One important simplifying feature of this machine is that it works in decimal rather than in the traditional binary number system.
Also, the VVM works with only one form of data - decimal integers.

## Slide 97: Hardware Components of VVM
I/O Log. This represents the system console which shows the details of relevant events in the execution of the program. Examples of events are the program begins, the program aborts, or input or output is generated.
Accumulator Register (Accum). This register holds the values used in arithmetic and logical computations. It also serves as a buffer between input/output and memory. Legitimate values are any integer between -999 and +999. Values outside of this range will cause a fatal VVM Machine error. Non integer values are converted to integers before being loaded into the register.
Instruction Cycle Display. This shows the number of instructions that have been executed since the current program execution began.

## Slide 98: Hardware Components of VVM
Instruction Register (Instr. Reg.). This register holds the next instruction to be executed. The register is divided into two parts: a one-digit operation code, and a two digit operand. The Assembly Language mnemonic code for the operation code is displayed below the register.
Program Counter Register (Prog. Ctr.). The two-digit integer value in this register "points" to the next instruction to be fetched from RAM. Most instructions increment this register during the execute phase of the instruction cycle. Legitimate values range from 00 to 99. A value beyond this range causes a fatal VVM Machine error.
RAM. The 100 data-word Random Access Storage is shown as a matrix of ten rows and ten columns. The two-digit memory addresses increase sequentially across the rows and run from 00 to 99. Each storage location can hold a three-digit integer value between -999 and +999.

## Slide 99: Data and Addresses
All data and address values are maintained as decimal integers.
The 100 data-word memory is addresses with two-digit addressed in the range 00-99.
Each memory location holds one data-word which is a decimal integer in the range -999 - +999.
Data values beyond this range cause a data overflow condition and trigger a VVM system error.

## Slide 100: VVM Program Editor

## Slide 101: VVM Program Editor

## Slide 102: VVM Structure and User Interface

## Slide 103: VVM System Errors
Data value out of range. This condition occurs when a data value exceeds the legitimate range -999 - +999. The condition will be detected while the data resides in the Accumulator Register. Probable causes are an improper addition or subtraction operation, or invalid user input.
Undefined instruction. This occurs when the machine attempts to execute a three-digit value in the Instruction Register which can not be interpreted as a valid instruction code. See the help topic "VVM Language" for valid instruction codes and their meaning. Probable causes of this error are attempting to use a data value as an instruction, an improper Branch instruction, or failure to provide a Halt instruction in your program.
Program counter out of range. This occurs when the Program Counter Register is incremented beyond the limit of 99. The likely cause is failure to include a Halt instruction in your program, or a branch to a high memory address.
User cancel. The user pressed the "Cancel" button during an Input or Output operation.

## Slide 104: The Language Instructions
Load Accumulator (5nn) [LDA nn] The content of RAM address nn is copied to the Accumulator Register, replacing the current content of the register. The content of RAM address nn remains unchanged. The Program Counter Register is incremented by one.
Store Accumulator (3nn) [STO nn] or [STA nn] The content of the Accumulator Register is copied to RAM address nn, replacing the current content of the address. The content of the Accumulator Register remains unchanged. The Program Counter Register is incremented by one.
Add (1nn) [ADD nn] The content of RAM address nn is added to the content of the Accumulator Register, replacing the current content of the register. The content of RAM address nn remains unchanged. The Program Counter Register is incremented by one.

## Slide 105: The Language Instructions
Subtract (2nn) [SUB nn] The content of RAM address nn is subtracted from the content of the Accumulator Register, replacing the current content of the register. The content of RAM address nn remains unchanged. The Program Counter Register is incremented by one.
Input (901) [IN] or [INP] A value input by the user is stored in the Accumulator Register, replacing the current content of the register. Note that the two-digit operand does not represent an address in this instruction, but rather specifies the particulars of the I/O operation (see Output). The operand value can be omitted in the Assembly Language format. The Program Counter Register is incremented by one with this instruction.
Output (902) [OUT] or [PRN] The content of the Accumulator Register is output to the user. The current content of the register remains unchanged. Note that the two-digit operand does not represent an address in this instruction, but rather specifies the particulars of the I/O operation (see Input). The operand value can be omitted in the Assembly Language format. The Program Counter Register is incremented by one with this instruction.

## Slide 106: The Language Instructions
Branch if Zero (7nn) [BRZ nn] This is a conditional branch instruction. If the value in the Accumulator Register is zero, then the current value of the Program Counter Register is replaced by the operand value nn (the result is that the next instruction to be executed will be taken from address nn rather than from the next sequential address). Otherwise (Accumulator >< 0), the Program Counter Register is incremented by one (thus the next instruction to be executed will be taken from the next sequential address).
Branch if Positive or Zero (8nn) [BRP nn] This is a conditional branch instruction. If the value in the Accumulator Register is nonnegative (i.e., >= 0), then the current value of the Program Counter Register is replaced by the operand value nn (the result is that the next instruction to be executed will be taken from address nn rather than from the next sequential address). Otherwise (Accumulator < 0), the Program Counter Register is incremented by one (thus the next instruction to be executed will be taken from the next sequential address).
Branch (6nn) [BR nn] or[BRU nn] or [JMP nn] This is an unconditional branch instruction. The current value of the Program Counter Register is replaced by the operand value nn. The result is that the next instruction to be executed will be taken from address nn rather than from the next sequential address. The value of the Program Counter Register is not incremented with this instruction.

## Slide 107: The Language Instructions
No Operation (4nn) [NOP] or [NUL] This instruction does nothing other than increment the Program Counter Register by one. The operand value nn is ignored in this instruction and can be omitted in the Assembly Language format. (This instruction is unique to the VVM and is not part of the Little Man Model.)
Halt (0nn) [HLT] or [COB] Program execution is terminated. The operand value nn is ignored in this instruction and can be omitted in the Assembly Language format.
Embedding Data in Programs
Data values used by a program can be loaded into memory along with the program. In Machine or Assembly Language form simply use the format "snnn" where s is an optional sign, and nnn is the three-digit data value. In Assembly Language, you can specify "DAT snnn" for clarity.

## Slide 108: Assembly Language
Specific to a CPU
1 to 1 correspondence between assembly language instruction and binary (machine) language instruction
Mnemonics (short character sequence) represent instructions
Used when programmer needs precise control over hardware, e.g., device drivers

## Slide 109: Example - Add 2 Numbers
Assume data is stored in mailbox address 90
Let us write instructions (using Mnemonics)
  00 IN; input 1st Number
  01 STO 90; store data in memory location 90
  02 IN; input 2nd Number
  03 ADD 90; add 1st # to 2nd #
  04 OUT; output result
  05 COB; stop
  90 DAT 00; data
Input a #
Store the #
Input a #
Add
Output the
number

## Slide 110: Example - Add 2 Numbers (Using Machine code)
Mailbox | Code | Instruction Description
00 | 901 | ;input 1st Number
01 | 390 | ;store data in memory location 90
02 | 901 | ;input 2nd Number
03 | 190 | ;add 1st # to 2nd #
04 | 902 | ;output result
05 | 000 | ;stop
90 | 000 | ;data

## Slide 111: Program Control
Branching (executing an instruction out of sequence)
  Changes the address in the counter
Halt
 |  | Content | 
 |  | Op Code | Operand (address)
BR (Jump) |  | 6 | xx
BRZ (Branch on 0) |  | 7 | xx
BRP (Branch on +) |  | 8 | xx
COB (stop) |  | 0 | (ignore)

## Slide 112: Instruction Set
ADD | 1xx | ADD
SUB | 2xx | SUB
STA or STO | 3xx | STORE
LDA | 5xx | LOAD
BR or BRU or JMP | 6xx | JUMP
BRZ | 7xx | BRANC ON 0
BRP | 8xx | BRANCH ON +
IN or INP | 901 | INPUT
OUT or PRN | 902 | OUTPUT
NOP or NUL | 400 | No Operation
HLT or COB | 000 | HALT (coffee break)

## Slide 113: Example - Find Positive Difference of 2 Numbers
00 | IN | 901 | ;input 1st Number
01 | STO 10 | 310 | ;store data in memory location 10
02 | IN | 901 | ;input 2nd Number
03 | STO 11 | 311 | ;store data in memory location 11
04 | SUB 10 | 210 | ;subtract 1st # from the 2nd #
05 | BRP 08 | 808 | ;test
06 | LDA 10 | 510 | ;if negative, reverse order
07 | SUB 11 | 211 | ;subtract 2nd # from the 1st #
08 | OUT | 902 | ;print result and
09 | HLT | 000 | ;stop
10 | DAT 00 | 000 | ;used for data
11 | DAT 00 | 000 | ;used for data