## Slide 1: BLM5207 Computer Organization
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
http://www3.yildiz.edu.tr/~naydin
Addressing Modes and Formats

## Slide 2: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement (Indexed)
Stack
Notes: 2

## Slide 3: Immediate Addressing
Operand is part of instruction
Operand = address field
e.g. ADD 5
  Add 5 to contents of accumulator
  Here 5 is operand
No memory reference to fetch data
Fast
Limited range
Operand
Opcode
Instruction
Notes: 3

## Slide 4: Direct Addressing
Address field contains address of operand
Effective address (EA) = address field (A)
e.g. ADD A
  Add contents of cell A to accumulator
  Look in memory at address A for operand
Single memory reference to access data
No additional calculations to work out effective address
Limited address space
Notes: 5

## Slide 5: Direct Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Notes: 6

## Slide 6: Indirect Addressing (1)
Memory cell pointed to by address field contains the address of (pointer to) the operand
Large address space
2n where n = word length
May be nested, multilevel, cascaded
Multiple memory accesses to find operand
Hence slower
Notes: 7

## Slide 7: Indirect Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Pointer to operand
Notes: 9

## Slide 8: Register Addressing (1)
Operand is held in register named in address field
EA = R
Limited number of registers
Very small address field needed
  Shorter instructions
  Faster instruction fetch
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
  Requires good assembly programming or compiler writing
Notes: 10

## Slide 9: Register Addressing Diagram
Register Address R
Opcode
Instruction
Registers
Operand
Notes: 12

## Slide 10: Register Indirect Addressing
Operand is held in memory cell pointed to by contents of register R named in address field
EA = (R)
Large address space (2n)
One fewer memory access than indirect addressing
Notes: 13

## Slide 11: Register Indirect Addressing Diagram
Register Address R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
Notes: 14

## Slide 12: Displacement Addressing
EA = A + (R)
Address field hold two values
  A = base value
  R = register that holds displacement
  or vice versa
Notes: 15

## Slide 13: Displacement Addressing Diagram
Register R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
Address A
+
Notes: 16

## Slide 14: Relative Addressing
A version of displacement addressing
R = Program counter (PC)
EA = A + (PC)
i.e. get operand from A cells from current location pointed to by PC
Notes: 17

## Slide 15: Base-Register Addressing
A holds displacement
R holds pointer to base address
R may be explicit or implicit
e.g. segment registers in 80x86
Notes: 18

## Slide 16: Indexed Addressing
A = base
R = displacement
EA = A + R
Good for accessing arrays
  EA = A + R
  R++
Notes: 19

## Slide 17: Combinations
Postindex
EA = (A) + (R)
Preindex
EA = (A+(R))
Notes: 20

## Slide 18: Stack Addressing
Operand is (implicitly) on top of stack
e.g.
  ADD Pop top two items from stack and add
Notes: 21

## Slide 19: Summary of basic addressing modes

## Slide 20: Instruction Formats
Layout of bits in an instruction
Includes opcode
Includes (implicit or explicit) operand(s)
Usually more than one instruction format in an instruction set

## Slide 21: Instruction Length
Affected by and affects:
  Memory size
  Memory organization
  Bus structure
  CPU complexity
  CPU speed
Trade off between powerful instruction repertoire and saving space

## Slide 22: Allocation of Bits
Number of addressing modes
Number of operands
Register versus memory
Number of register sets
Address range
Address granularity