## Slide 1: BLM5207 Computer Organization
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
http://www3.yildiz.edu.tr/~naydin
Computer Arithmetic

## Slide 2: Arithmetic & Logic Unit
Does the calculations
Everything else in the computer is there to service this unit
Handles integers
May handle floating point (real) numbers
May be separate FPU (maths co-processor)
May be on chip separate FPU (486DX +)

## Slide 3: ALU Inputs and Outputs

## Slide 4: Integer Representation
Only have 0 & 1 to represent everything
Positive numbers stored in binary
  e.g. 41=00101001
No minus sign
No period
Sign-Magnitude
Two’s complement

## Slide 5: Sign-Magnitude
Left most bit is sign bit
0 means positive
1 means negative
+18 = 00010010
-18 = 10010010
Problems
  Need to consider both sign and magnitude in arithmetic
  Two representations of zero (+0 and -0)

## Slide 6: Two’s Complement
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101

## Slide 7: Characteristics of Twos Complement Representation and Arithmetic

## Slide 8: Benefits
One representation of zero
Arithmetic works easily (see later)
Negating is fairly easy
  3 = 00000011
  Boolean complement gives 11111100
  Add 1 to LSB 11111101

## Slide 9: Negation Special Case 1
0 = 00000000
Bitwise not 11111111
Add 1 to LSB +1
Result 1 00000000
Overflow is ignored, so:
- 0 = 0 

## Slide 10: Negation Special Case 2
-128 = 10000000
bitwise not 01111111
Add 1 to LSB +1
Result 10000000
So:
-(-128) = -128 X
Monitor MSB (sign bit)
It should change during negation

## Slide 11: Range of Numbers
8 bit 2s complement
  +127 = 01111111 = 27 -1
  -128 = 10000000 = -27
16 bit 2s complement
  +32767 = 011111111 11111111 = 215 - 1
  -32768 = 100000000 00000000 = -215

## Slide 12: Conversion Between Lengths
Positive number pack with leading zeros
+18 = 00010010
+18 = 00000000 00010010
Negative numbers pack with leading ones
-18 = 10010010
-18 = 11111111 10010010
i.e. pack with MSB (sign bit)

## Slide 13: Fixed-Point Representation
Number representation discussed so far also referred as fixed point.
  Because the radix point (binary point) is fixed and assumed to be to the right of the rightmost digit (least significant digit).

## Slide 14: Integer Arithmetic
Negation:
  In sign magnitude, simply invert the sign bit.
  In twos complement:
    Apply twos complement operation (take bitwise complement including sign bit, and add 1)

## Slide 15: Addition and Subtraction
Normal binary addition
Monitor sign bit for overflow
Take twos complement of subtrahend and add to minuend
  i.e. a - b = a + (-b)
So we only need addition and complement circuits

## Slide 16: Addition and Subtraction
Overflow rule
  If two numbers are added and they are both positive or both negative, then overflow occurs if and only if the result has the opposite sign
Subtraction rule
  To subtract one number(subrahend) from another (minuhend), take twos complement (negation) of the subtrahend and add it to the minuhend

## Slide 17: Addition of Numbers in Twos Complement Representation

## Slide 18: Subtraction of Numbers in Twos Complement Representation (M – S)

## Slide 19: Hardware for Addition and Subtraction

## Slide 20: Multiplication
Complex
Work out partial product for each digit
Take care with place value (column)
Add partial products

## Slide 21: Multiplication Example
1011 Multiplicand (11 dec)
x 1101 Multiplier (13 dec)
1011 Partial products
0000 Note: if multiplier bit is 1 copy
1011 multiplicand (place value)
1011 otherwise zero
10001111 Product (143 dec)
Note: need double length result

## Slide 22: Unsigned Binary Multiplication

## Slide 23: Execution of Example

## Slide 24: Flowchart for Unsigned Binary Multiplication

## Slide 25: Multiplying Negative Numbers
This does not work!
Solution 1
  Convert to positive if required
  Multiply as above
  If signs were different, negate answer
Solution 2
  Booth’s algorithm

## Slide 26: Booth’s Algorithm

## Slide 27: Example of Booth’s Algorithm

## Slide 28: Division
More complex than multiplication
Negative numbers are really bad!
Based on long division

## Slide 29: Division of Unsigned Binary Integers
001111
1011
00001101
10010011
1011
001110
1011
1011
100
Quotient
Dividend
Remainder
Partial
Remainders
Divisor

## Slide 30: Flowchart for Unsigned Binary Division

## Slide 31: Example

## Slide 32: Real Numbers
Numbers with fractions
Could be done in pure binary
  1001.1010 = 24 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
  Very limited
Moving?
  How do you show where it is?

## Slide 33
123 000 000 000 000
        1.23 X 1014
0.0000000000000123
        1.23 X 10-14

## Slide 34: Floating Point
+/- .significand x 2exponent
Misnomer
Point is actually fixed between sign bit and body of mantissa
Exponent indicates place value (point position)

## Slide 35: Floating Point Examples

## Slide 36: Signs for Floating Point
Mantissa is stored in 2s complement
Exponent is in excess or biased notation
  e.g. Excess (bias) 128 means
  8 bit exponent field
  Pure value range 0-255
  Subtract 128 to get correct value
  Range -128 to +127

## Slide 37: Normalization
FP numbers are usually normalized
i.e. exponent is adjusted so that leading bit (MSB) of mantissa is 1
Since it is always 1 there is no need to store it
(c.f. Scientific notation where numbers are normalized to give a single digit before the decimal point
e.g. 3.123 x 103)

## Slide 38: FP Ranges
For a 32 bit number
  8 bit exponent
  +/- 2256  1.5 x 1077
Accuracy
  The effect of changing lsb of mantissa
  23 bit mantissa 2-23  1.2 x 10-7
  About 6 decimal places

## Slide 39: Expressible Numbers

## Slide 40: Density of Floating Point Numbers

## Slide 41: IEEE 754
Standard for floating point storage
32 and 64 bit standards
8 and 11 bit exponent respectively
Extended formats (both mantissa and exponent) for intermediate results

## Slide 42: IEEE 754 Formats

## Slide 43: IEEE 754 Format Parameters

## Slide 44: Interpretation of IEEE 754 Floating-Point Numbers

## Slide 45: Floating-Point Numbers and Arithmetic Operations

## Slide 46: A floating-point operation may produce one of these conditions:
Exponent overflow:
  A positive exponent exceeds the maximum possible expo-nent value. In some systems, this may be designated as +∞ or —∞.
Exponent underflow:
  A negative exponent is less than the minimum possible exponent value (e.g., —200 is less than —127). This means that the number is too small to be represented, and it may be reported as 0.
Significand underflow:
  In the process of aligning significands, digits may flow off the right end of the significand. Some form of rounding is required.
Significand overflow:
  The addition of two significands of the same sign may result in a carry out of the most significant bit. This can be fixed by realignment.

## Slide 47: FP Arithmetic +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result

## Slide 48: FP Arithmetic +/- Phase 1
Zero check
Because addition and subtraction are identical except for a sign change, the process begins by changing the sign of the subtrahend if it is a subtract operation. Next, if either operand is 0, the other is reported as the result.

## Slide 49: FP Arithmetic +/- Phase 2
Significand alignment
Numbers needs to be manipulated so that the two exponents are equal.
  To see the need for aligning exponents, consider the following decimal addition:
  (123 x 100) + (456 x 10-2)
  Clearly, we cannot just add the significands. The digits must first be set into equivalent positions, that is, the 4 of the second number must be aligned with the 3 of the first. Under these conditions, the two exponents will be equal,which is the mathematical condition under which two numbers in this form can be added. Thus,
  (123 x 100) + (456 x 10-2) = (123 x 100) + (4.56 x 100) = 127.56x100

## Slide 50: FP Arithmetic +/- Phase 2
Alignment may be achieved by shifting either the smaller number to the right (increasing its exponent) or shifting the larger number to the left. Because either operation may result in the loss of digits, it is the smaller number that is shifted; any digits that are lost are therefore of relatively small significance. The alignment is achieved by repeatedly shifting the magnitude portion of the significand right 1 digit and incrementing the exponent until the two exponents are equal. (Note that if the implied base is 16, a shift of 1 digit is a shift of 4 bits.) If this process results in a 0 value for the significand, then the other number is reported as the result. Thus, if two numbers have exponents that differ significantly, the lesser number is lost.

## Slide 51: FP Arithmetic +/- Phase 3
Addition
The two significands are added together, taking into account their signs. Because the signs may differ, the result may be 0. There is also the possibility of significand overflow by 1 digit. If so, the significand of the result is shifted right and the exponent is incremented. An exponent overflow could occur as a result; this would be reported and the operation halted.

## Slide 52: FP Arithmetic +/- Phase 4
Normalization
Normalization consists of shifting significand digits left until the most significant digit (bit, or 4 bits for base-16 exponent) is nonzero. Each shift causes a decrement of the exponent and thus could cause an exponent underflow. Finally, the result must be rounded off and then reported. We defer a discussion of rounding until after a discussion of multiplication and division.

## Slide 53: FP Addition & Subtraction Flowchart

## Slide 54: FP Arithmetic x/
Check for zero
Add/subtract exponents
Multiply/divide significands (watch sign)
Normalize
Round
All intermediate results should be in double length storage

## Slide 55: Floating Point Multiplication

## Slide 56: Floating Point Division