## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2
Arithmetic for Computers

## Slide 3: Outline
Arithmetic & Logic Unit
Integer Representation
  Sign-Magnitude
  Two’s Complement
  Integer Arithmetic
    Addition and Subtraction
    Multiplication
    Booth’s Algorithm
    Division
Floating Point
  Floating Point Arithmetic
    Addition and Subtraction
    Multiplication and Division

## Slide 4: Arithmetic & Logic Unit
Does the calculations
Everything else in the computer is there to service this unit
Handles integers
May handle floating point (real) numbers
May be separate FPU (maths co-processor)
May be on chip separate FPU (486DX +)

## Slide 5: Arithmetic & Logic Unit
(Top) A 1-bit ALU that performs AND, OR, and addition on a and b or a' and b'
  includes a direct input that is connected to perform the set on less than operation
(Bottom) a 1-bit ALU for the most significant bit.
  has a direct output from the adder for the less than comparison called Set.

## Slide 6: Arithmetic & Logic Unit
A 32-bit ALU constructed from the 31 copies of the 1-bit ALU and one 1-bit ALU in the bottom of the figüre in previous slide.
The Less inputs are connected to 0 except for the least significant bit, which is connected to the Set output of the most significant bit.

## Slide 7: Arithmetic & Logic Unit
The final 32-bit ALU with a Zero detector

## Slide 8: Arithmetic & Logic Unit
The values of the three ALU control lines, Bnegate, and Operation, and the corresponding ALU operations
The symbol commonly used to represent
an ALU

## Slide 9: Integer Representation
Only have 0 & 1 to represent everything
Positive numbers stored in binary
  e.g. 41=00101001
No minus sign
No period
Sign-Magnitude
Two’s complement

## Slide 10: Sign-Magnitude
Left most bit is sign bit
0 means positive
1 means negative
+18 = 00010010
-18 = 10010010
Problems
  Need to consider both sign and magnitude in arithmetic
  Two representations of zero (+0 and -0)

## Slide 11: Two’s Complement
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
-1 = 11111111
-2 = 11111110
-3 = 11111101

## Slide 12: Characteristics of Twos Complement Representation and Arithmetic

## Slide 13: Benefits
One representation of zero
Arithmetic works easily
Negating is fairly easy
  3 = 00000011
  Boolean complement gives 11111100
  Add 1 to LSB 11111101

## Slide 14: Negation Special Case 1
0 = 00000000
Bitwise not 11111111
Add 1 to LSB +1
Result 1 00000000
Overflow is ignored, so:
- 0 = 0 

## Slide 15: Negation Special Case 2
-128 = 10000000
bitwise not 01111111
Add 1 to LSB +1
Result 10000000
So:
-(-128) = -128
Monitor MSB (sign bit)
It should change during negation

## Slide 16: Range of Numbers
8 bit 2s complement
  +127 = 01111111 = 27 -1
  -128 = 10000000 = -27
16 bit 2s complement
  +32767 = 011111111 11111111 = 215 - 1
  -32768 = 100000000 00000000 = -215

## Slide 17: Conversion Between Lengths
Positive number pack with leading zeros
+18 = 00010010
+18 = 00000000 00010010
Negative numbers pack with leading ones
-18 = 10010010
-18 = 11111111 10010010
i.e. pack with MSB (sign bit)

## Slide 18: Fixed-Point Representation
Number representation discussed so far also referred as fixed point.
  Because the radix point (binary point) is fixed and assumed to be to the right of the rightmost digit (least significant digit).

## Slide 19: Integer Arithmetic
Binary Addition
Carry in
Carry out
Notes: Binary addition, showing carries from right to left. The rightmost bit adds 1 to 0, resulting in the sum of this bit being 1 and the carry out from this bit being 0. Hence, the operation for the second digit to the right is 0 1 1 1 1. This generates a 0 for this sum bit and a carry out of 1. The third digit is the sum of 1 1 1 1 1, resulting in a carry out of 1 and a sum bit of 1. The fourth bit is 1 1 0 1 0, yielding a 1 sum and no carry.

## Slide 20: Integer Arithmetic
Negation:
  In sign magnitude
    simply invert the sign bit.
  In twos complement:
    apply twos complement operation
Normal binary addition
  Monitor sign bit for overflow
Subtraction
  Take twos complement of subtrahend and add to minuhend
    i.e. a - b = a + (-b)
So we only need addition and complement circuits

## Slide 21: Addition and Subtraction
Overflow rule
  If two numbers are added and they are both positive or both negative, then overflow occurs if and only if the result has the opposite sign

## Slide 22: Addition of Numbers in Twos Complement Representation

## Slide 23: Subtraction of Numbers in 2s Complement Representation (M – S)

## Slide 24: Hardware for Addition and Subtraction

## Slide 25: Multiplication
Complex
Work out partial product for each digit
Take care with place value (column)
Add partial products
Example:
1011 Multiplicand (11 dec)
x 1101 Multiplier (13 dec)
1011 Partial products
0000
1011
1011
10001111 Product (143 dec)
Note: need double length result

## Slide 26: Unsigned Binary Multiplication
Flowchart

## Slide 27: Unsigned Binary Multiplication
Block diagram of ALU circuitry

## Slide 28: Execution of Example

## Slide 29: Signed Binary Multiplication
This does not work!
Solution 1
  Convert to positive if required
  Multiply as above
  If signs were different, negate answer
Solution 2
  Booth’s algorithm

## Slide 30: Signed Binary Multiplication
Booth’s Multiplier

## Slide 31: Signed Binary Multiplication
Flowchart of Booth’s Multiplier

## Slide 32: Example of Booth’s Algorithm

## Slide 33: Division of Unsigned Binary Integers
More complex than multiplication
  Negative numbers are really bad!
Based on long division

## Slide 34: Unsigned Binary Division
Flowchart

## Slide 35: Unsigned Binary Division
Example using division of the unsigned integer 7 by the unsigned integer 3

## Slide 36: Unsigned Binary Division
Schematic diagram of ALU circuitry

## Slide 37: Signed Binary Division
With signed division, we negate the quotient if the signs of the divisor and dividend disagree.
The remainder and the divident must have the same signs.
The governing equation is as follows:
  Remainder = Divident - (Quotient · Divisor) ,
  and the following four cases apply:

## Slide 38: Signed Binary Division
Flowchart

## Slide 39: Signed Binary Division
Example using division of +7 by the integer +3 and -3

## Slide 40: Signed Binary Division
Example using division of -7 by the integer +3 and -3

## Slide 41: Division in MIPS
MIPS supports multiplication and division using existing hardware, primarily the ALU and shifter.
  MIPS needs one extra hardware component –
    a 64-bit register able to support sll and sra instructions.
The upper (high) 32 bits of the register contains the remainder resulting from division.
  This is moved into a register in the MIPS register stack (e.g., $t0) by the mfhi command.
The lower 32 bits of the 64-bit register contains the quotient resulting from division.
  This is moved into a register in the MIPS register stack by the mflo command.
In MIPS assembly language code, signed division is supported by the div instruction and unsigned division, by the divu instruction.
MIPS hardware does not check for division by zero.
  Thus, divide-by-zero exception must be detected and handled in system software.
A similar comment holds for overflow or underflow resulting from division.

## Slide 42: Division in MIPS
MIPS ALU that supports integer arithmetic operations (+,-,x,/)

## Slide 43: Real Numbers
Numbers with fractions
Could be done in pure binary
  1001.1010 = 24 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
  Very limited
Moving?
  How do you show where it is?

## Slide 44: Real Numbers (exponantials)
123 000 000 000 000
        1.23 X 1014
0.0000000000000123
        1.23 X 10-14

## Slide 45: Floating Point
+/- .significand x 2exponent
Point is actually fixed between sign bit and body of mantissa
Exponent indicates place value (point position)

## Slide 46: Floating Point Examples

## Slide 47: Signs for Floating Point
Mantissa is stored in 2s complement
Exponent is in excess or biased notation
  e.g. Excess (bias) 128 means
  8 bit exponent field
  Pure value range 0-255
  Subtract 128 to get correct value
  Range -128 to +127

## Slide 48: Normalization
FP numbers are usually normalized
i.e. exponent is adjusted so that leading bit (MSB) of mantissa is 1
Since it is always 1 there is no need to store it
(c.f. Scientific notation where numbers are normalized to give a single digit before the decimal point
e.g. 3.123 x 103)

## Slide 49: FP Ranges
For a 32 bit number
  8 bit exponent
  +/- 2256  1.5 x 1077
Accuracy
  The effect of changing lsb of mantissa
  23 bit mantissa 2-23  1.2 x 10-7
  About 6 decimal places

## Slide 50: Expressible Numbers
2s complement integer (32 bits)
Floating point

## Slide 51: IEEE 754
Standard for floating point storage
32 bit standard (8 bit biased exponent)
  Single format
64 bit standard (11 bit biased exponent)
  Double format

## Slide 52: FP example
FPnumber = (-1)S · (1 + Significand) · 2(Exponent - Bias)
Example:

## Slide 53: IEEE 754 Format Parameters

## Slide 54: Interpretation of IEEE 754 Floating-Point Numbers

## Slide 55: Floating-Point Numbers and Arithmetic Operations

## Slide 56: A floating-point operation may produce one of these conditions:
Exponent overflow:
  A positive exponent exceeds the maximum possible expo-nent value.
  In some systems, this may be designated as +∞ or -∞.
Exponent underflow:
  A negative exponent is less than the minimum possible exponent value (e.g., -200 is less than -127).
  This means that the number is too small to be represented, and it may be reported as 0.
Significand underflow:
  In the process of aligning significands, digits may flow off the right end of the significand.
  Some form of rounding is required.
Significand overflow:
  The addition of two significands of the same sign may result in a carry out of the most significant bit.
  This can be fixed by realignment.

## Slide 57: FP Arithmetic +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result

## Slide 58: FP Arithmetic +/- Phase 1
Zero check
  Because addition and subtraction are identical except for a sign change, the process begins by changing the sign of the subtrahend if it is a subtract operation.
  Next, if either operand is 0, the other is reported as the result.

## Slide 59: FP Arithmetic +/- Phase 2
Significand alignment
  Numbers needs to be manipulated so that the two exponents are equal.
  To see the need for aligning exponents, consider the following decimal addition:
    (123 x 100) + (456 x 10-2)
  Clearly, we cannot just add the significands.
    The digits must first be set into equivalent positions,
      that is, the 4 of the second number must be aligned with the 3 of the first.
  Under these conditions, the two exponents will be equal,which is the mathematical condition under which two numbers in this form can be added. Thus,
    (123 x 100) + (456 x 10-2) = (123 x 100) + (4.56 x 100) = 127.56x100

## Slide 60: FP Arithmetic +/- Phase 2
Alignment may be achieved by shifting either the smaller number to the right (increasing its exponent) or shifting the larger number to the left.
  Because either operation may result in the loss of digits, it is the smaller number that is shifted; any digits that are lost are therefore of relatively small significance.
The alignment is achieved by repeatedly shifting the magnitude portion of the significand right 1 digit and incrementing the exponent until the two exponents are equal.
  Note that if the implied base is 16, a shift of 1 digit is a shift of 4 bits.
    If this process results in a 0 value for the significand, then the other number is reported as the result.
  Thus, if two numbers have exponents that differ significantly, the lesser number is lost.

## Slide 61: FP Arithmetic +/- Phase 3
Addition
  The two significands are added together, taking into account their signs.
    Because the signs may differ, the result may be 0.
  There is also the possibility of significand overflow by 1 digit.
  If so, the significand of the result is shifted right and the exponent is incremented.
  An exponent overflow could occur as a result;
    this would be reported and the operation halted.

## Slide 62: FP Arithmetic +/- Phase 4
Normalization
  Normalization consists of shifting significand digits left until the most significant digit (bit, or 4 bits for base-16 exponent) is nonzero.
  Each shift causes a decrement of the exponent and thus could cause an exponent underflow.
  Finally, the result must be rounded off and then reported.

## Slide 63: FP Addition & Subtraction Flowchart

## Slide 64: FP Arithmetic x/
Check for zero
Add/subtract exponents
Multiply/divide significands (watch sign)
Normalize
Round
All intermediate results should be in double length storage

## Slide 65: Floating Point Multiplication

## Slide 66: Floating Point Division