## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2
Performance Metrics

## Slide 3: Objectives
How can we meaningfully measure and compare computer performance?
Understand why program performance varies
  Understand how applications and the compiler impact performance
  Understand how CPU impacts performance
  What trade-offs are involved in designing a CPU?
Purchasing perspective vs design perspective

## Slide 4: Outline
Latency, delay, time
Throughput
Cost
Power
Energy
Reliability

## Slide 5: Basic Performance Metrics
Latency, delay, time
  Lower is better
    Complete a task as soon as possible
  Measured in sec, s, ns
Throughput (bandwith)
  Higher is better
    Complete as many tasks per time as possible
  Measured in bytes/sec, instructions/sec
Cost
  Lower is better
    Complete tasks for as little money as possible
  Measured in $, TL, etc.

## Slide 6: Basic Performance Metrics
Power
  Lower is better
    Complete tasks while dissipating as few joules/sec as possible
Energy
  Lower is better
    Complete tasks using as few joules as possible
  Measured in Joules, Joules/instruction
Reliability
  Higher is better
    Complete tasks with low probability of failure
  Measured in Mean time to failure (MTTF)
    MTTF: the average time until a failure occurs

## Slide 7: Latency vs Throughput
Madrid to Istanbul is about 3600 km
Time:
  Aircraft 1 is faster than Aircraft 2
    900/750 = 1.2 times or 20% faster
Throughput:
  Aircraft 2 has a higher throughput
    (750*600)/(900*400) = 1.25 times the throughput or 25% more throughput

## Slide 8: Response Time vs Throughput
Response time (latency)
  the time between the start and the completion of a task
    Important to individual users ( passengers)
Throughput (bandwidth)
  the total amount of work done in a given time
  Important to data center managers (airline)
Different performance metrics are required
  to benchmark embedded and desktop computers,
    which are more focused on response time,
  to benchmark servers,
    which are more focused on throughput

## Slide 9: Defining (Speed) Performance
Minimizing the execution time maximizes the performance:
  performance of X = 1 / execution_time of X
If X is n times faster than Y,
  then the performance ratio n is
  performance of X execution_time of Y
  --------------------- = -------------------------- = n
  performance of Y execution_time of X

## Slide 10: A Relative Performance Example
If computer A runs a program in 10 seconds and computer B runs the same program in 15 seconds,
  Which computer is faster?
  How much faster?
We know that A is n times faster than B if
  performance of A execution_time of B
  --------------------- = -------------------------- = n
  performance of B execution_time of A
The performance ratio n is 15/10 =1.5
So A is 1.5 times (50%) faster than B

## Slide 11: Ratios of Measure: Side Note
For bigger-is-better metrics,
  improved means increase
    Vnew = 2.5 * Vold
      A metric increased by 2.5 times (sometimes written 2.5x)
      A metric increased by 150% (x% increase == 0.01*x+1 times increase)
For smaller-is-better metrics,
  improved means decrease
    e.g., Latency improved by 2x, means latency decreased by 2x (i.e., dropped by 50%)
    e.g., Battery life worsened by 50%, means battery life decrease by 50%.

## Slide 12: Examples
Bigger-is-better examples
  Bandwidth per dollar (e.g., in networking (GB/s)/$)
  BW/Watt (e.g., in memory systems (GB/s)/W)
  Work/Joule (e.g., instructions/joule)
  In general
    Multiply by big-is-better metrics, divide by smaller-is-better metrics
Smaller-is-better examples
  Cycles/Instruction (i.e., Time per work)
  Latency * Energy -- Energy Delay Product
  In general:
    Multiply by smaller-is-better metrics, divide by bigger-is-better metrics

## Slide 13: Clock Cycle and Clock Rate
A clock cycle is a single electronic pulse of a CPU
  To synchronize different parts of the circuit
  To determine when events take place in the hardware
  Processor runs at a constant clock rate
  Clock cycle or tick or cycle = Discrete time interval
Clock rate (frequency)
  Number of clock cycles per second in hertz
    1 nsec (10-9) clock cycle => 1 GHz (109) clock rate
    0.5 nsec clock cycle => 2 GHz clock rate

## Slide 14: CPU Time (Execution Time)
A program takes 15x1010 cycles to execute on a computer with a clock cycle time of 500 picosec.
  How many seconds does it take for the program to execute?
Clock Cycles:
  How many cycles it takes for a program to execute!
CPU Time (Execution time):
  How many seconds it takes for a program to execute!

## Slide 15: CPU Time Example
Computer A has a 2GHz clock rate, executes a program in 10 sec (CPU time)
Designing Computer B by aiming for 6 sec CPU time
  With a faster clock, but this causes 1.2 × clock cycles
What is Computer B’s clock rate?

## Slide 16: Clock Cycles per Instruction (CPI)
Not all instructions take the same amount of time to execute
  There is a mix of instructions in a program
    E.g. Load, Store, ALU
  Need to know the frequency of the instructions
    Because instructions take different number of cycles to execute

## Slide 17: Instruction Mix and CPI
All these values depend on the particular hardware implementation, not the ISA
Values are for Intel’s Nehalem processor
Clock cycles per instruction (CPI)
  the average number of clock cycles each instruction takes to execute
  CPI is not the cycles required to execute a single instruction
  A way to compare two different implementations of the same Instruction Set Architectures (ISA)

## Slide 18: Comparing Computers
Computers A and B implement the same ISA.
  Computer A has a clock cycle time of 250 ps and an effective CPI of 2.0 for some program C
  Computer B has a clock cycle time of 500 ps and an effective CPI of 1.2 for the same program.
Which computer is faster and by how much?

## Slide 19: Comparing Computers
Clock Cycles = Instruction Count×Cycles per Instruction
CPU Time = Instruction Count×CPI×Clock Cycle Time
Each computer executes the same number of instructions, I, so
  CPU timeA = I × 2.0 × 250 ps = 500 × I ps
  CPU timeB = I × 1.2 × 500 ps = 600 × I ps
Clearly, A is faster than B by the ratio of execution times
performanceA execution_timeB 600 x I ps
------------------- = --------------------- = ---------------- = 1.2
performanceB execution_timeA 500 x I ps

## Slide 20: CPU Performance
Different programs do different amounts of work
  e.g., Playing a DVD vs writing a word document
The same program may do different amounts of work depending on its input
  Compiling a 1000-line program vs compiling a 100-line program
The same program may require a different number of instructions on different ISAs
  MIPS vs. x86
To make a meaningful comparison between two computer systems, they must be doing the same work.
  They may execute a different number of instructions (e.g., because they use different ISAs or a different compilers)
  But the task they accomplish should be exactly the same.

## Slide 21: CPU Performance
CPU time = Instruction_count × CPI / Clock Rate
Clock Rate = 1 / Clock Cycle

## Slide 22: Compiler Benefits
Comparing performance for bubble sort
  To sort 100,000 words with the array initialized to random values
    The unoptimized code has the best CPI, the O1 version has the lowest instruction count, but the O3 version is the fastest.
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm

## Slide 23: Instruction Count
Note that instruction count is dynamic
  its not the number of lines in the code, or
  number of lines in an assembly code that compiler generates
Static instruction count refers to the program as it was compiled
Dynamic instruction count refers to the program at runtime
Dynamic instruction count is more accurate
  For example, you have a loop in your program then some instructions get executed more than once or
  In the presence of branches, some instructions may not be executed at all.
Average CPI:
(5×1 + 1×44 + 1×21)/66= 1.06

## Slide 24: Instruction Mix
Measure MIPS instruction executions in benchmark programs (e.g. SPEC)
  Consider making the common case fast
  Consider compromises

## Slide 25: Dynamic Frequency
Most multi-core architectures nowadays support dynamic voltage and frequency scaling (DVFS) to adapt their speed to the system’s load and save energy.
  Enabled by the request from the Operating System
A core can exceed the its manufactured operation frequency
  Intel’s Turbo Boost and AMD Turbo CORE
Increased clock rate is limited by the power, current and thermal limits
  This is not similar to hearth rate increase
  CPU runs at a higher rate for awhile, it is discrete