## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2
External Memory

## Slide 3: Outline
Types of External Memory
  Magnetic Disk
    Magnetic Read and Write Mechanisms
    Data Organization and Formatting
    Physical Characteristics
    Disk Performance Parameters
  RAID
  Solid State Drives
    Flash Memory
    SSD Compared to HDD
    SSD Organization
  Optical Memory
    Compact Disk
    Digital Versatile Disk
    High-Definition Optical Disks
  Magnetic Tape

## Slide 4: Magnetic Disk
Disk substrate coated with magnetizable material (iron oxide…rust)
Substrate used to be aluminium
Now glass
  Improved surface uniformity
    Increases reliability
  Reduction in surface defects
    Reduced read/write errors
  Lower flight heights
  Better stiffness to reduce disk dynamics
  Better shock/damage resistance

## Slide 5: Write and Read Mechanisms
During read/write, head is stationary, platter rotates
Write (inductive)
  Current through coil produces magnetic field
  Pulses sent to head
  Magnetic pattern recorded on surface below
Read (magneto resistive) (MR)
  Separate read head, close to write head
  Partially shielded magneto resistive (MR) sensor
  Electrical resistance depends on direction of magnetic field
  High frequency operation
    Higher storage density and speed

## Slide 6: Data Organization and Formatting
Concentric rings or tracks
  Gaps between tracks
  Reduce gap to increase capacity
  Same number of bits per track (variable packing density)
  Constant angular velocity
Tracks divided into sectors
Minimum block size is one sector
May have more than one sector per block

## Slide 7: Disk Velocity
Bit near centre of rotating disk passes fixed point slower than bit on outside of disk
Increase spacing between bits in different tracks
Rotate disk at constant angular velocity (CAV)
  Gives pie shaped sectors and concentric tracks
  Individual tracks and sectors addressable
  Move head to given track and wait for given sector
  Waste of space on outer tracks
    Lower data density
Can use zones to increase capacity
  Each zone has fixed bits per track
  More complex circuitry

## Slide 8: Disk Layout Methods Diagram

## Slide 9: Finding Sectors
Some means is needed to locate sector positions within a track.
  There must be some starting point on the track and a way of identifying the start and end of each sector.
These requirements are handled by means of control data recorded on the disk.
  Thus, the disk is formatted with some extra data used only by the disk drive and not accessible to the user.

## Slide 10: Winchester Disk Format-Seagate ST506
An example of disk formatting:
  Each track contains 30 fixed-length sectors of 600 bytes each.
  Each sector holds 512 bytes of data plus control information useful to the disk controller.
  The ID field is a unique identifier or address used to locate a particular sector.
  The SYNCH byte is a special bit pattern that delimits the beginning of the field.
  The track number identifies a track on a surface.
  The head number identifies a head, because this disk has multiple surfaces.
  The ID and data fields each contain an error detecting code.

## Slide 11: Characteristics
Fixed (rare) or movable head
Removable or fixed
Single or double (usually) sided
Single or multiple platter
Head mechanism
  Contact (Floppy)
  Fixed gap
  Flying (Winchester)

## Slide 12: Fixed/Movable Head Disk
Fixed head
  One read write head per track
  Heads mounted on fixed ridged arm
Movable head
  One read write head per side
  Mounted on a movable arm

## Slide 13: Removable or Not
Removable disk
  Can be removed from drive and replaced with another disk
  Provides unlimited storage capacity
  Easy data transfer between systems
Nonremovable disk
  Permanently mounted in the drive

## Slide 14: Multiple Platter
One head per side
Heads are joined and aligned
Aligned tracks on each platter form cylinders
Data is striped by cylinder
  reduces head movement
  Increases speed (transfer rate)

## Slide 15: Multiple Platters

## Slide 16: Tracks and Cylinders

## Slide 17: Floppy Disk
8”, 5.25”, 3.5”
Small capacity
  Up to 1.44Mbyte (2.88M never popular)
Slow
Universal
Cheap
Obsolete?

## Slide 18: Winchester Hard Disk (1)
Developed by IBM in Winchester (USA)
Sealed unit
One or more platters (disks)
Heads fly on boundary layer of air as disk spins
Very small head to disk gap
Getting more robust
Universal
Cheap
Fastest external storage!
Getting larger all the time
  Terabyte now easily available

## Slide 19: Typical Hard Disk Drive Parameters
Parameters for typical contemporary high-performance disks

## Slide 20: Timing of Disk I/O Transfer
The actual details of disk I/O operation depend on the computer system, the operating system, and the nature of the I/O channel and disk controller hardware.
A general timing diagram of disk I/O transfer:

## Slide 21: Disk Performance Parameters-Speed
Seek time
  Moving head to correct track
(Rotational) latency
  Waiting for data to rotate under head
Transfer time
  Depends on the rotation speed of the disk
    T: transfer time,
    b: number of bytes to be transferred,
    N: number of bytes on track,
    r: rotation speed, in revolution per sconds
Access time = Seek + Latency
Ts: average seek time
  Transfer rate

## Slide 22: RAID
Redundant Array of Independent Disks
Redundant Array of Inexpensive Disks
6 levels in common use
Not a hierarchy
Set of physical disks viewed as single logical drive by O/S
Data distributed across physical drives
Can use redundant capacity to store parity information

## Slide 23: RAID 0
No redundancy
Data striped across all disks
Round Robin striping
Increase speed
  Multiple data requests probably not on same disk
  Disks seek in parallel
  A set of data is likely to be striped across multiple disks

## Slide 24: RAID 1
Mirrored Disks
Data is striped across disks
2 copies of each stripe on separate disks
Read from either
Write to both
Recovery is simple
  Swap faulty disk & re-mirror
  No down time
Expensive

## Slide 25: RAID 2
Disks are synchronized
Very small stripes
  Often single byte/word
Error correction calculated across corresponding bits on disks
Multiple parity disks store Hamming code error correction in corresponding positions
Lots of redundancy
  Expensive
  Not used

## Slide 26: RAID 3
Similar to RAID 2
Only one redundant disk, no matter how large the array
Simple parity bit for each set of corresponding bits
Data on failed drive can be reconstructed from surviving data and parity info
Very high transfer rates

## Slide 27: Example: Data reconstruction in RAID3
Consider an array of five drives (X0,X1,X2,X3 contain data, X4 is parity disk)
Parity of ith bit is calculated as:
X4(i)=X3(i)X2(i)X1(i)X0(i)
Suppose that drive X1 has failed. The contents of X1 can be regenerated as:
X1(i)=X4(i)X3(i)X2(i)X0(i)

## Slide 28: RAID 4
Each disk operates independently
Good for high I/O request rate
Large stripes
Bit by bit parity calculated across stripes on each disk
Parity stored on parity disk

## Slide 29: RAID 5
Like RAID 4
Parity striped across all disks
Round robin allocation for parity stripe
Avoids RAID 4 bottleneck at parity disk
Commonly used in network servers

## Slide 30: RAID 6
Two parity calculations
Stored in separate blocks on different disks
User requirement of N disks needs N+2
High data availability
  Three disks need to fail for data loss
  Significant write penalty

## Slide 31: RAID 0, 1, 2

## Slide 32: RAID 3 & 4

## Slide 33: RAID 5 & 6

## Slide 34: RAID Levels

## Slide 35: Data Mapping For RAID 0

## Slide 36: RAID Comparison

## Slide 37: RAID Comparison

## Slide 38: Solid State Drives (SSD)
A memory device made with solid state components that can be used as a replacement to a hard disk drive.
In recent years, it is used to complement or even replace hard disk drives (HDDs),
  both as internal and external secondary memory
SSDs now on the market and coming on line use a type of semiconductor memory referred to as flash memory

## Slide 39: Flash Memory
a type of semiconductor memory that has been around for a number of years
is used in many consumer electronic products,
  smart phones, GPS devices, MP3 players, digital cameras, and USB devices.
In recent years, the cost and performance of flash memory has evolved to the point where it is feasible to use flash memory drives to replace HDDs.
Next slide illustrates the basic operation of a flash memory

## Slide 40: Flash Memory
Transistor structure
  A small voltage applied to the gate can be used to control the flow of a large current between the source and the drain.
Flash memory cell in one state
  A second gate, called a floating gate because it is insulated by a thin oxide layer, is added to the transistor.
  Initially, the floating gate does not interfere with the operation of the transistor.
  In this state, the cell is deemed to represent binary 1.
Flash memory cell in zero state
  Applying a large voltage across the oxide layer causes electrons to tunnel through it and become trapped on the floating gate, where they remain even if the power is disconnected .
  In this state, the cell is deemed to represent binary 0.

## Slide 41: Flash Memory
Two distinctive types:
  NOR flash memory
    the basic unit of access is a bit,
    the logical organization resembles a NOR logic device
    provides high-speed random access
    can read and write data to specific locations,
    can reference and retrieve a single byte
    used to store cell phone operating system code and on Windows computers for the BIOS program that runs at startup
  NAND flash memory
    the basic unit is 16 or 32 bits,
    the logical organization resembles NAND devices
    reads and writes in small blocks
    used in USB flash drives, memory cards (in digital cameras, MP3 players, etc.), and in SSDs
    provides higher bit density than NOR and greater write speed
    does not provide a random-access external address bus so
    the data must be read on a blockwise basis (also known as page access), where each block holds hundreds to thousands of bits

## Slide 42: SSD Compared to HDD
SSDs have the following advantages over HDDs:
  High-performance input/output operations per second (IOPS):
    Significantly increases performance I/O subsystems.
  Durability:
    Less susceptible to physical shock and vibration.
  Longer lifespan:
    SSDs are not susceptible to mechanical wear.
  Lower power consumption:
    SSDs use as little as 2.1 watts of power per drive,
      considerably less than comparable-size HDDs.
  Quieter and cooler running capabilities:
    Less floor space required, lower energy costs, and a greener enterprise.
  Lower access times and latency rates:
    Over 10 times faster than the spinning disks in an HDD.

## Slide 43: SSD Compared to HDD
Comparison of Solid State Drives and Disk Drives (as of around 2013)

## Slide 44: SSD Organization
On the host system, operating system invokes file system software to access data on the disk.
The file system, in turn, invokes I/O driver software.
The I/O driver software provides host access to the particular SSD product.
If the device is an internal hard drive, a common interface is PCIe.
For external devices, one common interface is USB.
In addition to the interface to the host system, the SSD contains the following components:
  Controller:
    Provides SSD device level interfacing and firmware execution.
  Addressing:
    Logic that performs the selection function across the flash memory components.
  Data buffer/cache:
    High speed RAM memory components used for speed matching and to increased data throughput.
  Error correction:
    Logic for error detection and correction.
  Flash memory components:
    Individual NAND flash chips.

## Slide 45: Optical Storage
CD
  Compact Disk
CD-ROM
  Compact Disk Read-Only Memory
CD-R
  CD Recordable
CD-RW
  CD Rewritable
DVD
  Digital Versatile Disk
DVD-R
  DVD Recordable
DVD-RW
  DVD Rewritable

## Slide 46: Optical Storage CD-ROM
Originally for audio
650Mbytes giving over 70 minutes audio
Polycarbonate coated with highly reflective coat, usually aluminium
Data stored as pits
Read by reflecting laser
Constant packing density
Constant linear velocity

## Slide 47: CD Operation

## Slide 48: CD-ROM Drive Speeds
Audio is single speed
  Constant linier velocity
  1.2 ms-1
  Track (spiral) is 5.27km long
  Gives 4391 seconds = 73.2 minutes
Other speeds are quoted as multiples
e.g. 24x
Quoted figure is maximum drive can achieve

## Slide 49: CD-ROM Format
Sync: Identifies the beginning of a block. Consists of a byte of all 0s, 10 bytes of all 1s, and a byte of all 0s
Header: Contains the block address and the mode byte
  Mode 0=blank data field
  Mode 1=2048 byte data+error correction
  Mode 2=2336 byte data
Data: User data
Auxiliary: Additional user data in mode 2. In mode 1, this is a 288-byte error correcting code.

## Slide 50: Random Access on CD-ROM
Difficult
Move head to rough position
Set correct speed
Read address
Adjust to required location

## Slide 51: CD-ROM for & against
Large capacity (?)
Easy to mass produce
Removable
Robust
Expensive for small runs
Slow
Read only

## Slide 52: Other Optical Storage
CD-Recordable (CD-R)
  WORM
  Now affordable
  Compatible with CD-ROM drives
CD-RW
  Erasable
  Getting cheaper
  Mostly CD-ROM drive compatible
  Phase change
    Material has two different reflectivities in different phase states

## Slide 53: DVD
Digital Video Disk
  Used to indicate a player for movies
    Only plays video disks
Digital Versatile Disk
  Used to indicate a computer drive
    Will read computer disks and play video disks

## Slide 54: DVD - technology
Multi-layer
Very high capacity (4.7G per layer)
Full length movie on single disk
  Using MPEG compression
Finally standardized
Movies carry regional coding
Players only play correct region films

## Slide 55: DVD – Writable
Loads of trouble with standards
First generation DVD drives may not read first generation DVD-W disks
First generation DVD drives may not read CD-RW disks

## Slide 56: CD and DVD

## Slide 57: Magnetic Tape
Serial access
Slow
Very cheap
Backup and archive
Capacity: a couple of 100 GB

## Slide 58: Typical Magnetic Tape Features

## Slide 59: Internet Resources
Optical Storage Technology Association
  Good source of information about optical storage technology and vendors
  Extensive list of relevant links
DLTtape
  Good collection of technical information and links to vendors
Search on RAID