## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2: Computer Architecture
CPU Structure and Function

## Slide 3: Outline
CPU Structure
  Registers
  Instruction Cycle
  Data Flow
  Instruction Pipelining
  Dealing with conditional Branches

## Slide 4: CPU Structure
A CPU is responsible for...
  fetching instructions
  interpreting instructions
  fetching data
  processing data
  writing data
  CPU With Systems Bus
CPU Internal Structure
Notes: 22

## Slide 5: Registers
Top level of memory hierarchy
Temporary storage
User-visible registers
  Enable the machine- or assembly language programmer to minimize main memory references by optimizing use of registers
Control and status registers
  Used by the control unit to control the operation of the processor and by priviliged, operating system programs to control the execution of programs
Notes: 23

## Slide 6: Registers
User Visible Registers
  General Purpose registers
  Data registers
  Address registers
  Condition Codes (flags)
Control & Status Registers
  Program Counter (PC)
    Contains the address of an instruction to be fetched
  Instruction Decoding Register (IR)
    Contains the instruction most recently fetched
  Memory Address Register (MAR)
    Contains the addres of location in memory
  Memory Buffer Register (MBR)
    Contains a word or data to be written to memory or the word most recently read
Notes: 24

## Slide 7: Program Status Word
A set of bits containing status information
Includes Condition Codes (flags)
  Sign
    sign of last result
  Zero
    set when the result is 0
  Carry
    set if an operation resulted in a carry (addition) into or borrow (subtraction) out of a high order bit
  Equal
    set if a logical compare result is equality
  Overflow
    used to indicate arithmetic overflow
  Interrupt enable/disable
    used to enable or disable interrupts
  Supervisor
    Indicates whether the processor is executing in superviser mode or user mode.
    Certain privileged instructions can be executed only in supervisor mode, and certain areas of memory can be accessed only in supervisor mode
Notes: 31

## Slide 8: Example Register Organizations

## Slide 9: Instruction Cycle
Instruction Cycle
  Fetch
  Execute
  Interrupt
Indirect Cycle
  May require memory access to fetch operands
  Indirect addressing requires more memory accesses
  Can be thought of as additional instruction subcycle
Notes: 35

## Slide 10: Instruction Cycle State Diagram

## Slide 11: Data Flow (Instruction Fetch)
Depends on CPU design
In general following events take place in an instruction cycle:
Fetch
  PC contains address of next instruction
  Address moved to MAR
  Address placed on address bus
  Control unit requests memory read
  Result placed on data bus, copied to MBR, then to IR
  Meanwhile PC incremented by 1

## Slide 12: Data Flow (Data Fetch)
IR is examined
If indirect addressing, indirect cycle is performed
  Right most N bits of MBR transferred to MAR
  Control unit requests memory read
  Result (address of operand) moved to MBR

## Slide 13: Data Flow (Execute)
May take many forms
Depends on instruction being executed
May include
  Memory read/write
  Input/Output
  Register transfers
  ALU operations

## Slide 14: Data Flow (Interrupt)
Current PC saved to allow resumption after interrupt
Contents of PC copied to MBR
Special memory location (e.g. stack pointer) loaded to MAR
MBR written to memory
PC loaded with address of interrupt handling routine
Next instruction (first of interrupt handler) can be fetched

## Slide 15: Some strategies to increase the computer performance
Faster circuitry
Multiple registers
Cache memory
Parallel processing
Pipelining
Etc...
....

## Slide 16: Instruction Pipelining-
Similar to assembly line in a manifacturing plant
Remember that an instruction cycle has a number of stages
Here, instruction cycle can be divided into up to 10 tasks

## Slide 17: Prefetch-Improved Performance
Fetch accessing main memory
Execution usually does not access main memory
Can fetch next instruction during execution of current instruction
Called instruction prefetch or fetch overlap
  But performance is not doubled:
    Fetch usually shorter than execution
    Prefetch more than one instruction?
    Any jump or branch means that prefetched instructions are not the required instructions
Add more stages to improve performance
Notes: 36

## Slide 18: Pipelining
Consider the following decompositions of the instruction processing:
Fetch instruction (FI)
  Read the next expected instruction into a buffer
Decode instruction (DI)
  Determine the opcode and the operand specifiers
Calculate operands (CO)
  Calculate the effective address of each source operand
Fetch operands (FO)
  Fetch each operand from memory
Execute instructions (EI)
  Perform the indicated operation
Write operand (WO)
  Store the result in memory
Overlap these operations (6 stage pipeline)
Notes: 38

## Slide 19: Timing Diagram for Instruction Pipeline Operation
Notes: 39

## Slide 20: The Effect of a Conditional Branch on Instruction Pipeline Operation
Notes: 40

## Slide 21: Six Stage Instruction Pipeline

## Slide 22: Speedup Factors with Instruction Pipelining
Cycle time of an instruction
pipeline:
i = Time delay of the circuitry in the ith stage
m = Maximum stage delay
k = Number of stages
d = Time delay of a latch (equivalent to a clock pulse)
Total time for a pipeline:

## Slide 23: Dealing with conditional Branches
Multiple Streams
Prefetch Branch Target
Loop buffer
Branch prediction
Delayed branching
Notes: 41

## Slide 24: Multiple Streams
Have two pipelines
Prefetch each branch into a separate pipeline
Use appropriate pipeline
Leads to bus & register contention
Multiple branches lead to further pipelines being needed
Notes: 42

## Slide 25: Prefetch Branch Target
Target of branch is prefetched in addition to instructions following branch
Keep target until branch is executed
Used by IBM 360/91
Notes: 43

## Slide 26: Loop Buffer
Very fast memory
Maintained by fetch stage of pipeline
Check buffer before fetching from memory
Very good for small loops or jumps
Used by CRAY-1
Notes: 44

## Slide 27: Branch Prediction (1)
Predict never taken
  Assume that jump will not happen
  Always fetch next instruction
  68020 & VAX 11/780
  VAX will not prefetch after branch if a page fault would result (O/S v CPU design)
Predict always taken
  Assume that jump will happen
  Always fetch target instruction
Notes: 45

## Slide 28: Branch Prediction (2)
Predict by Opcode
  Some instructions are more likely to result in a jump than others
  Can get up to 75% success
Taken/Not taken switch
  Based on previous history
  Good for loops
Delayed Branch
  Do not take jump until you have to
  Rearrange instructions
Notes: 46

## Slide 29: Branch Prediction
Flowchart
State diagram

## Slide 30: Dealing With Branches

## Slide 31: Intel 80486 Pipelining (5 stage)
Fetch
  From cache or external memory
  Put in one of two 16-byte prefetch buffers
  Fill buffer with new data as soon as old data consumed
  Average 5 instructions fetched per load
  Independent of other stages to keep buffers full
Decode stage 1 (D1)
  Opcode & address-mode info
  At most first 3 bytes of instruction
  Can direct D2 stage to get rest of instruction
Decode stage 2 (D2)
  Expand opcode into control signals
  Computation of complex address modes
Execute (EX)
  ALU operations, cache access, register update
Writeback (WB)
  Update registers & flags
  Results sent to cache & bus interface write buffers

## Slide 32: 80486 Instruction Pipeline Examples

## Slide 33: Pentium 4 Registers

## Slide 34: EFLAGS Register

## Slide 35: Control Registers

## Slide 36: Pentium Interrupt Processing
Interrupts
  Maskable
  Nonmaskable
Exceptions
  Processor detected
  Programmed
Interrupt vector table
  Each interrupt type assigned a number
  Index to vector table
  256 * 32 bit interrupt vectors
5 priority classes

## Slide 37: PowerPC User Visible Registers

## Slide 38: PowerPC Register Formats