## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2: Computer Architecture
Control Unit Operation

## Slide 3: Outline
Control Unit Operation
  Major Advances in Computers
  Micro-Operations
  Constituent Elements of Program Execution
  Basic Functional Elements of Processor
  Types of Micro-operation
  Functions of Control Unit
  Control Signals
  Internal Processor Organization

## Slide 4: Major Advances in Computers(1)
The family concept
  IBM System/360 1964
  DEC PDP-8
  Separates architecture from implementation
Microprogrammed control unit
  Idea by Wilkes 1951
  Produced by IBM S/360 1964
Cache memory
  IBM S/360 model 85 1969

## Slide 5: Major Advances in Computers(2)
Solid State RAM
Microprocessors
  Intel 4004 1971
Pipelining
  Introduces parallelism into fetch execute cycle
Multiple processors

## Slide 6: Functional requirements for a processor
The following list determines what a processor must do:
  Operations (opcodes)
  Addressing modes
  Registers
  I/O module interfaces
  Memory module interfaces
  Interrupt processing structure
Question is:
how the verious elements of the processor are controlled to provide these functions?

## Slide 7: Micro-Operations
A computer executes a program
  Program cycle
A program is a collection of
  instruction cycles
An instruction cycle is made of
  Fetch and execute cycles
Each cycle has a number of steps
  Called micro-operations
Each step does very little
  Atomic operation of CPU

## Slide 8: Constituent Elements of Program Execution

## Slide 9: Fetch Cycle – (relevant Registers)
Memory Address Register (MAR)
  Connected to address bus
  Specifies address for read or write op
Memory Buffer Register (MBR)
  Connected to data bus
  Holds data to write or last data read
Program Counter (PC)
  Holds address of next instruction to be fetched
Instruction Register (IR)
  Holds last instruction fetched

## Slide 10: Sequence of events, Fetch cycle

## Slide 11: Fetch Sequence
Address of next instruction is in PC
Address (MAR) is placed on address bus
Control unit issues READ command
Result (data from memory) appears on data bus
Data from data bus copied into MBR
PC incremented by 1 (in parallel with data fetch from memory)
Data (instruction) moved from MBR to IR
MBR is now free for further data fetches

## Slide 12: Fetch Sequence (symbolic)
t1: MAR <- (PC)
t2: MBR <- (memory)
PC <- (PC) +1
t3: IR <- (MBR)
(tx = time unit/clock cycle)
or
t1: MAR <- (PC)
t2: MBR <- (memory)
t3: PC <- (PC) +1
IR <- (MBR)

## Slide 13: Rules for Clock Cycle Grouping
Proper sequence must be followed
  MAR <- (PC) must precede MBR <- (memory)
Conflicts must be avoided
  Must not read & write same register at same time
  MBR <- (memory) & IR <- (MBR) must not be in same cycle
Also: PC <- (PC) +1 involves addition
  Use ALU
  May need additional micro-operations

## Slide 14: Indirect Cycle
MAR <- (IRaddress) - address field of IR
MBR <- (memory)
IRaddress <- (MBRaddress)
MBR contains an address
IR is now in same state as if direct addressing had been used
(What does this say about IR size?)

## Slide 15: Interrupt Cycle
t1: MBR <-(PC)
t2: MAR <- save-address
PC <- routine-address
t3: memory <- (MBR)
This is a minimum
  May be additional micro-ops to get addresses

## Slide 16: Execute Cycle (ADD)
Different for each instruction
  e.g. ADD R1,X - add the contents of location X to Register 1 , result in R1
t1: MAR <- (IRaddress)
t2: MBR <- (memory)
t3: R1 <- R1 + (MBR)
Note no overlap of micro-operations

## Slide 17: Execute Cycle (ISZ)
ISZ X - increment and skip if zero
t1: MAR <- (IRaddress)
t2: MBR <- (memory)
t3: MBR <- (MBR) + 1
t4: memory <- (MBR)
  if (MBR) == 0 then PC <- (PC) + 1

## Slide 18: Execute Cycle (BSA)
BSA X - Branch and save address
  Address of instruction following BSA is saved in X
  Execution continues from X+1
t1: MAR <- (IRaddress)
MBR <- (PC)
t2: PC <- (IRaddress)
memory <- (MBR)
t3: PC <- (PC) + 1

## Slide 19: Instruction Cycle
Each phase decomposed into sequence of elementary micro-operations
E.g. fetch, indirect, and interrupt cycles
Execute cycle
  One sequence of micro-operations for each opcode
Need to tie sequences together
Assume new 2-bit register
  Instruction cycle code (ICC) designates which part of cycle processor is in
    00: Fetch
    01: Indirect
    10: Execute
    11: Interrupt

## Slide 20: Flowchart for Instruction Cycle
01

## Slide 21: Basic Funcional Elements of Processor
ALU
Registers
Internal data paths
External data paths
Control Unit

## Slide 22: Types of Micro-operation
Transfer data between registers
Transfer data from register to external
Transfer data from external to register
Perform arithmetic or logical operations

## Slide 23: Functions of Control Unit
Sequencing
  Causing the CPU to step through a series of micro-operations
Execution
  Causing the performance of each micro-op
This is done using Control Signals

## Slide 24: Model of Control Unit

## Slide 25: Control Signals
Clock
  One micro-instruction (or set of parallel micro-instructions) per clock cycle
Instruction register
  Op-code for current instruction
  Determines which micro-instructions are performed
Flags
  State of CPU
  Results of previous operations
From control bus
  Interrupts
  Acknowledgements

## Slide 26: Control Signals - output
Control signals within CPU
  Cause data movement
  Activate specific functions
Control signals to control bus
  To memory
  To I/O modules

## Slide 27: Example Control Signal Sequence-Fetch
MAR <- (PC)
  Control unit activates signal to open gates between PC and MAR
MBR <- (memory)
  Open gates between MAR and address bus
  Memory read control signal
  Open gates between data bus and MBR

## Slide 28: Data Paths and Control Signals

## Slide 29: Micro-operations and Control Signals

## Slide 30: Internal Processor Organization
Usually a single internal bus
Gates control movement of data onto and off the bus
Control signals control data transfer to and from external systems bus
Temporary registers needed for proper operation of ALU

## Slide 31: CPU with Internal Bus

## Slide 32: Intel 8085 CPU Block Diagram

## Slide 33: Intel 8085 External Signals...

## Slide 34: Intel 8085 External Signals

## Slide 35: Intel 8085 Pin Configuration

## Slide 36: Intel 8085 OUT Instruction Timing Diagram