## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2: Computer Architecture
Micro-Programmed Control

## Slide 3: Outline
Micro-Programmed Control
  Control Unit Implementation
    Hardwired Implementation
    Micro-programmed Control
  Control Unit Organization
  Micro-instruction Types
  Organization of Control Memory
  Sequencing Techniques
  Address Generation
  Microinstruction Execution
  Control Unit Organization
  Microinstruction Encoding

## Slide 4: Control Unit Implementation
Hardwired implementation
  Combinatorial circuit
Microprogrammed implementation

## Slide 5: Hardwired Implementation (1)
Control unit inputs
Flags and control bus
  Each bit means something
Instruction register
  Op-code causes different control signals for each different instruction
  Unique logic for each op-code
  Decoder takes encoded input and produces single output
  n binary inputs and 2n outputs

## Slide 6: Hardwired Implementation (2)
Clock
  Repetitive sequence of pulses
  Useful for measuring duration of micro-ops
  Must be long enough to allow signal propagation
  Different control signals at different times within instruction cycle
  Need a counter with different control signals for t1, t2 etc.

## Slide 7: A Decoder with four inputs and 16 outputs

## Slide 8: Control Unit with Decoded Inputs

## Slide 9: Control signal example
Consider a single signal, C5.
  causes data to be read from the external data bus into the MBR
Used twice in the table
Let us define two new control signals, P and Q:
  PQ = 00 Fetch cycle
  PQ = 01 Indirect cycle
  PQ = 10 Execute cycle
  PQ = 11 Interrupt cycle
Boolean expression for C5
  C5 = P'·Q'·T2 + P'·Q·T2
C5 is also needed during execute cycle
  Let us assume there are only three instructions
    LDA, ADD, AND
Boolean expression for C5 becomes
  C5 = P'·Q'·T2 + P'·Q·T2 + P·Q'·(LDA + ADD +AND)

## Slide 10: Problems With Hard Wired Designs
Complex sequencing & micro-operation logic
Difficult to design and test
Inflexible design
Difficult to add new instructions

## Slide 11: Micro-programmed Control
Consider the following table
  Notation looks like a programming language
In fact it is a language
  Called microprogramming language
Each line describes a set of micro-operations
  known as a microinstruction
A sequence of microinstructions
  Known as microprogram
  or firmware

## Slide 12: Control Unit Organization
All the control unit (CU) does is to generate a set of control signals
  Each control signal is reprented by a bit
    which is either on or off
  CU have a control word for each micro-operation
  CU have a sequence of control words for each machine code instruction
  CU adds an address to specify the next micro-instruction, depending on conditions

## Slide 13: Control Unit Organization
Today’s large microprocessor
  Many instructions and associated register-level hardware
  Many control points to be manipulated
This results in control memory that
  Contains a large number of words
    corresponding to the number of instructions to be executed
  Has a wide word width
    Due to the large number of control points to be manipulated

## Slide 14: Micro-program Word Length
Based on 3 factors
  Maximum number of simultaneous micro-operations supported
  The way control information is represented or encoded
  The way in which the next micro-instruction address is specified

## Slide 15: Micro-instruction Types
Vertical micro-programming
  Each micro-instruction specifies single (or few) micro-operations to be performed
Horizontal micro-programming
  Each micro-instruction specifies many different micro-operations to be performed in parallel

## Slide 16: Vertical Micro-programming
Width is narrow
n control signals encoded into log2 n bits
Limited ability to express parallelism
Considerable encoding of control information requires external memory word decoder to identify the exact control line being manipulated

## Slide 17: Horizontal Micro-programming
Wide memory word.
  1 bit for each internal processor control line
  1 bit for each system bus control line
  Condition field
  Addres field
High degree of parallel operations possible
Little encoding of control information

## Slide 18: Organization of Control Memory

## Slide 19: Control Unit Function
Sequence logic unit issues read command
Word specified in control address register is read into control buffer register
Control buffer register contents generates control signals and next address information
Sequence logic loads new address into control buffer register based on next address information from control buffer register and ALU flags

## Slide 20: Next Address Decision
Depending on ALU flags and control buffer register
  Get next instruction
    Add 1 to control address register
  Jump to new routine based on jump microinstruction
    Load address field of control buffer register into control address register
  Jump to machine instruction routine
    Load control address register based on opcode in IR

## Slide 21: Pros and Cons
Advantages of Microprogramming
  Simplifies design of control unit
    Cheaper
    Less error-prone
Disadvantages of Microprogramming
  Slower

## Slide 22: Tasks Done By Microprogrammed Control Unit
Microinstruction sequencing
  Get the next microinstruction from the control memory
Microinstruction execution
  Generate the control signals needed to execute the microinstruction
In designing the control unit, these tasks must be considered together,
  because both affect the format of the microinstruction
  and the timing of control unit

## Slide 23: Sequencing Techniques
Generation of the control memory addres for the next instruction is based on...
  current microinstruction,
  condition flags, and
  contents of IR,
A number of categories exist.
These categories are based on...
  format of address information:
    Two address fields
    Single address field
    Variable format

## Slide 24: Branch Control Logic: Two Address Fields
A multiplexer (MUX) ...
  serves as a destination for..
    both address fields, and
    IR
Based on an address selection input, MUX transmits either...
  the op-code or
  one of the two addresses
to CAR
CAR is subsequently decoded to produce the next microinstruction address
The address selection signals are provided by a branch logic module,
  whose input consists of ...
    CU flags, and
    bits from the control portion of the microinstruction

## Slide 25: Branch Control Logic: Single Address Field
Options for next address:
  Address field
  IR code
  Next sequential address
Determined by address selection signals
This approach reduces the number of address fields to one
Thus, there is some inefficiency in the microinstruction coding scheme

## Slide 26: Branch Control Logic: Variable Format
Two different microinstruction formats are provided:
  One bit designates which format is being used
In one format,...
  remaining bits are used to activate control signals
In the other format,...
  some bits drive the branch logic module, and
  the remaining bits provide the address.
Next address is either...
  the next sequential address or
  an address derived from the IR

## Slide 27: Address Generation
Looked at the sequencing problem from the point of format considerations and general logic requirement
Another view point is to consider the various ways in which the next address is computed
Can be divided into two main techniques
  Explicit techniques
    Address is explicitly available in the microinstruction
  Implicit techniques
    Require additional logic to generate address

## Slide 28: Address Generation
Explicit techniques have been discussed:
  With a two-field approach, two alternative addresses are available with each microinstruction.
  Using either a single address field or a variable format, various branch instructions can be implemented.
A conditional branch instruction depends on the...
  ALU flags
  part of the opcode or address mode fields of the machine instruction
  parts of a selected register, such as the sign bit
  status bits within the CU

## Slide 29: Address Generation
Three main implicit techniques:
Mapping
  Opcode portion of a machine instruction must be mapped into a microinstruction address
  This occurs only once per instruction cycle
Adding
  Two portions of an address are combined to form the complete address
Residual control
  Involves the use of a microinstruction address that has previously been saved in temporary storage within the CU.

## Slide 30: Address Generation
Explicit | Implicit
Two-field | Mapping
Unconditional Branch | Addition
Conditional branch | Residual control

## Slide 31: Microinstruction Execution
The microinstruction cycle is the basic event on a microprogrammed processor
Each cycle is made up of two events
  Fetch
    Determined by generation of microinstruction address
  Execute
    Effect is to generate control signals
    Some control points internal to processor
    Rest go to external control bus or other interface

## Slide 32: Control Unit Organization
Microinstructions can be classified in a variety of ways
Distinctions that are commonly made in the literature include...
  Vertical/horizontal
  Packed/unpacked
  Hard/soft microprogramming
  Direct/indirect encoding

## Slide 33: How to Encode
Consider that there are K different internal and external control signals
Not all of the possible combinations will be used.
For example:
  Two sources cannot be gated to same destination
  Register cannot be source and destination
  Only one pattern presented to ALU at a time
  Only one pattern presented to external control bus at a time
Require Q < 2K which can be encoded with log2Q < K bits
In practice this form of encoding is not used for the following reasons:
  As difficult to program as pure decoded scheme
  Requires complex slow control logic module
Instead, some compromises are made as follows:
  More bits than necessary are used to encode the possible combinations
  Some combinations that are physically allowable are not possible to encode

## Slide 34: Specific Encoding Techniques
Microinstruction organized as set of fields
Each field contains code
Activates one or more control signals
Organize format into independent fields
  Field depicts set of actions (pattern of control signals)
  Actions from different fields can occur simultaneously
Alternative actions that can be specified by a field are mutually exclusive
  Only one action specified for field could occur at a time

## Slide 35: Organizing encoded micro instruction in to fields
Two approaches ca be taken to organizing encoded micro instruction in to fields:
  Functional encoding
    Identifies functions within the machine and designates fields by function type.
    For example, if various sources can be used for transferring data ta the accumulator, one field can be designated for this purpose, with each code specifying a different source
  Resource encoding
    Views the machine as consisting of a set of independent resources and devotes one field to each (e.g., I/O, memory, ALU)

## Slide 36: Microinstruction Encoding Direct Encoding
Another aspect of encoding is whether it is direct or indirect