## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2: Computer Architecture
RISC Characteristics

## Slide 3: Outline
Major Advances in Computers
Comparison of processors
Driving force for CISC
Execution Characteristics
Large Register File
Registers for Local Variables
Global Variables
Compiler Based Register Optimization
Graph Coloring
Register Optimization
RISC Characteristics
RISC Pipelining

## Slide 4: Major Advances in Computers
The family concept
  IBM System/360 1964
  DEC PDP-8
  Separates architecture from implementation
Microporgrammed control unit
  Idea by Wilkes 1951
  Produced by IBM S/360 1964
Cache memory
  IBM S/360 model 85 1969
Solid State RAM
Microprocessors
  Intel 4004 1971
Pipelining
  Introduces parallelism into fetch execute cycle
Multiple processors

## Slide 5: RISC
Reduced Instruction Set Computer (RISC)
Key features
  Large number of general purpose registers
  And/or use of compiler technology to optimize register usage
  Limited and simple instruction set
  Emphasis on optimising the instruction pipeline

## Slide 6: Comparison of processors

## Slide 7: Driving force for CISC
Complex Instruction Set Computer (CISC)
Software costs far exceed hardware costs
Increasingly complex high level languages
Major cost in the lifecycle of a system is software, not hardware
Systems have also an element of unreliability
  It is common for programs, both system and application, to continue to exhibit new bugs after years of operation
Response from researchers and industry has been to develop ever more powerful and complex high-level programming languages
  HLLs allow programmers to express algorithms more concisely

## Slide 8: Driving force for CISC
This solution gave rise to another problem:
  Semantic gap, which is...
    difference between the operations provided in HLLs and those provided in computer architecture
  Symptoms of this gap:
    Execution ineficiency
    Excessive machine program size
    Compiler complexity
Processor designers response:
  Architectures intended to close this gap, such as...
    Large instruction sets
    More addressing modes
    Hardware implementations of HLL statements
      e.g. CASE (switch) on VAX

## Slide 9: Intention of CISC
Complex instruction sets are intended to...
Ease the task of compiler writer
Improve execution efficiency
  Complex operations can be implemented in microcode
Provide support for more complex HLLs

## Slide 10: Execution Characteristics
Studies have been done over the years to determine the characteristics and patterns of execution of machine instructions generated from HLL programs
The results of these studies inspired some researchers to look for a different approach:
  To make the architecture that supports the HLL simpler, rather than more complex
The aspects of computation of interest are as follows:
  Operations performed
    Determine the functions to be performed by the processor and its interaction with memory
  Operands used
    Determine the memory organization for storing them and the addressing modes for accessing them
  Execution sequencing
    Determines the control and pipeline organization

## Slide 11: Relative Dynamic Frequency of HLL Operations
A variety of studies have been done to analyze the behavior of HLL programs.
Dynamic studies are measured during the execution of the program
  The table indicates the relative significance of various statement types in an HLL
  Assignments
    Movement of data
  Conditional statements (IF, LOOP)
    Sequence control
Procedure call-return is very time consuming
  Depends on number of parameters passed
  Depends on level of nesting
Some HLL instruction lead to many machine code operations
Dynamic Occurrence
Machine-Instruction Weighted
Memory-Reference Weighted
Pascal
C
Pascal
C
Pascal
C
ASSIGN
45%
38%
13%
13%
14%
15%
LOOP
5%
3%
42%
32%
33%
26%
CALL
15%
12%
31%
33%
44%
45%
IF
29%
43%
11%
21%
7%
13%
GOTO
—
3%
—
—
—
—
OTHER
6%
1%
3%
1%
2%
1%

## Slide 12: Operands
Table shows dynamic percentage of operands
Mainly local scalar variables
Optimisation should concentrate on accessing local variables
Pascal
C
Average
Integer Constant
16%
23%
20%
Scalar Variable
58%
53%
55%
Array/Structure
26%
24%
25%

## Slide 13: Implications
Best support is given by optimising most used and most time consuming features
Large number of registers
  Operand referencing
Careful design of pipelines
  Branch prediction etc.
Simplified (reduced) instruction set

## Slide 14: Large Register File
Software solution
  Require compiler to allocate registers
  Allocate based on most used variables in a given time
  Requires sophisticated program analysis
Hardware solution
  Have more registers
  Thus more variables will be in registers

## Slide 15: Registers for Local Variables
Store local scalar variables in registers
Reduces memory access
Every procedure (function) call changes locality
Parameters must be passed
Results must be returned
Variables from calling programs must be restored

## Slide 16: Global Variables
There are two options for storing variables declared as global in an HLL:
  Allocated by the compiler to memory
    Instructions will use memory-reference operands
    Inefficient for frequently accessed variables
  Have a set of registers for global variables
    Fixed in number
    Available to all procedures
    Increased hardware burden
    Compiler must decide which global variables should be assigned to registers

## Slide 17: Registers v Cache
Large Register File
Cache
All local scalars
Recently-used local scalars
Individual variables
Blocks of memory
Compiler-assigned global variables
Recently-used global variables
Save/Restore based on procedure nesting depth
Save/Restore based on cache replacement algorithm
Register addressing
Memory addressing
Adressing overhead
  Large based register file is superior

## Slide 18: Compiler Based Register Optimization
Assume small number of registers (16-32)
Optimized register usage is the responsibility of the compiler
HLL programs have no explicit references to registers
The objective of compiler is to keep the operands for as many computations as possible in registers to minimize load-and-store operations
Following approach is taken:
  Assign symbolic or virtual register to each candidate variable
  Compiler maps (unlimited) symbolic registers to a fix number of real registers
  Symbolic registers that do not overlap can share the same real registers
  If you run out of real registers some variables use memory

## Slide 19: Graph Coloring
The essence of the optimization task is to decide which quantities are to be assigned to registers at any given point in the program
The technique commonly used in RISC compilers is known as graph coloring:
  Given a graph of nodes and edges
  Assign a color to each node such that...
    Adjacent nodes have different colors
    Use minimum number of colors
Graph coloring is adapted to the compiler problem as follows:
  Nodes of the graph are symbolic registers
  Two registers that are live in the same program fragment are joined by an edge
  Try to color the graph with n colors, where n is the number of real registers
  Nodes that share the same color can be assigned to the same register
  Nodes that can not be colored are placed in memory

## Slide 20: Graph Coloring Approach
Assume a program with 6 symbolic registers to be compiled into 3 actual registers
A possible coloring with 3 colors is indicated.
One symbolic register, F, is left uncolored and must be used dealt with using loads and stores

## Slide 21: Register Optimization
There is a trade of between...
  Use of large set of registers and...
  Compiler-based register optimization
In one study, reported that...
  With a simple register optimization, there is little benefit to the use of more than 64 registers
  With reasonably sofisticated register optimization techniques, there is only marginal performance improvement with more than 32 registers

## Slide 22: Why CISC (1)?
Two principle reasons:
  Compiler simplification?
    Disputed…
    Complex machine instructions harder to exploit
    Optimization more difficult
  Smaller programs?
    Program takes up less memory but…
    Memory is now cheap
    May not occupy less bits, just look shorter in symbolic form
      More instructions require longer op-codes
      Register references require fewer bits

## Slide 23: Why CISC (2)?
Faster programs?
  Bias towards use of simpler instructions
  More complex control unit
  Microprogram control store larger
  thus simple instructions take longer to execute
It is far from clear that CISC is the appropriate solution

## Slide 24: RISC Characteristics
Common characteristics of RISC are:
  One instruction per cycle
  Register to register operations
  Few, simple addressing modes
  Few, simple instruction formats
  Hardwired design (no microcode)
  Fixed instruction format
  More compile time/effort

## Slide 25: RISC v CISC
Not clear cut
Many designs borrow from both philosophies
More recent RISC designs are no longer pure RISC
More recent CISC designs are no longer pure CISC
  e.g. PowerPC and Pentium II

## Slide 26: RISC Pipelining
Most instructions are register to register
An instruction cycle has two phases of execution:
  I: Instruction fetch
  E: Execute
    Performs an ALU operation with register input and output
For load and store operations, there are three stages:
  I: Instruction fetch
  E: Execute
    Calculates memory address
  D: Memory
    Register to memory or memory to register operation

## Slide 27: Sequential execution
Timing of a sequence of instructions with...
  No pipelining
This is a wasteful process

## Slide 28: Pipelined timing - I
This is a...
  Two stage pipelining
  Provides upto twice the execution rate of a serial scheme
I and E stages of two different instructions are performed simultaneously
Two main problems:
  Only one memory access per stage
    Assuming that single port main memory is used
  Branch instruction interrupts the sequencial flow of execution
    NOOP is inserted by compiler or assembler for minimum circuitry

## Slide 29: Pipelined timing - II
Pipelining can be improved by...
  permitting two memory access per stage
  Upto three instructions can be overlapped, prividing...
    An improvement as much as a factor of 3.
Branch instruction interrupts the sequencial flow of execution
  NOOP is inserted by compiler or assembler for minimum circuitry

## Slide 30: Pipelined timing - III
Because E stage involves ALU operation, it may be longer.
Threfore E stage...
  can be devided into two substages
    E1 : register file read
    E2 : ALU operation and register write...
This results in a ...
  four stage pipeline
  Maximum speed up of a factor of 4

## Slide 31: Optimization of Pipelining
Pipelining in RISC is efficient.
The reason for this is that...
  RISC instructions are simple and regular
However branch dependencies reduce the overall execution rate
To compensate for these dependencies ...
  some code recognition techniques have been developed
Delayed branch
  Does not take effect until after execution of following instruction
  This following instruction is the delay slot
  Illustrated in next slide

## Slide 32: Normal and Delayed Branch
Address
Normal Branch
Delayed Branch
Optimized Delayed Branch
100
LOAD X, rA
LOAD X, rA
LOAD X, rA
101
ADD 1, rA
ADD 1, rA
JUMP 105
102
JUMP 105
JUMP 106
ADD 1, rA
103
ADD rA, rB
NOOP
ADD rA, rB
104
SUB rC, rB
ADD rA, rB
SUB rC, rB
105
STORE rA, Z
SUB rC, rB
STORE rA, Z
106
STORE rA, Z

## Slide 33: Traditional pipeline
JUMP instruction is fetched at time 4.
At time 5, JUMP is executed and ADD is fetched
  However, pipeline must be cleared of instruction 103 because of JUMP instruction
At time 6, instruction 105 is loaded
There must be a special circuitry to clear pipeline in branch instructions

## Slide 34: RISC pipeline with inserted NOOP
Because a NOOP inserted, there is no need for special circuitry to clear pipeline
  NOOP executes with no effect

## Slide 35: Reversed instructions
JUMP is fetched at time 2, before the ADD instruction
However, ADD is fetched before JUMP is executed
At time 4, ADD is executed at the same time that instruction 105 is fetched

## Slide 36: Use of Delayed Branch

## Slide 37: Controversy
Quantitative
  compare program sizes and execution speeds
Qualitative
  examine issues of high level language support and use of VLSI real estate
Problems
  No pair of RISC and CISC that are directly comparable
  No definitive set of test programs
  Difficult to separate hardware effects from complier effects
  Most comparisons done on “toy” rather than production machines
  Most commercial devices are a mixture

## Slide 38: MIPS R4000
1st commercial RISC chip developed by MIPS Technology inch
MIPS R2000 and R3000, are 32 bit RISC processors
MIPS R4000 is 64 bit processor
R4000 is partitioned into two sections:
  One contains CPU
  The other contains the coprocessor for memory management
32 64 bit registers
Upto 128 Kbytes of high-speed cache

## Slide 39: Instruction set

## Slide 40: Instruction set

## Slide 41: Instruction set

## Slide 42: MIPS instruction formats