## Slide 1: Computer Architecture
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
nizamettinaydin@gmail.com
http://www.yildiz.edu.tr/~naydin

## Slide 2: Computer Architecture
Instruction Level Parallelism and Superscalar Processors

## Slide 3: Outline
What is Superscalar?
Superpipelining
Limitations
  Data Dependency
  Procedural Dependency
  Resource Conflict
Effect of Dependencies
Instruction level parallelizm and machine level parallelism
Instruction Issue Policy
Antidependency
Register Renaming
Machine Parallelism

## Slide 4: What is Superscalar?
A superscalar implementation of a processor architecture is one in which...
  common instructions (arithmetic, load/store, conditional branch) can be
    initiated simultaneously and
    executed independently
Superscalar approach can be equally applicable to RISC & CISC
In practice usually RISC

## Slide 5: Why Superscalar?
The term superscalar refers to a machine that is designed to improve the performance of the execution of scalar instructions
In most applications, most operations are on scalar quantities
Improve these operations to get an overall improvement
Essence of the superscalar approach is the ability to execute instructions independently in different pipelines

## Slide 6: General Superscalar Organization - Superpipelining
Superpipelining is an alternative approach to achieving greater performance
It exploits the fact that many pipeline stages need less than half a clock cycle
Double internal clock speed gets two tasks per external clock cycle
Superscalar allows parallel fetch execute

## Slide 7: Superscalar vSuperpipeline
Ordinary pipeline
Superpipelined approach:
  2 pipeline stages per clock cycle
Superscalar implementation
  Executing two instances of each stage in parallel
Higher-degree superpipeline and superscalar implementations are possible

## Slide 8: Limitations
Superscalar approach depends on the ability to execute multiple instructions in parallel
Instruction level parallelism refers to the degree to which, on average, the instructions of a program can be executed in parallel
To maximize instruction-level parallelism:
  Compiler based optimisation
  Hardware techniques
Fundamental limitations to parallelism:
  True data dependency
  Procedural dependency
  Resource conflicts
  Output dependency
  Antidependency

## Slide 9: True Data Dependency
A true data dependency occurs when an instruction depends on the result of a previous instruction
Consider the following sequence:
  ADD r1, r2 (r1 := r1+ r2;)
  MOVE r3,r1 (r3 := r1;)
Can fetch and decode second instruction in parallel with first
  However, can NOT execute the second instruction until the first one is finished
Also called flow dependency or write-read dependency

## Slide 10: True Data Dependency
d

## Slide 11: Procedural Dependency
The presence of branches in an instruction sequence complicates the pipeline operation
The instruction following a branch
  have a procedural dependency on the branch and
  can not be executed until the branch is executed
Also, if instruction length is not fixed, instructions have to be decoded to find out how many fetches are needed
This prevents simultaneous fetches

## Slide 12: Effect of a branch on a superscalar pipeline of degree 2

## Slide 13: Resource Conflict
A resource conflict is...
  a competition of two or more instructions requiring access to the same resource at the same time
    e.g. two arithmetic instructions
In terms of pipeline it exhibits similar behavior to a data dependency
However, resource conflict can be overcome by duplication of resources
  e.g. have two arithmetic units

## Slide 14: Resource Conflict

## Slide 15: Effect of Dependencies
d

## Slide 16: Instruction level parallelizm and machine level parallelizm
Instruction level parallelism exists when...
  Instructions in a sequence are independent
Therefore execution can be overlapped
Degree of instruction level parallelizm determined by the frequency of true data and procedural dependencies in the code
For example consider the following codes:
Load R1  R2 Add R3  R3 , ”1”
Add R3  R3, ”1” Add R4  R3 , R2
Add R4  R4, R2 Store [R4]  R0
Instructions on the left are independent, so they can be executed in parallel
Instructions on the right are not independent (data dependency), so they cannot be executed in parallel

## Slide 17: Instruction level parallelizm and machine level parallelizm
Machine Parallelism is a measure of the...
  ability to take advantage of instruction level parallelism
It is determined by ...
  the number of instructions that can be fetched and executed at the same time
    (number of parallel pipelines)
  the speed and sophistication of the mechanisms that the processor uses to find independent instructions
Both instruction level and machine level paralellizm are important factors in enhancing performance

## Slide 18: Instruction Issue Policy
Instruction issue is the process of initiating instruction execution in the processor’s functional units
Instruction issue policy is the protocol to issue instructions
The processor is trying to look ahead of the current point of execution to locate instructions that can be brought into the pipeline and executed
Three types of orderings are important:
  Order in which instructions are fetched
  Order in which instructions are executed
  Order in which instructions change registers and memory

## Slide 19: Instruction Issue Policy
In general, instruction issue policies can be devided into the following categories:
  In-order issue with in-order completion
  In-order issue with out-of-order completion
  Out-of-order issue with out-of-order completion

## Slide 20: In-Order Issue with In-Order Completion
Issue instructions in the order they occur
Not very efficient
May fetch >1 instruction
Instructions must stall if necessary
Next slide is an example to this policy
Assume a superscale pipeline ...
  capable of fetching and decoding 2 instructions at a time,
  have 3 seperate functional unit, and
  two instances of the write-back pipeline stage
Example assumes the following constraints
  I1 requires 2 cycles to execute
  I3 and I4 conflict for the same functional unit
  I5 depends on the value produced by I4
  I5 and I6 conflict for a functional unit

## Slide 21: In-Order Issue with In-Order Completion (Diagram)
Instructions are fetched in pairs and passed to the decode unit
Next 2 instructions must wait until the pair of decode pipeline stages has cleared
When there is a conflict for a functional unit or when a functional unit requires more than 1 cycle to generate a result, issuing of instructions temporarily stalls

## Slide 22: In-Order Issue with Out-of-Order Completion
Used in scalar RISC processors to improve the performance of instructions that require multiple cyles
  next slide illustrates its use on a superscalar processor
Output dependency (write-write dependency)
I1: R3  R3 + R5
I2: R4  R3 + 1
I3: R3  R5 + 1
I4: R7  R3 + R4
  I2 depends on result of I1 - data dependency
  If I3 completes before I1, the result from I1 will be wrong

## Slide 23: In-Order Issue with Out-of-Order Completion (Diagram)
Out-of-order completion requires more complex instruction issue logic than in-order completion
More difficult to deal with instruction interrupts and exceptions
When an interrupt happens, instruction execution at the current point is suspended, to be resumed later

## Slide 24: Out-of-Order Issue with Out-of-Order Completion
To allow out-of-order issue, it is necessary...
  to decouple decode pipeline from execution pipeline
    This is done with a buffer referred to as an instruction window
  After a processor has finished decoding an instruction, it is placed into instruction window
  Since instructions have been decoded, processor can look ahead
Processor can continue to fetch and decode new instructions until this buffer is full
When a functional unit becomes available in the execution stage, an instruction from the instruction window may be issued to the execute stage
Any instruction may be issued, provided that...
  it needs the particular functional unit that is available
  no conflict or dependencies block this instruction
Next slide illustrates this policy

## Slide 25: Out-of-Order Issue Out-of-Order Completion (Diagram)
2 instructions fetched into the decode stage
2 instructions move to the instruction window
It is possible to issue I6 ahead of I5 (I6 does not depend on I5)
One cycle is saved
Window implies that the processor has sufficient information about that instruction to decide when it can be issued

## Slide 26: Antidependency
An instruction cannot be issued if it violates a dependency or conflict
In out-of-order issue with out-of-order completion policy, more instructions are available for issuing reducing the possibility that a pipeline stage will have to stall
Antidepencency (read-write dependency) arises
I1: R3  R3 + R5
I2: R4  R3 + 1
I3: R3  R5 + 1
I4: R7  R3 + R4
  I3 cannot complete execution before I2 starts as I2 needs a value in R3 and I3 changes R3
  It is called antidependency because the constraint is similar to that of true data dependency, but reversed,

## Slide 27: Register Renaming
Output and antidependencies occur because register contents may not reflect the correct ordering from the program
May result in a pipeline stall
One solution is duplication of resources:
  called register renaming
Registers allocated dynamically by the processor hardware, and they are associated with the values needed by instructions at various points in time.
  i.e. registers are not specifically named

## Slide 28: Register Renaming example
I1: R3b  R3a + R5a
I2: R4b  R3b + 1
I3: R3c  R5a + 1
I4: R7a  R3c + R4b
Without subscript refers to logical register in instruction
With subscript is hardware register allocated
In this example, the creation of R3c in I3 avoids...
  the antidependency on the 2nd instruction and
  output dependency on the 1st instruction,
and it does not interfere with the correct value being accessed by I4.
The result is that I3 can be issued until the 1st instruction is complete and the 2nd instruction is issued

## Slide 29: Machine Parallelism
3 hardware techniques in superscalar processors to enhance performance:
  Duplication of Resources
  Out of order issue
  Renaming
Next slide shows results of a study, made use of a simulation that modeled a machine with the characteristic of the MIPS R2000, augmented with various superscalar features

## Slide 30: Speedups of Machine Organizations without Procedural Dependencies
Graphs yield some important conclusions:
  Not worth duplication functions without register renaming
  Need instruction window large enough (more than 8)

## Slide 31: Superscalar Execution

## Slide 32: Superscalar Implementation
Simultaneously fetch multiple instructions
Logic to determine true dependencies involving register values
Mechanisms to communicate these values
Mechanisms to initiate multiple instructions in parallel
Resources for parallel execution of multiple instructions
Mechanisms for committing process state in correct order

## Slide 33: Pentium 4
80486 - CISC
Pentium – some superscalar components
  Two separate integer execution units
Pentium Pro – Full blown superscalar
Subsequent models refine & enhance superscalar design

## Slide 34: Pentium 4 Block Diagram

## Slide 35: Pentium 4 Operation
Fetch instructions form memory in order of static program
Translate instruction into one or more fixed length RISC instructions (micro-operations)
Execute micro-ops on superscalar pipeline
  micro-ops may be executed out of order
Commit results of micro-ops to register set in original program flow order
Outer CISC shell with inner RISC core
Inner RISC core pipeline at least 20 stages
  Some micro-ops require multiple execution stages
    Longer pipeline
  c.f. five stage pipeline on x86 up to Pentium

## Slide 36: Pentium 4 Pipeline

## Slide 37: Pentium 4 Pipeline Operation (1)

## Slide 38: Pentium 4 Pipeline Operation (2)

## Slide 39: Pentium 4 Pipeline Operation (3)

## Slide 40: Pentium 4 Pipeline Operation (4)

## Slide 41: Pentium 4 Pipeline Operation (5)

## Slide 42: Pentium 4 Pipeline Operation (6)

## Slide 43: PowerPC
Direct descendent of IBM 801, RT PC and RS/6000
All are RISC
RS/6000 first superscalar
PowerPC 601 superscalar design similar to RS/6000
Later versions extend superscalar concept

## Slide 44: PowerPC 601 General View

## Slide 45: PowerPC 601 Pipeline Structure

## Slide 46: PowerPC 601 Pipeline