## Slide 1
Introduction to Cryptology
22.05.2023, v51
Lecture-15
Identification Protocols
Physical Security

## Slide 2
Cryptographic
Identification Mechanisms/Protocols
Secret Key Mechanisms
Public Key Mechanisms
Required for every solid security system!

## Slide 3
1. Secret-Key Identification Mechanisms
Require a secret key agreement!

## Slide 4
Challenge-Response Identification Mechanisms
Explicit Secret Key Signature
Authenticity without Secrecy
Prover A
Verifier
Ki
Ki
Set up: Agree on a secret key Ki
and a One-Way Function F
Who are you ? : Prove by using R that you know Ki
Authentication Request
Generate
a random R
(Challenge)
RES=F(Ki , R)
I am A, and this is the proof : RES
(Response)
If RES = F(Ki , R)
then accept
?

## Slide 5
SIM Card
Ki
H
GSM Challenge-Response Identification
(SIM-Card identification)
Verifier‘s
GSM-HLR
CH(t) 128 bits
RES‘’ 32 bits
Ki
H
RES
Random Generator
CH(t)
=
Accept /
Reject
RES‘=RES?
COMP128
Hash mapping

## Slide 6
Improved Symmetric Challenge-Response Identification Mechanism
(Standard usage in modern network protocols)
I am A, and this is the proof : RES, Rt
(Response)
If RES = F(Ki, Rt, Rv)
then accept
?
Prover A
Verifier
Ki
Ki
Set up: Agree on a secret key Ki
and a One-Way Function F
RES=F(Rt, Ki, Rv)
Rt
Who are you ? : Prove by using Rv that you know Ki
Authentication Request
Generate
a random Rv
(Challenge)
Rv

## Slide 7
2. Public-Key Identification Protocols
No secret key agreement is necessary!

## Slide 8
Identification Protocols/Mechanisms
Zero- Knowledge Iterative Proof (ZKIP)
Authenticity without Secrecy
Prover
Verifier
Who are you ?
I am A, and this is the proof without revealing secrets
Authentication Request
The proof is called a Zero-Knowledge proof if:
Prover reveals no secrets (whatever) to the verifier !
This protocol can be repeated many times for higher security !

## Slide 9
S = r 2
Fiat-Shamir Proof-of-Identity Protocol (1986)
Prover A
Verifier
( I am user A, S )
t
randomly choose b
b = 1 or 0
m is RSA type modulus
ya = xa2 in Zm (mod m)
public directory
b
t = r. xab
xa = secret key of A
xa
If t2 = S . Yab = r2 . (Xa) 2b
then A is authentic
(A knows xa )
A chooses a unit r, gcd(m,r)=1
in Zm and computes
A Zero-Knowledge proof protocol !
Prob. of a successful attack after k random trials = 2-k
S ya
m = p1 p2
p1 p2 are secrets
which no body
should know
Security relies on the
Factoring Problem !
Attacker can cheat if he stores earlier verification with the same b sequence!!

## Slide 10
Example: Fiat-Shamir Proof-of-Identity Protocol (1986)
Prover A
Verifier
( I am user A, S=16 )
t =18
randomly choose b
b = 1 or 0
m= 35 is RSA type modulus
ya = xa2 =29 in Zm (mod m)
public directory
b=1
t = r. xab = 11 X 8 = 18
xa = secret key of A=8
xa
If t2 = S . yab =
182 = 16 X 291
9 = 9
then A is authentic
(A knows xa )
A chooses a unit r=11 , gcd (11,35)=1
in Zm and computes
A Zero-Knowledge proof protocol !
S = r 2 = 112 = 16
S ya
m = p1 p2 = 35
p1 p2 are secrets
which no body
should know

## Slide 11
Omura Proof-of-Identity Protocol
Prover A
Verifier
I am user A,
R Xa
Randomly choose k
compute R =  k
 is a primitive element in GF(p)
ya = public key of A
public directory
Who are you?, R
R Xa =  k. Xa
 Xa = ya
xa
R Xa
check R Xa = yak =  k. Xa
R
Is not Zero knowledge if verifier cheats !
Security relies on the
Discrete Log. Problem !

## Slide 12
Example: Omura Proof-of-Identity Protocol
Prover A
Verifier
I am user A,
RXa = 40
Randomly choose k=40
compute R =  k =41
Who are you?, R=41
 Xa = 211 = 56 = ya
xa
R Xa = 4111 = (240)11
= 2440 mod 82 = 40
check R Xa = yak
40 = 5640
40 = (211)40=40
=> User is authentic
R=41
GF(83)
Ya = 56
Public directory
 = 2

## Slide 13
GF(p), Element α has order q such that q is prime which divides p-1
yA : public key of signer A
Template of Schnorr’s Identification/signature Scheme
Open Directory (as DH public directory)
Secret key xA< q
Prover A
verifier
User A sings a message M:
Random
4
1
5
6
Verifiecation
7
Then, M signed by A is authentic
2
Hash :
A good and strong hash H function is required
3
Similarity to ElGamal Signature!
A signed message M is : M, (S,m)

## Slide 14
Physical Security
Why Physical Security
Physical Unclonability

## Slide 15
Commercial-economic reasons (Cloning)
Identity (Privacy)
Know-How protection (IP-Cores)
Medical
Automotive units
E-Money ….
Smart-Home, -City, -Gouvernement, Consumer, IoT ..
Why Physical Security?
Why unclonable physical units?

## Slide 16
Popular Attack Scenarios Physical Replacement/Substitution Attack
Customer
Legal
Unit
Intruder
False
Unit
Examples: - False mobile base station attack (GSM Mobile system)
- False Internet host

## Slide 17
Popular Attack Scenarios Tele-service attack: Channel Hijacking Attack
Customer
Internet
Legal
Service Access
False Access
Diverted/Hijacked channel
Machine

## Slide 18
Fake unit
Illegal
Monitor/Node
Popular Attack Scenarios Network unit replacement attack

## Slide 19
Popular Attack Scenarios Replacement Attack- Hardware patch
Manufacturer cheats!
Attacker has successfully cloned the unit!
Requirements
Unit structure should be unclonable or clone-resistant!
Unit should be unchangeable “Tamper-Proof”!
Gateway in
Gateway out
TÜV
cert
HW
Fake
HW
FCC
cert
HW

## Slide 20: Two Basic Requirements for Solid Security
Identify and trust each other (Mutual-Authentication)
Establish a secured link (secrecy)
Internet
Machine

## Slide 21: Contemporary State of the Art
Identify & Trust (Authentication) Physical Security
Secured link (secrecy)
- Electro-Mechanical identity (Mechatronic-Identity) !!?
(Automobile, Production Machines, Robots ….)
- Physical uniqueness !! ?
- Unclonable units !! ?
Relatively mature technology

## Slide 22
State of the Art for basically clonable Physical Units

## Slide 23
International Mobile Equipment Identity
IMEI (non-secured)
Practical GSM Security Gaps
A5 Cipher Broken 1999
SIM (secured)
Subscriber Identity Module
Cloned for some standard function
(150 000 challenges. Berkeley Univ.)
No collapse. System still solid!

## Slide 24
Identity
IMEI
Open Identity
Tamperproof
hardware entity
System
Software
Identity request
Manufacturer Identity
IMEI
IMEI (legal response)
IMEI
IMEI‘ (Fake response)!
Jump
(Soft-Patch)
Attack on GSM device Identity IMEI
Mobile serial number IMEI (International Mobile Equipment Identity)

## Slide 25: Physically Unique Units Production
inject
un-removable
and Provable
Identity
Fabricate equal objects
Unique objects
Common technique:

## Slide 26: Personalizing Physical Entities : One-Way Injection
One-Way
(One-time)
Injection
Unique object
One Way secret-key
injection
Unique
Provable
Identity
Module
- tamperproof
- un-removable
Basically clonable as somebody knows the injected key and can reveal it
Mechanical simulation
Neutral objects

## Slide 27
Requirements on Physical Uniqueness in Production
Personalization requirements:
Uniqueness - Unclonable, Clone-Resistant - Remotely and securely Identifiable - Low cost - Resilient security if cloned!
(brake-one brake-all impossible!)
Notes: 27

## Slide 28
State of the Art in Unclonable Physical Units
DNA-like
Physically Unclonable Functions
(PUF‘s)
Bio-Inspired Provable Physical Identity
Make use of born uniqueness properties (DNA like)

## Slide 29
Physical Unclonable Functions PUFs offer DNA like Identification Techniques
Analogue
Response
Discrete
Extractor
Discrete
Identification
Response
Ideal PUFs are: Born unpredictable and unclonable physical VLSI properties.
In other words: PUFs are analogue non-linear, hard to model or to copy, unpredictable huge mapping in a semiconductor VLSI device
Chemical
Extractor
Chemical Markers
Select
Markers
Identification by matching markers
Bio DNA: 248 combinations ≈3 · 1012
Biological DNA
Best physical Identity: As the born DNA-like provable identification
PUF
Unknown
DNA like
Mapping
VLSI
Discrete
stimulation
(select marker)
Notes: 29
29

## Slide 30
Since 2000 many proposals
optical PUF
coating PUF
Silicon PUF
optical fiber PUF
RF COA
LC-PUF
S-RAM PUF
Arbiter PUF
fluorescent PUF
State of the Art: Unclonable Devices by: Analog Physical Unclonable Functions (PUFs)
Delay PUF
Butterfly PUF
diode breakdown PUF
reconfigurable PUF
acoustic PUF
controlled PUF
phosphor PUF
...
Unclonable
DNA-Chain
Delay based
Optical
Coating PUF
(Capacity)
So far all have
“Reproducibility”
problems!
Analog functions!!!
Born properties: Similar to the biological DNA

## Slide 31
PUFs inconsistency and aging difficulties
K
Crypto
cryptographic
key
- Same input =>Different response
“noisy function”
PUF
challenge C
response R
Physical System
“complex interaction”
R
pdfR
* Source: Roel Maes, ESAT/COSIC, K.U.Leuven, BCRYPT Workshop:
Bad reproducibility due to : Operating conditions, quantization (Metastability) , Aging, …
Fuzzy Extractors: Complex, Costly (Sign. Proc + ECC)
Fuzzy
Extractor
*
PUF
x
y
fuzzy
secret
*

## Slide 32
Fuzzy Extractor for (PUFs)
Fuzzy Extractor: is used to correct errors in reproducing the PUF response by deploying error correcting codes /Helper Data Concept
C
R
PUF
Helper Data (HD)
Helper Data Extractor
Key
Enrolment process
C
R’
PUF
Helper Data (HD)
Fuzzy Extractor
Error Correction
Key
Reconstruction
One-Time-Process
Repeated Action
NOTICE: Helper Data: need not to be secured!

## Slide 33
Bio-Inspired Identification Protocol
DNA-Like Marker-Based Identification
DNA-Like Marker-Based Identification
List generated and kept secret by the proving authority
If max | C,R|  , Then unit is unclonable
Secret Pair’s List
C1 - R1
C2 - R2
…
Ci - Ri
…
Up to 
P1
Pi
P2
DNA-like Identity chain Carrier/function
Ci
Ri
C2 – R2
R‘2
Tow-way Protocol:
1- send C2 to the object
2- Object responds with R2 if authentic
- Cancel the pair C2 - R2 from the list and never use it again
If C and R each having n-Bits, Max table size: 2n 2n (example: for n=128 impossible to store) , that is the unit is unclonable!
Same ?

## Slide 34
Biological DNA Identification (Fatherhood Test):
Chemical
Extractor
Chemical Markers
Select
Markers
Identification by matching markers
Bio DNA: 248 combinations ≈3 · 1012
Biological DNA
Best physical Identity: the born DNA-like provable identification
≠
≠
≠
Extract at same marker position
Different entities for Non-equal marker extracts A’ ≠ B’ ≠ C’ ≠ D’
A
B
C
D
A’
B’
C’
D’
System is unclonable iff: # markers → ∞
Notes: 34
34

## Slide 35
Silicon PUF
Intrinsic PUF
Optical PUF
Coating PUF
Few promissing PUF´s
Selected Proposed
Physical Unclonable Functions PUFs
Unique
+
Unclonable
PUF
Identification module (Function)
Identification by checking challenge-response behavior
Like DNA
Response
Challenge
Device
Notes: 35

## Slide 36
MUX Chain or Arbiter PUFs
1.
Silicon PUF
…
Challenge
Rising Edge
step
D
Q
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
0
1
0
1
G
…
1 if top
path is
faster,
else 0
D
Q
1
1
0
0
1
0
0
1
1
0
0
1
0
1
0
1
G
Response
0
0
1
1
Principle: Compare delay time in a chain. Each physical chips exhibits own different delay time behaviour which identifies it
Source [8]
Notes: 36

## Slide 37
Compare frequencies of two oscillators.The faster oscillator is randomly determined by manufacturing variations
Ring Oscillator Design Procedure
Silicon PUF
N oscillators
MUX
counter
counter
>?
Output
Input
0 or 1
2467MHz
2453MHz
2519MHz
1
2
N

## Slide 38
Intrinsic PUF(I-PUF)
5.
S-RAM PUF
Power up
Source [8]
S-RAM initial state after power on
Is mostly the same. (re-production !!)
However different from chip to chip

## Slide 39
SRAM PUF : Intra-Chip Variation
Intrinsic PUF(I-PUF)
Principle: Read some memory area to identify physical units
S-RAM initial state after power on is mostly the same. (re-production !!)
However different from chip to chip
Source [8]
Notes: 39

## Slide 40
Microsemi SmartFusion®2 Techn. SRAM PUF
Real-Field SRAM PUF in the Market
50-100 K Gate
Manufacturer secrets!
Xilinx FPGA: SRAM PUF many IP-Cores … SRAM, Delay-based, …
Hard-Core PUF
16 kb RAM

## Slide 41
3.
Challenge
Response
Optical PUF
Laser beam
Scattered/reflected
beam
Principle: Difference in reflected and refracted ray of light on a surface
Source [8]
Notes: 41

## Slide 42
Practical set-up relatively complex
Optical PUF
Laser
Camera
PUF
Source [8]
Notes: 42

## Slide 43
Possible Integrated PUF
Optical PUF
Source [8]
Notes: 43

## Slide 44
Coating PUF
Sensor
Sensor
top metal
Bulk
Active layers + lower metal layers
passivation
1
2
Principle: Different capacity sensed at by different sensors
Source [8]
dielectric coating material
Capacity sensor grid
Capacity differences
Notes: 44

## Slide 45
Coating PUF
Source [8]
Notes: 45

## Slide 46
Possible attacks on PUFs
7.
- Manufacturer cheats!
Manufacturer has to be trustable!
Tamper-Proof technology is required!
Fake
PUF
Challenge
Response
Detectable !
Notes: 46

## Slide 47
All Analog PUFs are however,
7.
Still complex and costly to produce
Sensitive to temperature and supply voltage etc.
Have long-term reproducibility “Aging” issues ! (non-Consistent in the long term!)
Still relatively limited for real field use!
Notes: 47