## Slide 1: BLM1612 - Circuit Theory
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
Kirchhoff’s Current Law
Kirchhoff’s Voltage Law

## Slide 2: Objectives of the Lecture
Present Kirchhoff’s Current and Voltage Laws.
Demonstrate how these laws can be used to find currents and voltages in a circuit.
Explain how these laws can be used in conjunction with Ohm’s Law.

## Slide 3: Resistivity, r
Resistivity is a material property
  Dependent on the number of free or mobile charges (usually electrons) in the material.
    In a metal, this is the number of electrons from the outer shell that are ionized and become part of the ‘sea of electrons’
  Dependent on the mobility of the charges
    Mobility is related to the velocity of the charges.
    It is a function of the material, the frequency and magnitude of the voltage applied to make the charges move, and temperature.

## Slide 4: Resistivity of Common Materials at Room Temperature (300K)
Material | Resistivity (W-cm) | Usage
Silver | 1.64x10-8 | Conductor
Copper | 1.72x10-8 | Conductor
Aluminum | 2.8x10-8 | Conductor
Gold | 2.45x10-8 | Conductor
Carbon (Graphite) | 4x10-5 | Conductor
Germanium | 0.47 | Semiconductor
Silicon | 640 | Semiconductor
Paper | 1010 | Insulator
Mica | 5x1011 | Insulator
Glass | 1012 | Insulator
Teflon | 3x1012 | Insulator

## Slide 5: Resistance, R
Resistance takes into account the physical dimensions of the material
  where:
    L is the length along which the carriers are moving
    A is the cross sectional areathat the free charges move through.

## Slide 6: Ohm’s Law
Voltage drop across a resistor is proportional to the current flowing through the resistor
Units: V = AW
where A = C/s

## Slide 7: Short Circuit
If the resistor is a perfect conductor (or a short circuit)
  R = 0 W,
then
  v = iR = 0 V
  no matter how much current is flowing through the resistor

## Slide 8: Open Circuit
If the resistor is a perfect insulator, R = ∞ W
then
  no matter how much voltage is applied to (or dropped across) the resistor.

## Slide 9: Conductance, G
Conductance is the reciprocal of resistance
  G = R-1 = i/v
  Unit for conductance is S (siemens) or (mhos, )
G = As/L
where s is conductivity,
which is the inverse of resistivity, r

## Slide 10: Power Dissipated by a Resistor
p = iv = i(iR) = i2R
p = iv = (v/R)v = v2/R
p = iv = i(i/G) = i2/G
p = iv = (vG)v = v2G

## Slide 11: Power Dissipated by a Resistor
Since R and G are always real positive numbers
  Power dissipated by a resistor is always positive
The power consumed by the resistor is not linear with respect to either the current flowing through the resistor or the voltage dropped across the resistor
  This power is released as heat. Thus, resistors get hot as they absorb power (or dissipate power) from the circuit.

## Slide 12: Short and Open Circuits
There is no power dissipated in a short circuit.
There is no power dissipated in an open circuit.

## Slide 13: Circuit Terminology
Node
  point at which 2+ elements have a common connection
    e.g., node 1, node 2, node 3
Path
  a route through a network, through nodes that never repeat
    e.g., 1→3→2, 1→2→3
Loop
  a path that starts & ends on the same node
    e.g., 3→1→2→3
Branch
  a single path in a network; contains one element and the nodes at the 2 ends
    e.g., 1→2, 1→3, 3→2

## Slide 14: Exercise
For the circuit below:
  Count the number of circuit elements.
  If we move from B to C to D, have we formed a path and/or a loop?
  If we move from E to D to C to B to E, have we formed a path and/or a loop?

## Slide 15: Kirchhoff’s Current Law (KCL)
Gustav Robert Kirchhoff: German university professor, born while Ohm was experimenting
Based upon conservation of charge
  the algebraic sum of the charge within a system can not change.
  the algebraic sum of the currents entering any node is zero.
Where N is the total number of branches connected to a node.

## Slide 16: Kirchhoff’s Voltage Law (KVL)
Based upon conservation of energy
  the algebraic sum of voltages dropped across components around a loop is zero.
  The energy required to move a charge from point A to point B must have a value independent of the path chosen.
Where M is the total number of branches in the loop.

## Slide 17: Example-01
For the circuit, compute the current through R3 if it is known that the voltage source supplies a current of 3 A.
Use KCL

## Slide 18: Example-02
Referring to the single node below, compute:
  iB, given iA = 1 A, iD = –2 A, iC = 3 A, and iE = 4 A
  iE, given iA = –1 A, iB = –1 A, iC = –1 A, and iD = –1 A
Use KCL
iA + iB - iC - iD - iE = 0
iB = -iA + iC + iD + iE
iB = -1 + 3 - 2 + 4 = 4 A
iE = iA + iB - iC - iD
iE = -1 - 1 + 1 + 1 = 0 A

## Slide 19: Example-03
Determine I, the current flowing out of the voltage source.
  Use KCL
    1.9 mA + 0.5 mA + I are
    entering the node.
    3 mA is leaving the node.
    V1 is generating power.

## Slide 20: Example-04
Suppose the current through R2 was entering the node and the current through R3 was leaving the node.
  Use KCL
    3 mA + 0.5 mA + I are
    entering the node.
    1.9 mA is leaving the node.
    V1 is dissipating power.

## Slide 21: Example-05
If voltage drops are given instead of currents,
  you need to apply Ohm’s Law to determine the current flowing through each of the resistors before you can find the current flowing out of the voltage supply.
    I1 is leaving the node.
    I2 is entering the node.
    I3 is entering the node.
    I is entering the node.
I3
I1
I2

## Slide 22: Example-06
For each of the circuits in the figure below, determine the voltage vx and the current ix.
  Applying KVL clockwise around the loop and Ohm’s law

## Slide 23: Example-07
For the circuit below, determine
  vR2
  vx
  a.
  b.

## Slide 24: Example-08
For the circuit below, determine
  a. vR2 b. vx if vR1 = 1 V.
  a.
  b.

## Slide 25: Example-09
For the circuit below, determine vx

## Slide 26: Example-10…
Find the voltage across R1.
    Note that the polarity of the voltage has been assigned in the circuit schematic.
  First, define a loop that include R1.

## Slide 27: …Example-10…
If the red loop is considered
  By convention, voltage drops are added and voltage rises are subtracted in KVL.
–5 V – VR1+ 3 V = 0 VR1 = -2 V

## Slide 28: …Example-10
Suppose you chose the green loop instead.
    Since R2 is in parallel with I1, the voltage drop across R2 is also 3V.
    –5 V – VR1+ 3 V = 0 VR1 = -2 V

## Slide 29: Example-11…
Find the voltage across R2 and the current flowing through it.
  First, draw a loop that includes R2.

## Slide 30: …Example-11…
If the green loop is used:
    –11.5 V + 2.4 V + VR2= 0 VR2 = 9.1 V

## Slide 31: …Example-11…
If the blue loop is used:
  First, find the voltage drop across R3
    1 mA × 1.1 kW = 1×10-3 A × 1.1×103 W = 1.1 V
    1.1 V + 8 V - VR2= 0 VR2 = 9.1 V

## Slide 32: …Example-11
  Once the voltage across R2 is known, Ohm’s Law is applied to determine the current.
    IR2 = 9.1 V / 4.7 kW = 9.1 V / (4.7×103 W)
    IR2 = 1.94×10-3 A = 1.94 mA
IR2