## Slide 1: BLM1612 - Circuit Theory
Prof. Dr. Nizamettin AYDIN
naydin@yildiz.edu.tr
www.yildiz.edu.tr/~naydin
Mathematical Preliminaries
Nodal Analysis
Nodal Analysis with Supernodes
Mesh Analysis
Mesh Analysis with Supermeshes

## Slide 2: Objectives of Lecture
Provide step-by-step instructions for nodal analysis, which is a method to calculate node voltages and currents that flow through components in a circuit.
Provide step-by-step instructions for mesh analysis, which is a method to calculate voltage drops and mesh currents that flow around loops in a circuit.

## Slide 3: Mathematical Preliminaries
Consider the following equations, where x and y are the unknown variables and a1, a2, b1, b2, c1, and c2 are constants:
(1)
(2)
Solution by substitution
  Rearrange (1)
  Substitute x into (2) to obtain y
  Find x

## Slide 4: Mathematical Preliminaries
Solution by Determinant:
  Rearrange (1) and (2) into matrix form
  Determinants are:

## Slide 5: Mathematical Preliminaries
Using determinats, the following solutions for x and y can be found

## Slide 6: Mathematical Preliminaries
Consider the three following simultaneous equations:

## Slide 7: Nodal Analysis
Technique to find currents at a node using Ohm’s Law and the potential differences betweens nodes.
  First result from nodal analysis is the determination of node voltages (voltage at nodes referenced to ground).
    These voltages are not equal to the voltage dropped across the resistors.
  Second result is the calculation of the currents

## Slide 8: Steps in Nodal Analysis
Vin

## Slide 9: Steps in Nodal Analysis
Vin
Pick one node as a reference node
  Its voltage will be arbitrarily defined to be zero

## Slide 10: Step 1
Vin
Pick one node as a reference node
  Its voltage will be arbitrarily defined to be zero

## Slide 11: Step 2
Label the voltage at the other nodes
Vin

## Slide 12: Step 3
Label the currents flowing through each of the components in the circuit

## Slide 13: Step 4
Use Kirchoff’s Current Law

## Slide 14: Step 5
Use Ohm’s Law to relate the voltages at each node to the currents flowing in and out of them.
  Current flows from a higher potential to a lower potential in a resistor
    The difference in node voltage is the magnitude of electromotive force that is causing a current I to flow.

## Slide 15: Step 5
We do not write an equation for I7 as it is equal to I1

## Slide 16: Step 6
Solve for the node voltages
  In this problem we know that V1 = Vin

## Slide 17: Example 01…
Once the node voltages are known, calculate the currents.

## Slide 18: …Example 01…
From Previous Slides

## Slide 19: …Example 01…
Substituting in Numbers

## Slide 20: …Example 01…
Substituting the results from Ohm’s Law into the KCL equations

## Slide 21: …Example 01…
Node voltages must have a magnitude less than the sum of the voltage sources in the circuit
One or more of the node voltages may have a negative sign
  This depends on which node you chose as your reference node.
Node Voltages | (V)
V1 | 10
V2 | 5.55
V3 | 4.56
V4 | 3.74
V5 | 3.46

## Slide 22: …Example 01…
Voltage across resistors | (V)
VR1 = (V1 – V2) | 4.45
VR2 = (V2 – V3) | 0.990
VR3 = (V3 – V5) | 1.10
VR4 = (V3 – V4) | 0.824
VR5 = (V4 – V5) | 0.274
VR6 = (V5 – 0V) | 3.46
The magnitude of any voltage across a resistor must be less than the sum of all of the voltage sources in the circuit
  In this case, no voltage across a resistor can be greater than 10 V.

## Slide 23: …Example 01
None of the currents should be larger than the current that flows through the equivalent resistor in series with the 10V supply.
  Req = 7+[5||(1+3)]+2+9 = 20.2 kΩ
  Ieq = 10 / Req = 10 V/ 20.2 kΩ = 495 µA
Currents | (mA)
I1 | 495
I2 | 495
I3 | 220
I4 | 275
I5 | 275
I6 | 495
I7 | 495

## Slide 24: Summary
Steps in Nodal Analysis
  1. Pick one node as a reference node
  2. Label the voltage at the other nodes
  3. Label the currents flowing through each of the components in the circuit
  4. Use Kirchoff’s Current Law
  5. Use Ohm’s Law to relate the voltages at each node to the currents flowing in and out of them.
  6. Solve for the node voltage
  7. Once the node voltages are known, calculate the currents.

## Slide 25: Example 02…
Determine the current flowing left to right through the 15 ohms resistor.

## Slide 26: …Example 02…
Two equations with two unknown variables (v1, v2)
(1)
(2)
Solution by substitution
  Rearrange (2)
  Substitute v1 into (1) to obtain v2
V
  Find v1

## Slide 27: …Example 02
Two equations with two unknown variables (v1, v2)
(1)
(2)
Solution by determinant

## Slide 28: Nodal Analysis with Supernodes
Floating voltage source
  a voltage source that does not have either of its terminals connected to the ground node.
  A floating source is a problem for the Nodal Analysis
    In this circuit, battery V2 is floating
  Applying Nodal Analysis
Using Supernode
  The voltage at node c
  battery current
  the KCL equation at node b
  to find currents, Ohm's Law can be used

## Slide 29: Nodal Analysis with Supernodes

## Slide 30: Example 03…
Determine the node-to-reference voltages in the circuit provided.
  identify the nodes & supernodes
  write KCL at each node (except the reference)

## Slide 31: …Example 03
When we relate the source voltages to the node voltages
When we express the dependent current source in terms of the assigned variables

## Slide 32: Mesh Analysis
Technique to find voltage drops within a loop using the currents that flow within the circuit and Ohm’s Law
  First result is the calculation of the current through each component
  Second result is a calculation of either the voltages across the components or the voltage at the nodes.
Mesh
  the smallest loop around a subset of components in a circuit
    Multiple meshes are defined so that every component in the circuit belongs to one or more meshes

## Slide 33: Mesh Analysis
Vin
Identify all of the meshes in the circuit
Label the currents flowing in each mesh
Label the voltage across each component in the circuit
Use Kirchoff’s Voltage Law
  -Vin + V1 + V2+ V3 + V6 = 0
  -V3 + V4+ V5 = 0
i1
i2
-
V1
+
+
V3
_
+
V5
_
+
V6
_
+ V2 -
+ V4 -

## Slide 34: Mesh Analysis
Use Ohm’s Law to relate the voltage drops across each component to the sum of the currents flowing through them.
  Follow the sign convention on the resistor’s voltage.
Vin
i1
i2
-
V1
+
+
V3
_
+
V5
_
+
V6
_
+ V2 -
+ V4 -

## Slide 35: Mesh Analysis
Voltage drops on the resistors:
Vin
i1
i2
-
V1
+
+
V3
_
+
V5
_
+
V6
_
+ V2 -
+ V4 -

## Slide 36: Mesh Analysis
Solve for the mesh currents, i1 and i2
  These currents are related to the currents found during the nodal analysis.
    i1 = I7 = I1 = I2 = I6
    i2 = I4 = I5
    I3 = i1 - i2
                Once the voltage across all of the components are known, calculate the mesh currents.
Vin
i1
i2
-
V1
+
+
V3
_
+
V5
_
+
V6
_
+ V2 -
+ V4 -

## Slide 37
Example 04…
12V
-
V1
+

## Slide 38: …Example 04…
From Previous Slides
  -Vin + V1 + V2 + V3 + V6 = 0
  -V3 + V4 + V5 = 0

## Slide 39: …Example 03…
Substituting the results from Ohm’s Law into the KVL equations
  -12 + V1 + V2 + V3 + V6 = 0
  -V3 + V4 + V5 = 0
will result in:
Mesh Currents | (mA)
i1 | 740
i2 | 264

## Slide 40: …Example 04…
Voltage across resistors | (V)
VR1 = i1R2 | 2.96
VR2 = i2 R2 | 5.92
VR3 =(i1 – i2) R3 | 2.39
VR4 = i2 R4 | 1.59
VR5 = (V4 – V5) | 0.804
VR6 = (V5 – 0V) | 0.740
The magnitude of any voltage across a resistor must be less than the sum of all of the voltage sources in the circuit
  In this case, no voltage across a resistor can be greater than 12V.
  Vin = V1+V2+V3+V6
  12 = 2.96+5.92+2.39+0.74
  12 V= 12.01 V
  0.01 V difference is caused by rounding error

## Slide 41: …Example 04
None of the mesh currents should be larger than the current that flows through the equivalent resistor in series with the 12V supply.
  Req = 1+[5||(3+6)]+8+4 = 16.2 kΩ
  Ieq = 12 / Req = 12 V/ 16.2 kΩ = 740 µA
Currents | (mA)
IR1 = i1 | 740
IR2 = i1 | 740
IR3 = i1- i2 | 476
IR4 = i2 | 264
IR5 = i2 | 264
IR6 = i1 | 740
I Vin = i1 | 740

## Slide 42: Summary
Steps in Mesh Analysis
  1. Identify all of the meshes in the circuit
  2. Label the currents flowing in each mesh
  3. Label the voltage across each component in the circuit
  4. Use Kirchoff’s Voltage Law
  5. Use Ohm’s Law to relate the voltage drops across each component to the sum of the currents flowing through them.
  6. Solve for the mesh currents
  7. Once the voltage across all of the components are known, calculate the mesh currents.

## Slide 43: Example 05
Determine the loop currents i1 and i2

## Slide 44: Example 06
Determine the power supplied by the 2 V source
Mesh 1
Mesh 2
Power absorbed by the 2 V source
  Actually 2.474 W is supplied

## Slide 45: Mesh Analysis with Supermeshes
Consider the following circuit.
  Both mesh I and mesh II go through the current source.
    It is possible to write and solve mesh equations for this configuration.
Using supermesh
  You can drop one of the meshes and replace it with the loop that goes around both meshes, as shown here for loop III.
  You then solve the system of equations exactly the same as the Mesh Analysis

## Slide 46: Mesh Analysis with Supermeshes

## Slide 47: Example 07
Determine the current i as labeled in the circuit.
Supermesh
Mesh 2
Independent source current is related to the mesh currents
+
-
+
-
+
-
+
-
+ -

## Slide 48: Nodal vs. Mesh Analysis: A Comparison
The following is a planar circuit with 5 nodes and 4 meshes.
  Planar circuits are circuits that can be drawn on a plane surface with no wires crossing each other.
Determine the current ix

## Slide 49: Planar vs Non-planar circuits
Planar
Non-planar

## Slide 50: Nodal vs. Mesh Analysis: A Comparison
Using Nodal Analysis
  Although we can write four distinct equations, there is no need to label the node between the 100 V source and the 8 ohm resistor, since that node voltage is clearly 100 V.
We write the following three equations:
Solving, we find that

## Slide 51: Nodal vs. Mesh Analysis: A Comparison
Using Mesh Analysis
  We see that we have four distinct meshes
  However it is obvious that i4= −8 A
  We therefore need to write three distinct equations.
Writing a KVL equation for meshes 1, 2, and 3:
Solving, we find that